3GPP TSG-SA WG6 Meeting #42-e	S6-210689 rev B1

e-meeting, 1st – 9th March 2021	(revision of S6-210570 rev1)

Source:	Convida Wireless LLC

Title:	EEC Context

Spec:	3GPP TS 23.558 v1.3.0

Agenda item:	7.6

Document for:	Approval

Contact:	Catalina Mladin, mladin.catalina@convidawireless.com

- Introduction

This contribution describes:

-	The EEC Registration Context IE. The concept has been presented previously to SA6 as “Registration Context” within the EEC context during post SA6#41 conf call discussions and proposals

-	The relocation procedures defined for the EEC Registration Context IE. The use of these procedures is further described via a related “Context relocation in ACR” SA6#42 contribution.

The most substantive changes in this proposal, compared to the earlier ones are:

- Decoupling of the Service Session Context IE from the EEC Registration Context IE.

- Removal of the manager/attendant role in context maintenance, and the corresponding functionality. To answer concerns about clarifying which entity updates the context, it is proposed to rely upon exiting mechanisms as follows:

  - TS 23.502 clause 4.26 provides information about context transfer procedures between CN NFs. In it, it is clarified that a direct and an indirect mode of transferred are assumed, as specified in TS 29.501.

  - TS 29.501 clause 4.9 provides information about the direct and indirect modes. In indirect mode only links (rather than the entire resource/IE content) are provided in the transfer, with the assumption that a GET would enable the receiver to perform a read. Moreover TS 29.501 clause 4.6.1.4 provides specifics about how to support seamless change of NF producers (which is the analogous process to seamless change of EESs, when it comes to the context).

  - Therefore, it is proposed that SA6 follows the SA2 path in describing context transfer by specifying the Pull and Push procedures (like those in TS 23.502 clause 4.26), and acknowledging that the existing  29.501 mechanisms can be used to determine how updates to a context can be handled after a transfer.

2. Reason for Change

To provide clarity on EEC Context and enable EEC Context relocation .

3. Proposal

It is proposed to agree the following changes to 3GPP TS 23.558 v1.3.0.

* * * First Change * * * *

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 23.501: "System Architecture for the 5G System; Stage 2".

[3]	3GPP TS 23.502: "Procedure for the 5G System; Stage 2".

[4]	3GPP TS 29.522: "5G System; Network Exposure Function Northbound APIs; Stage 3".

[5]	3GPP TS 29.122: "T8 reference point for northbound Application Programming Interfaces (APIs)".

[6]	3GPP TS 23.222: "Functional architecture and information flows to support Common API Framework for 3GPP Northbound APIs; Stage 2".

[7]	3GPP TS 23.271: "Functional stage 2 description of Location Services (LCS)".

[8]	3GPP TS 36.305: "Evolved Universal Terrestrial Radio Access Network (E-UTRAN); Stage 2 functional specification of User Equipment (UE) positioning in E-UTRAN".

[9]	3GPP TS 23.273: "5G System (5GS) Location Services (LCS); Stage 2".

[10]	3GPP TS 38.305: "NG Radio Access Network (NG-RAN); Stage 2 functional specification of User Equipment (UE) positioning in NG-RAN".

[11]	3GPP TS 23.401: "General Packet Radio Service (GPRS) enhancements for Evolved Universal Terrestrial Radio Access Network (E-UTRAN) access".

[12]	3GPP TS 23.503: "Policy and charging control framework for the 5G System (5GS); Stage 2".

[13]	3GPP TS 23.434: "Service enabler architecture layer for verticals; Functional architecture and information flows; Stage 2".

[14]	3GPP TS 23.286: "Application layer support for Vehicle-to-Everything (V2X) services; Functional architecture and information flows ".

[15]	ETSI ISG MEC ETSI GS MEC 003 V2.1.1 (2019-01), "Multi-access Edge Computing (MEC); Framework and Reference Architecture"

[16]	OMA-TS-REST_NetAPI_ACR: "RESTful Network API for Anonymous Customer Reference Management"

[17]	3GPP TS 23.682: "Architecture enhancements to facilitate communications with packet data networks and applications".

[18]	3GPP TS 23.288: "Architecture enhancements for 5G System (5GS) to support network data analytics services".

[rr]	3GPP TS 29.501: "5G System; Principles and Guidelines for Services Definition; Stage 3".

* * * Next Change * * * *

### 7.2.M	EEC Context ID

The EEC Context ID is a globally unique value which identifies a set of parameters (i.e. EEC Context) associated with the EEC registration and maintained in the Edge Enabler Layer.

If the EEC registration request does not include a previously assigned EEC Context ID value, the receiver EES assigns a new EEC Context ID and creates an EEC Context IE as described in 8.2.A.1.

Providing a previously assigned EEC Context ID at registration allows maintaining context of the EEC in the Edge Enabler Layer beyond the lifetime of a registration, subject to policies.

NOTE: How the EEC Context ID is assigned is out of scope of this specification.

* * * Next Change * * * *

### 8.2.A	EEC Context

The EEC Context includes information about an EEC for receiving edge enabler services.

Table 8.2.A-1: EEC Context

| Information element | Status | Description |
| --- | --- | --- |
| EEC ID | M | Unique identifier of the EEC. |
| EEC Context ID | M | Identifier assigned to the EEC Context |
| Source EES ID | M | Identifier of the EES that provided EEC context ID. |
| UE ID | O | Identifier of the UE hosting the EEC |
| Co-located EEC ID list | O | List of EEC IDs of the EECs determined to be hosted by the same UE. |
| List of subscriptions | O | List of EES subscriptions related to the given EEC or Edge UE ID. |
| UE location | O | Latest UE location of the UE hosting the EEC which was available at the EES. |
| List of Service Session Contexts | O | List of Service Session Context IEs associated. Each Service Session Context includes information maintained by the EES for the services received by an AC from an EAS registered to the EES. |
| > Service Session Context | M | Service Session Context as described in Table 8.2.A-2 |

Table 8.2.A-2: Service Session Context

| Information element | Status | Description |
| --- | --- | --- |
| EEC ID | M | Unique identifier of the EEC. |
| EAS ID | M | Identifier of the EAS providing the application services |
| EAS Endpoint | M | Endpoint information of the EAS. |
| EEC context ID | O | Identifier of the EEC Context received at registration, if available. |
| Edge UE ID | O | UE ID used on Edge-3 interactions with the corresponding EAS |
| AC Profile | O | Information about the corresponding AC. as described in Table 8.2.2-1. |
| List of subscriptions | O | List of session-related subscriptions (i.e. EAS subscriptions related to the EEC or Edge UE ID) managed by the EES |
| >CN subscription resource URI | O | URI of the subscription resource at the SCEF/NEF, or the corresponding subscriptionId. This information may be provided for UE location events, User plane path management events, Session with QoS events. |

Editor’s Note: Additional IE(s) for the subscriptions to CN the list of IEs is FFS, pending SA2 discussions (see TR 23.748 clause 9.2.6).

* * * Next Change * * * *

## 8.x EEC Context relocation

### 8.x.1 General

EEC Context contains information related to an EEC which is used by EESs to provide the Edge Enabler Layer services. EEC Context relocation procedures allow the EEC Context information to be shared between EESs (via EDGE-9 interactions) as an  EEC moves.

An EEC Context IE shall be created for each registered EEC, after a successful registration, by the receiver EES, as follows:

  - The EEC ID and UE ID shall be set based on the corresponding registration request parameters.

  - If the EEC registration request contains an EEC context ID, the EEC context ID and source EES ID are set based on the corresponding registration request parameters;

Otherwise, the receiver EES shall assign an EEC context ID and set the source EES ID to its EES ID.

  - Elements of the list of  Service Session Context IEs shall be set created by the EES when it determines that a registered EAS is providing services to an AC on the served EEC.

Editor’s Note: How the EES determines that a registered EAS is providing services to an AC is FFS.

NOTE: EESs in bypass mode do not provide services based on EEC context, therefore EEC Context IE management does not apply in bypass mode.

An EEC Context IE shall be determined to be stale after successful EEC de-registration procedure.

NOTE 1: Stale EEC Context IEs are subject to information persistence policies and privacy policies. Mechanisms for re-use of stale EEC Context IEs are not in scope of the current version of specification.

A Service Session Context IE shall be determined to be stale as follows:

- After a successful Service Session Context Relocation procedure targeting the IE, or

- When the EES determines that a registered EAS is no longer providing services to an AC on the served EEC.NOTE 1: Stale Service Session Context IEs are subject to information persistence policies and privacy policies. Mechanisms for re-use of stale Service Session Context IEs are not in scope of the current version of specification.

- NOTE 2: In this version of specification, mechanisms used by EES to determine that a registered EAS is no longer providing services to an AC on a served EEC are implementation-dependent.

An EEC Context IEs shall be updated as follows:

- When EEC Registration update requests targeting the corresponding EEC Context ID are received, all optional parameters may be updated.

- When EEC Context IEs are created, either after a registration request or based on EEC Context relocation procedure, the EES shall check whether the UE ID corresponds to an existing EEC Context and update the co-located EEC ID list of the two EEC Context IEs accordingly.

- When subscriptions targeting the corresponding UE ID are processed, the list of subscriptions shall be updated accordingly

A Service Session Context IE may be updated as follows:

- When EAS subscriptions targeting the corresponding UE ID are processed, the list of subscriptions shall be updated accordingly

### 8.x.2 Procedures

#### 8.x.2.1	General

The following procedures are supported for EEC Context relocation:

- EEC Context Push; and

- EEC Context Pull.

#### 8.x.2.2	EEC Context Pull relocation

An EEC Context is relocated via an EEC Context Pull request initiated by the target EES.

Figure 8.x.2.2 -1 illustrates the EEC Context Pull.

Pre-conditions:

- The source EES has provided the EEC with an EEC Context ID

- The target EES has received the EEC Context ID, source EES ID.

Figure 8.x.2.3-1: EEC Context Pull procedure

- The target EES requests an EEC Context from the source EES. The request includes EEC Context ID.

- Upon receiving the request from the target EES, the source EES validates the request and verifies the security credentials of the requester. The source EES uses the EEC Context ID provided to identify and authorize the EEC Context IE to be relocated. If the EEC Context relocation is authorized, other procedures may be initiated to ensure that all necessary Edge Enabler Layer entities are being updated and set up with necessary information about the new EEC Context location.

Editor’s Note: The additional procedures to be executed are FFS.

- The source EES sends a successful EEC Context response. The target EES stores the received EEC Context IE. When all procedures have been executed successfully the Target EES serves as registration EES.

If the EEC Context is not identified or maintained at the source EES, e.g. for source EES in bypass mode, an unsuccessful EEC Context Pull response is provided with an appropriate cause.

#### 8.x.2.3	EEC Context Push relocation

An EEC Context is relocated via an EEC Context Push request initiated by the source EES.

Pre-conditions:

- The source EES has provided the EEC with an EEC Context ID.

- A target EES has received the EEC Context ID, source EES ID.

Figure 8.x.2.2-2: EEC Context relocation procedure initiated by source EES.

- The source EES determines to forward EEC Context for relocation to a target EES. The source EES determines the target and the EEC Context IE to be forwarded.

- The source EES sends EEC Context Push request to the target EES including the EEC Context IE determined.

- Upon receiving the request from the source EES, the target EES validates the request and verifies the security credentials. The target EES uses the EEC Context ID provided to authorize the EEC Context to be stored and managed. Then the target EES sends an EEC Context response indicating success.

If the target EES operates in bypass mode an unsuccessful EEC Context Push response is provided with an appropriate cause.

### 8.x.3	Information flows

#### 8.x.3.1	General

The following information flows are specified for EEC Context relocation:

- EEC Context Pull request and response.

- EEC Context Push request and response.

#### 8.x.3.2	EEC Context Pull request

Table 8.x.3.2-1 describes information elements in the EEC Context Pull request between two EES.

Table 8.x.3.2-1: EEC Context Pull request

| Information element | Status | Description |
| --- | --- | --- |
| EES ID | M | Unique identifier of the requesting EES. |
| Security credentials | M | Security credentials resulting from a successful authorization for the edge computing service. |
| EEC Context ID | M | Unique identifier of the EEC Context used to authorize the transfer. |
| List of Service Session Contexts requested | O | List of Service Session Context IEs requested to be pulled |
| > EAS ID | M | Identifier of the EAS providing the application services |
| > EEC ID | O | Unique identifier of the EEC. |

#### 8.x.3.3	EEC Context Pull response

Table 8.x.3.3-1 describes information elements in the EEC Context Pull response between two EESs.

Table 8.x.3.3-1: EEC Context Pull response.

| Information element | Status | Description |
| --- | --- | --- |
| Successful response | O | Indicates that the request was successful. |
| >EEC Context IE | O | EEC Context IE, mandatory if the request was successful |
| Failure response | O | Indicates that the request failed. |
| > Cause | O | Indicates the cause of request failure, mandatory if the request failed. |

#### 8.x.3.4	EEC Context Push request

Table 8.x.3.4-1 describes information elements in the EEC Context Push request between two EESs.

Table 8.x.3.4-1: EEC Context Push request.

| Information element | Status | Description |
| --- | --- | --- |
| EES ID | M | Unique identifier of the requesting EES. |
| Security credentials | M | Security credentials resulting from a successful authorization for the edge computing service. |
| EEC Context IE | M | EEC Context IE |
| List of Service Session Contexts requested | O | List of Service Session Context IEs requested to be pushed |
| > EAS ID | M | Identifier of the EAS providing the application services |
| > EEC ID | O | Unique identifier of the EEC. |

#### 8.x.3.5	EEC Context Push response

Table 8.x.3.5-1 describes information elements in the EEC Context Push request between two EES.

Table 8.x.3.5-1: EEC Context Push response

| Information element | Status | Description |
| --- | --- | --- |
| Successful response | O | Indicates that the request was successful. |
| Failure response | O | Indicates that the request failed. |
| > Cause | O | Indicates the cause of request failure, mandatory if the request failed. |

* * * Next Change * * * *

#### 8.4.2.2	Procedures

##### 8.4.2.2.1	General

Following are supported for EEC registration:

-	EEC registration procedure;

-	EEC registration update procedure;

-	EEC de-registration procedure;

-	EEC Context relocation procedure.

Editor’s Note: The use of the registration procedure to jointly register multiple EECs on the same UEs is FFS.

##### 8.4.2.2.2	EEC registration

Figure 8.4.2.2.2-1 illustrates EEC registration procedure.

Pre-conditions:

1.	The EEC is authorized to access the EES for the purpose of performing registration and has received relevant security credentials as specified in clause 8.10; and

2.	The EEC has received service provisioning information from the ECS, including information for accessing the EES.

Figure 8.4.2.2.2-1: EEC registration procedure

1.	The EEC sends EEC registration request to the EES. The request from the client includes the security credentials received after successful authorization for edge computing services and may include a proposed expiration time. The request also optionally includes information indicating to the EES how the EEC expects to use the services of the EES.

If the EEC is moving to this EES from the purview of another EES, called source EES, the request from the EEC may include the identity and endpoint of the source EES and an EEC context ID that was provided by the source EES to maintain continuity of the EEC context and to authorize EEC context relocation.

2.	Upon receiving the request from the EEC, the EES validates the registration request and verifies the security credentials. The EES further determines whether the requirements that were indicated in the AC Profile(s) can be fulfilled and reserves corresponding resources.

3.	Upon successful validation of the request, if the received EEC registration request contains an EEC context ID, a source EES ID and EES endpoint, the EES performs  EEC Context Pull relocation (clause 8.x.2.2) from the source EES. Otherwise, the receiver EES assigns an EEC Context ID and creates an EEC Context IE as described in 8.2.A.1..

NOTE: Only a single EEC Context ID may be provided in the EEC registration request.

Editor’s Note: The use of the registration procedure to relocate multiple EEC contexts is FFS.If the EEC registration request fails, e.g. the EES cannot reserve the necessary resources while meeting the capability requirements of the existing registered EECs, the EES shall determine the EEC Context stale and send a failure response with a corresponding cause.

4.	The EES sends a successful registration response, which includes the registration ID and may include a newly assigned EEC context ID. The EEC stores the new EEC context ID and uses it if and when it registers with another EES. The EES may also provide an expiration time to indicate to the EEC when the registration will automatically expire. To maintain the registration, the EEC shall send a registration update request prior to the expiration. If a registration update request is not received prior to the expiration time, the EES shall treat the EEC as implicitly de-registered.

* * * Next Change * * * *

##### 8.4.2.3.3	EEC registration response

Table 8.4.2.3.3-1 describes information elements in the EEC registration response from the EES to the EEC.

Table 8.4.2.3.3-1: EEC registration response

| Information element | Status | Description |
| --- | --- | --- |
| Successful response | O | Indicates that the registration request was successful. |
| > Registration ID | M | Identifier of the EEC registration. |
| > Expiration time | M | Indicates the expiration time of the registration. To maintain an active registration status, a registration update is required before the expiration time. |
| > EEC context ID | O | Identifier of the EEC Context information available at the EES that performed the registration. |
| > Context Relocation Result | M | Indicates whether a successful context relocation has been performed |
| Failure response | O | Indicates that the registration request failed. |
| > Cause | M | Provides the cause for registration request failure. |