## Slide 1: New SID on Data Integrity Service in IOT
China Unicom
linl12@chinaunicom.cn

## Slide 2: WHY
The requirement of data integrity in verticals
  Data collected from IoT devices/sensors is mostly sent to service platform directly at the present, e.g. position data in logistics services.
  However IoT data for finance related services may be very crucial. Hence verticals such as supply chain finance and insurance have strict requirements for data integrity, e.g. environment data(e.g. temperature and windspeed) for agricultural insurance and warehouse data (e.g. number and weight of goods) for inventory financing. Those services require to data exchange from UE to the third party SP（service provider).
  Gap between 3GPP and requirement of verticals
  While data integrity methods are provided within the 3GPP network, there are gaps in ensuring end-to-end data integrity service from a UE to 3rd party Service Providers using the 3GPP Network.
  Moreover, data integrity protection is important for data verification services(e.g. an insurance claim)
  In any case, all kinds of IoT UEs and SPs of the enterprises above are connected to MNO’s networks, especially the more extensive cross industry SP business model.
  Need to get ready to provide a mechanism to realize data integrity service for the community in the interest alliance.
3GPP System
3GPP UE
Data integrity and Encryption in 3GPP
Data integrity from UE to SPs
UPF
3rd party SPs
Cross industry
WID Study Area

## Slide 3: RELATED
  TS 22.261 descrbe Data Integrity Service Requirements in 5GS to assure the integrity of the data exchanged between the 5G network and a third-party service provider:
Subject to regulatory requirements and based on operator policy, the 5G system shall provide a mechanism to support data integrity verification service to assure the integrity of the data exchanged between the 5G network and a third-party service provider.
NOTE: This requirement could apply to mechanisms supported over the interface between 5G core network and an external application, with no impact on RAN and UE.

## Slide 4
Cold Chain Logistics
During the transportation of vaccines/drugs, vaccines/drugs containers in cold chain logistics may be equipped with IoT sensors which send data to the vehicles. Those vehicles connect to a SP platform by 3GPP network for data gathering and processing. Monitoring is very critical since the products in the container may exceptionally sensitive to changes in pH, temperature and even light conditions.
Ensuring the trustiness of the collected environment data in each container/sensor is necessary to the service in order to guarantee vaccine/drug activity.
In this use case, the requirements are to achieve the data integrity for the environment data from IoT sensors to the SP.
Moreover, If problems arose, SP (hospital or vaccine company) would claim to trace and verify all the environment data during transportation afterwards.
EXAMPLE

## Slide 5: Service Flow Example-1/3
IoT UE
IoT UE
Data+data signature
Data+data signature
3GPP System
UE access network
Data Generation
Example of Logistics
IoT UE=Vehicles belonging to logistics companies that deliver vaccines and medicines.
Data+data signature=Application data(temperature in the container) and related digital signature (IoT UE source) . NOTE: Application data and data signature is only transmitted .3GPP would not store or process any of this part of data. Application collected data(temperature in the container)+hash algorithm+UE private key->Data signature
Data Integrity Service Enabler=Application Layer enabler to reliaze data integrity service
UE : Application data(temperature in the container)
+Data signature
Data Integrity Service Enabler
Integrity Verification
SP
Hospital
Logistics

## Slide 6: Service Flow Example-2/3
IoT UE
IoT UE
Data+data signature
Data+data signature
UE access network
Data Generation
Verify the Data Integrity
Logisics company requires to verify the data in ” Data+data signature” has not be tampered.
  Data+data signature” is transmitted via 3GPP system.
  IoT UE belong to 3GPP. If ” Data+data signature” have no changes, the vaccine is correctly transported.
3GPP System
Data Integrity Service Enabler
Integrity Verification
SP
Hospital
Logistics
Verify Data integrity
request

## Slide 7: Service Flow Example-3/3
IoT UE
IoT UE
Data+data signature
3GPP System
UE access network
Data Generation
3GPP can provide data integrity verification service based on the application layer solutions
3GPP network/IOT UE：have verification Key（e.g.UE’s public Key），and the “banding information” of the UE identifier and other necessary metadata for integrity verification
Obtain Verification Key: The Data Integrity Service Enabler could
  obtain verification Key（e.g.UE’s public Key） from IOT UE.
  verify the “Data+data signature” by using verification key.
UE’s public Key
banding information
Data Integrity Service Enabler
Integrity Verification
SP
Hospital
Logistics
Obtain verification Key
UE’s public Key

## Slide 8: Requirement Gap Analysis
AKMA（SA3）
  TS 33.535 specifies the security features and mechanisms to support authentication and key management aspects for applications based on subscription credential(s) in 5G system.
  GAP1: AKMA is an authentication mechanism in 5G network layer.
  GAP2: Identify new Network Element AAnF and protocols .
Study on Data Integrity Service in IOT
  This SID is designed to provide Data Integrity Service in IOT from UE to a third party SP in application layer.
  Have no effcts on Nework layer and UE.
GBA（SA3）
  TS 33.220 describes the security features and mechanisms to bootstrap authentication and key agreement for application security.
  GAP1:GBA provide an authentication mechanism in 4G network layer
  GAP2:Identify new Network Element BSF and protocols.

## Slide 9: What SA6 can do?
Data Integrity Service in IOT
1)Analyze existing requirements of data integrity service based on TS 22.261 Subclause 8.9.
2)Evaluate application architectural requirements and application layer architectures for data integrity service.
3)Analyze the re-use of functionalities from SA6 specifications for the solutions, where applicable.
4)Identify key issues and develop solutions based on 1) -3) .
Data Integrity Service Enabler
CN
RAN
3rd SP1
3rd SP2
Interface-1
Data/Data Signature Transfer
UICC
Note1： Red Line marked is inside SA6 Scope
  Note2：Application solutions have no effcts on Nework layer and UE.
Interface-2
Communication Module
IOT Device
Data Integrity Service Client
Access Control Module
Commnucation Module
Data Management Module
......

## Slide 10: Thank you