## Slide 1: SA2 solution – RAN Scalability Issue in Rel-17 MBS Multicast
Joakim Åkesson
Ericsson
S6-212281

## Slide 2: Summary of Multicast scalability concern
5MBS Multicast (and Broadcast) solution shall meet capacity and performance requirements in TS 22.261 incl TS 22.179
5MBS not only addresses MCPTT but several other use cases – a flexible solution has been specified
  MC/BC, no semi static allocation (compare eMBMS), UE specific delivery and feedback modes (PTP/PTM; indiv/shared)
Capacity (number of UEs supported in one cell) and performance (call setup time for large groups) limitations have been identified in current architecture/solutions/procedures
Different needs for Public Safety group communication and other use cases. The solution with associated PDU sessions was designed targeting heterogenous NG-RAN deployments, less optimized for group communication with high concentration of users in same area
Concern: 5G multicast MBS solution (Rel-17 TS 23.247 approved but not yet frozen) will not meet the KPI requirements from Public Safety, not even in coming releases. Parallel paging and parallel PDU session UP activation (DRB establishment) for 100s (or 1000s) of UEs (in RRC Idle/Inactive) does not scale
Proposal: remove the mandate for an associated PDU session UP for UE join and MBS session activation in Rel-17. Plan for NG-RAN enhancements (incl group paging/configuration and RRC Inactive/Idle support) in Rel-18

## Slide 3: Mission Critical services – need for Multicast Resource efficiencyCapacity, CoverageQoS, Mobility
Even distribution
Cell edge incident
“unlimited” capacity
  Excl mobility, sign and UL
  Excl coding/coverage (single cell / intra DU)
(dynamic) tradeoff – Coverage & QoS vs Capacity
RAN state optimizations
RRC Connected UE
RRC Inactive/Idle UE (Rel-18 candidate)
Poor radio (Idle) UE
(4G) MBSFN
Coverage: on par with unicast Capacity target: on par or beyond actual BC
Data stream, robust MCS, repetitions
Data stream, MC re-tx etc.
Single cell BC is suitable for non-real time, non-Mission Critical use cases – AL-FEC + unicast repair
Broadcast
Multicast

## Slide 4: Group activation efficiency issue
AMF is not aware of joined UEs
MB-SMF notifies SMF for MBS Session Activation
SMF builds candidate UE list for paging and sends to AMF
AMF processes the UE list for information preparation (e.g. paging area, with some issues when also paging optimization should be applied) and sends paging request to NG-RANs
If the UE list is long, the processing UE list takes time. It brings difficulties to meet call setup time requirement for large groups (performance).
AMF
SMF
Group activation (MBS session ID, UE list)
MB-SMF
MBS session activation (MBS session ID)
Paging
Paging
Process UE list

## Slide 5: Enhancement for group activation efficiency issue
AMF constantly prepares paging information towards RAN in advance along knowledge of joined UEs (and respective paging strategies)
At MBS session activation request received from MB-SMF, AMF sends paging request to NG-RANs immediately.
Note, that the same approach is expected to be applied for (RAN) paging of INACTIVE UEs
AMF
MB-SMF
MBS session activation (MBS session ID)
Paging
Paging
AMF holds UEs’ join status

## Slide 6: RAN scalability issue
SMF request NG-RAN to setup shared MBS resources by means of (UE individual) PDU session resource setup/modify protocol means
consequently, NG-RAN will setup PDU session resources for the UE and then associate them with the MBS session
  take time (especially at Session Activation  performance)
  occupy resources (capacity)
  RAN admission control may reject due to lack of PDU session resources for each participating UE (consequence: UE cannot receive MBS data) (capacity/scalability)
AMF
SMF
Service Request
( join / back from IDLE )
N1N2MessageTransfer (PDU session resource setup)
N2Message (PDU session resource setup)

## Slide 7: Enhancement for RAN scalability issue
Rel-17:
AMF holds UEs’ join status
Hierarchical Session Activation directly towards AMF/NG-RAN
For RRC_CONNECTED UEs: Shared MBS Resources immediately setup
  No mandate to setup associated PDU Sessions for UEs being able to receive multicast traffic
RRC_IDLE UEs to be paged (shared resources may be setup due to other joined UEs presence)
  After service request, no mandate to immediately setup associated PDU Sessions for multicast traffic reception.
RRC_INACTIVE UEs to be RAN paged
Rel-18:
Group paging/configuration & Multicast reception in RRC_INACTIVE/IDLE further addresses timing and capacity issues
  Including capacity & timing issues related RACH congestion
AMF
MB-SMF
NG-RAN
MBS session activation
AMF holds UEs’ join status
for CM-CONNECTED UEs: MBS session activation
for CM-IDLE UEs: (Group) Paging)

## Slide 8: Proposals for way forward
Benefits:
  Performance: shorten call setup time for large groups
  Capacity: Efficient resource usage
  Scalability & Performance: PDU session resources not needed at UE join and MBS session activation (call setup)
To mitigate the group activation efficiency issue & RAN scalability issue:
  AMF needs to be aware of UE join status
  AMF can prepare paging information in advance
  MB-SMF inform AMF for MBS session activation directly
  AMF add UEs into NG-RAN without PDU session resources required
Remind SA2 to secure the Rel-17 specifications (incl RAN dependencies) meet or allow enhancements to meet defined Mission Critical requirements

## Slide 9: Backup material

## Slide 10: Reference point architecture
Transport-only mode:
    CP: AF -> (NEF) -> MB-SMF
    UP: AF -> MB-UPF
Full-service mode:
    CP: AF -> (NEF) -> MBSF -> MB-SMF
    UP: AF -> MBSTF -> MB-UPF
Shared delivery:
    MB-UPF -> NG-RAN -> UE
Individual delivery:
    MB-UPF -> UPF -> NG-RAN -> UE (MBS data sent via PDU Session)

## Slide 11: Shared delivery and Individual delivery
5GC Shared MBS traffic delivery method:
    Broadcast and multicast MBS sessions
    Deliver (a single copy of) MBS data packets to RAN node
    multicast transport & unicast transport options
5GC Individual MBS traffic delivery method:
    Applicable for Multicast MBS session
    NG-RAN not supporting MBS
    Deliver (multiple copies of) MBS data packets per-UE PDU session

## Slide 12: Multicast session activation
MB-SMF activates the NG-RANs via AMF
SMF request AMF to page those IDLE UEs: If NG-RAN support 5MBS group paging applies, otherwise legacy individual paging applies
When UE responds paging, SMF establish QoS flows for individual delivery and “add” the UE to be associated with the MBS Session
Requiring PDU session resources (DRB established)