## Slide 1
2021.11
Study on Application layer support for Personal IoT and Residential Networks (PIRateAPP)

## Slide 2
02.
Requirements, Scenarios, Motivations
03.
Objects
01.
Aspects
CONTENTS

## Slide 3
  PIRates = PIN (Personal IoT Networks) + 5G Residential (CPN, customer premise network)
  CPNs and PINs have in common that in general they are owned, installed and/or (at least partially) configured by a customer of a public network operator.
  Personal IoT Networks (PINs) and Customer Premises Networks (CPNs) provide local connectivity between UEs and/or non-3GPP devices in PIRates network.
    CPN:
      via eRG (evolved Residential Gateway), provide access to 5G network
      Via PRAS (Premises Radio Access Station), UEs can get access to the CPN and/or 5G network services.
    PIN:
      via PIN elements with Gateway capability, provide access to 5G network; Can communicate with PIN Elements that are not within range to use PIN Direct Connection.
      PIN elements communicate each other using PIN Direct Connection;
PIRate network introduction (clause 6.38, TS 22.261)
5GS
Gateway Accesses
UE & Devices
PIRATES
PRAS
eRG
PEGC

## Slide 4
  Types of gateway
    PIN Element with Gateway Capabilities (PEGC) (e.g., relay UE)
    Premises Radio Access Station (PRAS)
    evolved Residential Gateway (eRG)
  Personal IoT Network (PIN)
    Localized with PEGC (at least one within a PIN)
    Direct 5GS access (not localized)
  Customer Premises Network (CPN)
    Localized with eRG
    Localized with PRAS
    Localized with PRAS+eRG
Aspects within Personal IoT and Resident networks
5GS
PIN Element
(not localized)
PIN Element
(not localized)
CPN
PRAS
CPN
eRG
PIN
(localized)
PEGC

## Slide 5
03.
Objectives
01.
Aspects
02.
Requirements, Scenarios, Motivations
CONTENTS

## Slide 6
Scenarios and Motivations
UE inside PIRates network:
  UE inside PIRate network discovers a printer and this printer’s service
  UE has direct communication with PIRates element and delivers the picture to this printer
  UE triggers the application to print the picture
Figure: Application and service discovery
UE B outside PIRate
PIRate Network
UE A inside PIRate
5GS
PIRates direct communication
External communication
UE outside PIRates network:
  UE outside PIRate network discovers a printer and this printer’s service via 5GS.
  5GS does potential Authentication and authentication
  For allowed UE, UE delivers the picture to this printer via 5GS
  For allowed UE, UE triggers the application to print the picture via 5GS
PIRates element: printer
Note: SA2 focus on UE/PIN elements discovery, and SA6 focus on service/application discovery in PIRates

## Slide 7
When UE A located outside of room, the UE display the video on UE screen.
When UE A move inside the room, the UE may have the actions below:
  UE discovers the PIRates elements and applications which can display the video in room
  UE switches the video from UE to the PIRate elements
  The application in PIRate network interacts with server and display the video.
Scenarios and Motivations
UE A outside room
server
Localized Network
UE A inside room
UE A move from outside to inside room
PIRates direct communication
UE A move into room
Service flow for UE A outside
5GS
Figure: Service switch in when UE moves inside
Service flow for UE A inside

## Slide 8
Potential Architecture to support PIRatesAPP
Notes: Interface to 3GPP: network exposure
Existing capability: PIN elements topography, N6 Traffic Routing requirements, network topography, UE ID, UE location …

## Slide 9
02.
Requirements, Scenarios, Motivations
Objectives
01.
Aspects
CONTENTS
03.

## Slide 10
  Analyse the Stage 1 specifications (TS 22.261, TS 22.101) to determine which requirements of PIRates have potential application level impacts; For example, service discovery, service switch
  Develop key issues, corresponding architecture requirements and solution recommendations to enable the application layer support for PIRates services over 3GPP systems
      Application architecture to support PIRates, e.g.: Service enabler layer in PIN elements or PRAS
      Information and support from 3GPP network to PIRatesAPP network, e.g.: network exposure
  Service or applications discovery within a PIRates network.
      Service registration in PIRates network, for example in home or office
      Service discovery in PIRates network, from both PIRates elements or UE outside PIRates.
  To study the service path switch from between PIRates entity.
      Service switch from one PIN elements or UE to another PIN elements
      Service flow establishments or maintenance from PIRates elements to servers
Objectives

## Slide 12
Annex

## Slide 13
Requirements from TS 22.261 of connection:
  The 5G system shall allow PIN Elements to communicate when there is no connectivity between a PIN Element with Gateway Capability and a 5G network.
  The 5G system shall support applications on an Application Server connected to a CPN or PIN.
  Subject to regulatory requirements and operator policy, the 5G system shall support an efficient data path within the CPN for intra-CPN communications.
Requirements from TS 22.261 of service discovery:
  The 5G system shall efficiently support service discovery mechanisms where a UE or non-3GPP device in a CPN or PIN can discover, subject to access rights:
    availability and reachability of other entities (e.g. other UEs or non-3GPP devices) on the CPN or PIN;
    capabilities of other entities on the CPN or PIN (e.g. eRG, relay UE, connection types) and/or;
    services provided by other entities on the CPN or PIN (e.g. the entity is a printer).The 5G system shall support a mechanism for the PIN user to indicate whether a PIN element is discoverable by other PIN elements of the same PIN.
  The 5G system shall support a mechanism for the PIN user to indicate whether a PIN element is discoverable by UEs that are not members of the PIN.
Requirements from SA1
Application connection and service discovery
CPN
CPN
PIN
(localized)
5GS
PIN
PIN Element
(not localized)
PIN Element
(not localized)
UE outside
PIN
UE outside
PIN
PRAS
eRG
PEGC