3GPP TSG-SA WG6 Meeting #46-e	S6-212591

e-meeting, 15th – 23rd November 2021	(revision of S6-21xxxx)

Source:	China Mobile

Title:	solution for KI 14

Spec:	3GPP TR 23.700-99

Agenda item:	10.7

Document for:	Approval

Contact:	Shaowen Zheng, zhengshaowen@chinamobile.com

1. Introduction

This paper proposes a solution for KI 14.

2. Reason for Change

This solution proposes a solution for key issue 14. An EES can provide 5GC with the required N6 traffic routing info for an EAS in advance. Then the EES can trigger the AF request to influence traffic routing for any UE accessing the EAS.

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-98 V0.3.0.

* * * First Change * * * *

# 7	Solutions

## 7.0	Mapping of solutions to key issues

Table 7.0-1 Mapping of solutions to key issues

|  | KI #1 | KI #2 | KI #3 | KI #4 | KI #5 | KI #6 | KI #7 | KI #8 | KI #9 | KI #10 | KI #12 | KI #13 | KI #14 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Sol #X |  |  |  |  |  |  |  |  |  |  |  |  | X |

* * * Next Change * * * *

## 7.x	Solution #x: Application traffic influence for initially selected EAS

### 7.x.1	Architecture enhancements

### None.

### 7.x.2	Solution description

7.x.2.1 General

This solution provide a solution for key issue 14. An EES can provide 5GC with the required N6 traffic routing info for an EAS in advance, e.g. after EAS is instantiated and registered to an EES. Then the EES can trigger the AF request to influence traffic routing for any UE accessing the EAS.

7.X.2.2 procedure

Figure 7.X.2.2:  AF influence the traffic for EAS

1.	The EAS sends an EAS registration request to the EES with traffic influence request, the request consists of traffic Route selection parameter such as N6 Traffic Routing requirements.

2.	The EES performs an authorization check to verify whether the EAS has the authorization to register on the EES and application traffic influence.

3.	Upon successful authorization, the EES sends the traffic influence request to 5GC to influence the traffic for EAS as described in 3GPP TS 23.501, clause 5.6.7.1.

4.	The EES sends the EAS registration response to EAS with traffic influence response.

Then the Traffic influence request/response should be added to EAS registration request and response table.

Table 8.4.3.3.2-1: EAS registration request

| Information element | Status | Description |
| --- | --- | --- |
| EAS Profile | M | EAS Profile as described in Table 8.2.4-1 |
| Security credentials | M | Security credentials of the EAS. |
| Proposed expiration time | O | Proposed expiration time for the registration |
| Traffic influence request | O | Indicator of whether the traffic influence is required. |
| > traffic route selection parameter | O | If traffic influence is required, the traffic route selection parameter such as N6 Traffic Routing requirements is also provided. |

Table 8.4.3.3.3-1: EAS registration response

| Information element | Status | Description |
| --- | --- | --- |
| Successful response | O | Indicates that the registration request was successful. |
| > Registration ID | M | Identifier of the registration. |
| > Expiration time | O | Indicates the expiration time of the registration. To maintain an active registration status, a registration update is required before the expiration time. If the Expiration time IE is not included, it indicates that the registration never expires. |
| Failure response | O | Indicates that the registration request failed. |
| > Cause | O | Indicates the cause of registration request failure |
| Traffic influence response | O | Indicates that the Traffic influence was successful or not. |

# Text boxes

## 4.14	Key issue #14: Application traffic influence for initially selected EAS

The application traffic is between the AC and EAS and 3GPP CN provides the underlying connectity for the application traffic. The EEC starts with EAS discovery first in order to offer EAS(s) to AC to start communication with the initially selected EAS. Later on, if the EAS relocation criteria is met, the EAS relocation procedure happens, which consists of EAS discovery, application traffic influence, application context transfer and AC communication with the new EAS.

Currently, it is not clear in the specification how to influence the application traffic with best optimal user plane routing when initial EAS discovery is completed in the application layer.

Open issues:

-	Whether and how the EEL can be involved to influence the application traffic routing in AC communication with the initially selected EAS.