3GPP TSG-SA WG6 Meeting #46-e	S6-212655

e-meeting, 15th – 23rd November 2021	(revision of S6-xxxx)

Source:	Huawei, Hisilicon

Title:	Key issue on enhancement to EEL support for application context transmission

Spec:	3GPP TR 23.700-98 v0.3.0

Agenda item:	10.7

Document for:	Approval

Contact:	Yajie Hu <Huyajie1@huawei.com>

1. Introduction

This pCR provides a Solution on support for roaming UEs.

2. Reason for Change

The Application context is transferred via EEL is specified in release 17. This approach has the following advantages:

- It will simplify the deployment of EES and EAS for ECSPs (especially when MNOs are also ECSPs): Currently, in most ACR scenarios, two different data transmission mechanisms are used for the application context transmission and EEC context transmission. Using one unified transmission mechanism enabled by the EES will enhance the value of ECSP services provided towards the EASs.

- It will provide better transmisson performance: The ECSP transmission mechanism is usually a dedicated IP connection e.g. VPN, whose connectivity performance is better than that of application layer.

- It can offer a value added mechanism that can be utilized by the EAS to enable them to reduce the implementation complexity of EAS handling of context transmission mechanisms and also enables reuse of commonly deployed mechanisms of the ECSP by the EAS.

But it is limited to the EELManagedACR scenario. Other ACR scenarios can also use the same machanism by using such EEL capability especially for the EAS without dedicated connection.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-98 v0.3.0.

* * * First Change * * * *

## 4.X	Key issue #x: Enhancement to edge enabler layer support for application context transmission

The Application context is transferred via EEL is specified in release 17. But in Rel 17, Application context transferred via EEL is limited to the EELManagedACR mechanism supported in the S-EES executed ACR scenario specified in 3GPP TS 23.558[x] clause 8.8.2.5. Other ACR scenarios can also use the same machanism by using such EEL capability especially for the EAS without dedicated connection.

Open issue:

-	Whether and how to utilize EES capability to transfer the application context for ACR scenarios 8.8.2.2, 8.8.2.3, 8.8.2.4 and 8.8.2.6?

* * * End of Change * * * *