3GPP TSG-SA WG6 Meeting #46-e	S6-212673

e-meeting, 15th – 23rd November 2021	(revision of S6-21xxxx)

Source:	Samsung

Title:	Proposal of new open issue for key issue #14 Application traffic influence for initially selected EAS

Spec:	3GPP TR 23.700-98 0.3.0

Agenda item:	10.7

Document for:	Approval

Contact:	Cheolung LEE <chw.lee @samsung.com>

1. Introduction

This contribution proposes a new open issue for key issue #14 Application traffic influence for initially selected EAS

2. Reason for Change

This contribution proposes clarification of open issues. It is not clear whether EEL can derive that solution on its own or interact with 5GC to solve the open issues about how to influence application traffic routing in AC communication. 5GC may be involved to influence for AC-EAS sessions. Therefore, it is necessary to discuss which Entity or Procedure can interact with 5GC. It can also be discussed which entities can configure or provide information for influence of AC-EAS session creation or update.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes in TS 23.700-98.

* * * First Change * * * *

## 4.14	Key issue #14: Application traffic influence for initially selected EAS

The application traffic is between the AC and EAS and 3GPP CN provides the underlying connectity for the application traffic. The EEC starts with EAS discovery first in order to offer EAS(s) to AC to start communication with the initially selected EAS. Later on, if the EAS relocation criteria is met, the EAS relocation procedure happens, which consists of EAS discovery, application traffic influence, application context transfer and AC communication with the new EAS.

Currently, it is not clear in the specification how to influence the application traffic with best optimal user plane routing when initial EAS discovery is completed in the application layer.

Open issues:

-	Whether and how the EEL can be involved to influence the application traffic routing in AC communication with the initially selected EAS.

-	Whether and how EEL configuration information that may influence application traffic routing.

-	Which entities can configure or provide information for application traffic influence routing.

-	Whether and how EEL interact with 5GC for application traffic influence routing.

* * * END OF Change * * * *