3GPP TSG-SA WG6 Meeting #46-e	S6-212636(rev1)

15-23 November 2021, e-meeting 	revision of S6-212308

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.558 | CR | 0042 | rev | 3 | Current version: | 17.1.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Cancellation Support in ACR |
| --- | --- |
| Source to WG: | Huawei, HiSilicon, China Mobile, China Telecom, CATT |
| Source to TSG: |  |
| Work item code: | EDGEAPP |  | Date: | 2021-11-10 |
| Category: | F |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Currently five ACR scearios have been specified in clause 8.8.2. ACR scenarios of clauses 8.8.2.2, 8.8.2.3 and 8.8.2.6 are initiated by EEC. ACR of 8.8.2.4 is decided and started by S-EAS. The ACR in clause 8.8.2.5 can be detected by EEC or S-EAS, but it is started by S-EES. In addition each ACR scenario, supports service continuity planning. According clause 8.8.1.2: Quote from TS23.558: “In service continuity planning, the Application Context may be duplicated and sent from the S EAS to the T EAS before the UE moves to the expected location. In this case, the Application Contexts in S EAS and T EAS are synchronized when the Application Context is updated until the AC connects to the T-EAS.” In all ACR scenarios, currently the below NOTE is misinterpreted as ACR termination mechanism: “NOTE: The S-EAS or T-EAS can further decide to terminate the ACR, and the T-EAS can discard the application context based on information received from EEL and/or other methods (e.g. monitoring the location of the UE). It is up to the implementation of the S-EAS and T-EAS whether and how to make such a decision.” In reality there is a lack of ACR termination or cancellation mechanism and it is assumed that the ACR termination can be handled by EAS implementation which are out of the scope of the current specification. The following issues exist with such assumption about termination mechanism: In EEC initiated scenarios, due to UE mobility planning changes there may be a need to terminate an already launched ACR. However, there is no way that the S-EAS or T-EAS can detect this intention from the EEC, and hence cannot further decide to terminate the ACR by just monitoring the current location of the UE. In such scenarios how the termination happens is unspecified and is left to implementation of the S-EAS and T-EAS, and hence leading to case where ACR can continue to exist for a very long time and hence will occupy network, computing and storage resources of the EAS, which in turn may lead to denial of service. According to the above quote, ACT and application context synchronization between the EASs continues until the UE connects to the T-EAS which is unnecessary. In such scenarios EEC context is also transferred between S-EES and the T-EES which again consums network, computing and storage resources at the T-EES, as there is a lack of any mechanism to cancel EEC context relocation and free up unnecessary storage which in turn may lead to denial of service. The implementation of the EAS is burdned to handle all the logic related to termination behaviours of ACR which will be unreliable, arbitrary, and not testable for the ACR scenarios. In addition, this unnecessary increased complexity of the EAS implemenation may demotivate the use of ACR service provided by the EEL. Several parallel ACRs for the same EEC can be initiated e.g. for a UE with high mobility and high reliability requirement (e.g. Vehicular UE or a UE in a vehicle). Due to high mobility, an ACR that has been initiated might not be needed and it cannot rely only on EAS implementation to handle the required ACR termination. Due to the above listed issues for current mechanism of ACR termination, the real deployment of ACR may lead to frequent and serious misoperations (FASMO). To prevent these FASMO, this CR proposes addition of the cancellation mechanism to ACR. This has the following benefits: It enables the ACR initiator to cancel the ongoing ACR, as the ACR initiator also has all the triggering conditions for ACR cancellation. It prevents unnecessary application context synchronization between EASs and also prevents the unnecessary occupation of network, computing and storage resources at the EASs. It enables timely clean up of unused EEC context at the T-EES and also prevents the unnecessary occupation of network, computing and storage resources at the EESs. It enables the EAS to implement a clean termination logic, for the ACR scenarios which are initiated by EEC or EES. It enables testability of ACR launching and corresponding cancellation. Currenly the bellow NOTE in captured for the ACT step in ACR scenarios, but it can create confusion that S-EAS and T-EAS can terminate the ACR in all scenarios. “NOTE: The S-EAS or T-EAS can further decide to terminate the ACR, and the T-EAS can discard the application context based on information received from EEL and/or other methods (e.g. monitoring the location of the UE). It is up to the implementation of the S-EAS and T-EAS whether and how to make such a decision.” However, the S-EAS and T-EAS engage only in ACT and hence the EASs can only terminate the ACT process. Therefore, we propose to correct the usage of ACR to ACT in the NOTE. The aspect of S-EAS cancelling the initiated ACR for the scenario of clause 8.8.2.4 is supported by the proposed ACR cancellation mechanism. In the current release it is proposed to support ACR cancellation only by the ACR initiator. |
| Summary of change: | 8.8.3.x: Add a new section for ACR cancellation procedure. 8.8.4.y: Add a new section for ACR cancellation request. 8.8.4.z: Add a new section for ACR cancellation response. 8.8.4.yy: Add a new section for ACR cancellation indication. 8.8.4.zz: Add a new section for ACR cancellation indication response. 8.8.2.2, 8.8.2.3, 8.8.2.4, 8.8.2.5, 8.8.2.6: In ACR scenarios add the cancellation step. |
| Consequences if not approved: | Lack of an ACR cancellation mechanism leads to FASMO of the ACR feature where the entities like EAS and EES cannot be controlled for triggering conditions which necessitates ACR cancellation, e.g. UE permanently stops moving, changes in UE mobility planning, etc. |
| Clauses affected: | 8.8.3.x (new), 8.8.4.y (new), 8.8.4.z (new), 8.8.4.yy (new), 8.8.4.zz (new), 8.8.2.2, 8.8.2.3, 8.8.2.4, 8.8.2.5, 8.8.2.6 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

# * * * Change 1 * * * *

#### 8.8.1.3            Actions during the interval between ACT and the application context being taken in to use

After ACT but before the context at the T-EAS is taken into use, the S-EAS and T-EAS must maintain and synchronize the transferred context. The interval between ACT and taking the context into use can be significant (e.g. in the predicted case). During this interval, the following events are possible:

a)   the UE remains in its current service area and does not take the transferred application context into use;

b)   the UE moves to a service area served by a different T-EAS; or

If the EEC decides ACR then the EEC should for events a) and b) re-send the ACR request (8.8.3.4) with updated information, i.e. action set to cancellation.

# * * * Change 2 * * * *

#### 8.8.3.4	ACR launching procedure

Figure 8.8.3.4-1 illustrates the ACR launching procedure by the EEC or the S-EAS.

If this procedure is triggered by the EEC, depending on the ACR action indicated in the ACR request, the procedure is used for either ACR initiation or ACR determination.

If this procedure is triggered by the S-EAS, the procedure is used for ACR determination.

Pre-condition:

1.	The EEC has been authorized to communicate with the EES as specified in clause 8.11, if the procedure is triggered by the EEC; and

2.	Information related to the S-EES is available with the S-EAS, if the procedure is triggered by the S-EAS.

Figure 8.8.3.4-1: ACR launching procedure

1.	The EEC or the S-EAS sends an ACR request message to the EES in order to start ACR. The ACR request message includes ACR action to indicate ACR initiation request or ACR determination request or ACR cancellation request. If the procedure is triggered by the S-EAS, the ACR request message is only for ACR determination.

An ACR request for ACR initiation sent by the EEC:

-	includes an indication of whether the EEC requests the EES to perform EAS notification; and

-	provides information used by EES to perform AF traffic influence as in 3GPP TS 23 501 [2].

An ACR request for ACR determination sent either by the EEC or the EAS informs the EES that the need for ACR has been detected by the requestor.

2.	The EES checks if the requestor is authorized for this operation. If authorized, the EES processes the request and performs the required operations.

If the request in step 1 is for ACR initiation:

-	the EES may use information provided in the request to apply the AF traffic influence with the N6 routing information of the T-EAS in the 3GPP Core Network (if applicable), as described in 3GPP TS 23.501 [2], clause 5.6.7.1; and

-	if the EAS notification indication is provided in the step 1 request and the EAS has subscribed to receive such notification, the EES shall notify the EAS about the need to start ACR.

If the request in step 1 is for ACR determination, the EES decides to execute ACR as described in clause 8.8.2.5.

If the request in step 1 is for ACR cancellation:

-  the EES sends ACR cancellation indication to the remote EES to inform about the cancellation of the ACR. S-EES and T-EES handle the EEC context as defined in clause 8.9.1.4.

If the request in step 1 is to the S-EES, the remote EES is the T-EES of the ACR. Otherwise if the request in step 1 is to the T-EES, the remote EES is the S-EES.

-  if the EAS notification indication is provided in the step 1 request and the EAS has subscribed to receive such notification, the EES shall notify the EAS about the cancellation of the ACR.

3.	The EES responds to the requestor's request with an ACR response message.

# * * * Change 3 * * * *

#### 8.8.4.4	ACR request

Table 8.8.4.4-1 describes information elements for the ACR request sent either from the EEC to the S-EES or T-EES, or by the S-EAS to the S-EES.

Table 8.8.4.4-1: ACR request

| Information element | Status | Description |
| --- | --- | --- |
| Requestor Identifier | M | Unique identifier of the requestor (i.e. EECID or EASID). |
| Security credentials | M | Security credentials resulting from a successful authorization for the edge computing service. |
| EASID | O | Identifier of the EAS |
| UE identifier (NOTE 4) | O | The identifier of the UE (i.e. GPSI). |
| ACR action (NOTE 3) | M | Indicates the ACR action (ACR initiation or ACR determination or cncellation) |
| ACR initiation data (NOTE 2) | O | ACR initiation IEs to be included in an ACR request message when ACR action indicates it is ACR initiation request. |
| > T-EAS Endpoint | M | Endpoint information (e.g. URI, FQDN, IP 3-tuple) of the T-EAS. |
| > DNAI of the T-EAS | O | DNAI information associated with the T-EAS. |
| > N6 Traffic Routing requirements | O | The N6 traffic routing information and/or routing profile ID corresponding to the T-EAS DNAI. |
| > EAS notification indication | M | Indicates whether to notify the EAS about the need of ACR. |
| > S-EAS endpoint (NOTE 1) | O | Endpoint information of the S-EAS |
| > EEC context relocation details | O | Information required for EEC context relocation using the EEC context push or EEC context pull mechanisms. |
| >> EEC Context ID (NOTE 5) | O | Identifier of the EEC Context |
| >> S-EES ID (NOTE 5) | O | Identifier of the EES that provided EEC context ID. |
| >> S-EES endpoint (NOTE 5) | O | The endpoint address (e.g. URI, IP address) of the EES that provided EEC context ID. |
| >> T-EES ID (NOTE 6) | O | Identifier of the T-EES. |
| >> T-EES endpoint (NOTE 6) | O | The endpoint address (e.g. URI, IP address) of the T-EES. |
| ACR determination data (NOTE 2) | O | ACR determination IEs to be included in an ACR request message when ACR action indicates it is ACR determination request. |
| > S-EAS endpoint | M | Endpoint information of the S-EAS |
| ACR cancellation data (NOTE 2) | O | ACR cancellation IEs to be included in an ACR request message when ACR action indicates it is ACR cancellation request. |
| > S-EAS endpoint | M | Endpoint information of the S-EAS |
| > T-EAS Endpoint | M | Endpoint information (e.g. URI, FQDN, IP 3-tuple) of the T-EAS. |
| > EAS notification indication | M | Indicates whether to notify the EAS about the cancellation of ACR. |
| > EEC Context ID | O | Unique identifier of the EEC Context indicated to be related to a cancelled ACR. |
| > S-EES ID (NOTE 5) | O | Identifier of the EES that provided EEC context ID. |
| > S-EES endpoint (NOTE 5) | O | The endpoint address (e.g. URI, IP address) of the EES that provided EEC context ID. |
| > T-EES ID (NOTE 6) | O | Identifier of the T-EES. |
| > T-EES endpoint (NOTE 6) | O | The endpoint address (e.g. URI, IP address) of the T-EES. |
| NOTE 1: This IE shall be present if the EAS notification indication indicates that the EAS needs to be informed. NOTE 2: One of the ACR initiation or ACR determination or ACR cancellation shall be included corresponding to the ACR action. NOTE 3: This IE shall indicate ACR determination if the request originates from the S-EAS. NOTE 4: This IE shall be present if the request originates from the EEC. NOTE 5: This IE may be present only if the request originates from the EEC towards the T-EES. NOTE 6: This IE may be present only if the request originates from the EEC towards the S-EES. |

# * * * Change 4 * * * *

#### 8.9.1.4	EEC Context handling at Application Context Relocation

The EEC Context provided to a target EES in an EEC Context Pull relocation or an EEC context Push relocation shall be stored at the target EES, as follows:

-	If an EEC context with the same EEC ID, EEC Context ID and source Endpoint already exists at the target EES, the EEC Context is updated.

-	If an EEC context with the same EEC ID, EEC Context ID and source Endpoint does not exist at the target EES, the EEC Context is stored.

After a successful EEC Context Relocation procedure is performed at ACR, the source EES shall determine to be stale the element(s) of the list of Service Session Context(s) information included in the request (i.e., relocated). If all Service Session Context(s) information in the EEC Context are stale, the EEC Context is determined to be stale and the EEC to be de-registered.

During the ACR one EES can send an ACR cancellation indication message to the other EES as described in clause 8.8.4.4. In that case, the S-EES and T-EES clean up the any residual EEC context indiacted in the ACR cancellation indication, if it has been transferred due to EEC context relocation within the corresponding ACR procedure.

# * * * Change 5 * * * *

#### 8.8.4.yy	ACR cancellation indication

Table 8.8.4.yy-1 describes the information elements for the ACR cancellation indication sent from the S-EES to the T-EES or from T-EES the S-EES.

Table 8.8.4.y-1: ACR cancellation indication

| Information element | Status | Description |
| --- | --- | --- |
| Requestor Identifier | M | Unique identifier of the requesting EES. |
| Security credentials | M | Security credentials resulting from a successful authorization for the edge computing service. |
| EEC Context ID | M | Unique identifier of the EEC Context indicated to be related to a cancelled ACR. |

#### 8.8.4.zz	ACR cancellation indication response

Table 8.8.4.zz-1 describes the information elements for the ACR cancellation indication response sent either from the T-EES to the S-EES or from S-EES the T-EES.

Table 8.8.4.zz-1: ACR cancellation indication response

| Information element | Status | Description |
| --- | --- | --- |
| Successful response | O | Indicates that the ACR cancellation indication request was successful. |
| Failure response | O | Indicates that the ACR cancellation indication request failed. |
| > Cause | O | Indicates the cause of ACR cancellation indication request failure |

# * * * End of the Change(s) * * * *