3GPP TSG-SA WG6 Meeting #47-e	DRAFT_S6-220019

e-meeting, 14th – 22nd February 2022

3GPP TSG-SA Meeting #94-E	SP-211511

online, 14th – 20th December 2021

# Source:	InterDigital

# Title:	Revised SID on Study on enhanced architecture for UAS Applications

# Document for:	Agreement

Agenda Item:	10

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title:	Study on enhanced architecture for UAS Applications

## Acronym: FS_eUASAPP

## Unique identifier: 930012

## Potential target Release:	Rel-18

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X |  | X |  |
| No |  |  | X |  |  |
| Don't know | X |  |  |  | X |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a

|  | Feature |
| --- | --- |
|  | Building Block |
|  | Work Task |
| X | Study Item |

### 2.2	Parent Work Item

| Parent Work / Study Items |
| --- |
| Acronym | Working Group | Unique ID | Title (as in 3GPP Work Plan) |
| EAV | S1 | 840083 | 5G Enhancement for UAVs |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |
| 810019 | Study on EAV | SA1, Initial study on stage 1 requirement for UAS (FS_EAV) |
| 820011 | Study on supporting Uncrewed Aerial Systems Connectivity, Identification, and Tracking | SA2, Architectural aspects for UAS (FS_ID_UAS_SA2) |
| 810049 | Remote Identification of Uncrewed Aerial Systems | SA2, Architectural aspects for UAS (ID_UAS) |
| 940051 | Study on Phase 2 for UAS, UAV and UAM | SA2, Rel-18 Architecture Enhancement for UAV and UAM (FS_UAS_Ph2) |
| 880007 | Study on security aspects of Uncrewed Aerial Systems (UAS) | SA3, Security aspects for UAS (FS_UAS_SEC) |
| 820026 | Study on application layer support for Uncrewed Aerial System (UAS) | SA6, Application aspects for UAS (FS_UASAPP) |
| 920045 | Application layer support for Uncrewed Aerial System (UAS) | SA6, Application aspects for UAS (UASAPP) |

## 3	Justification

As part of Rel-17, SA6 normatively specified the overall application layer architecture to enable application support for UAS applications over 3GPP networks in 3GPP TS 23.255.

SA6 also specified related generic support for UAS applications in the SEAL layer in 3GPP TS 22.434.

The Rel-17 work for UAS included the fundamental features:

- communications between UAVs within a geographical area;

- UAV and UAV-C pairing and C2 QoS provisioning using Group ID;

- C2 communication mode selection and switching; and

- real-time UAV connection status monitoring and location reporting.

Relevant aspects of SEAL were enhanced to secure support for the following services:

- group management;

- location management; and

- network resource management.

In Rel-18, the UAS architecture requires enhancements to further improve and enhance functionality in 3GPP for improved support for the aviation industry.

In release 17, no work was done by 3GPP to support that the USS serving a UAV could change during flight. However, in wide and rural areas, the UAS may enter areas of responsibility of different USSes and experience both national as well as international roaming. Due to this, scenarios where a UAS is served by multiple USSes during the same flight must be studied and the impacts on the UAS application layer architecture (e.g. impact on services over UAE-E reference point) and SEAL to support such scenarios need to be identified.

The above may also impact location and support of PC5 versus the C2 switching. Due to this, new functionality for the UAS application due to location and support of PC5 versus C2 switching must be studied and the impacts on the UAS application layer architecture and SEAL to support such scenarios need to be identified.

## 4	Objective

The SA6 objectives of this study item include the following:

1)	analyze requirements in 3GPP TS 22.125 and further identify key issues, develop corresponding architectural requirements and potential enhancements to the application layer architecture as required, including:

a)	support for multiple USS/ UTMs;

b)	support for monitoring by USS/UTM of C2 communication QoS and communication link status including for UAV moving between EPS and 5GS, see 3GPP TS 22.125 clause 6.2;

c)	support for service restriction for UEs onboard of UAV, see 3GPP TS 22.125 clause 6.3; and

d)	usage of PC5 communication between UAVs or UAV and UAV-C;

2)	identify potential solutions as required, including the information flows and the APIs satisfying the architectural requirements and enhancements identified in bullet 1) above; and

3)	identify potential improvements to SEAL based on the architectural requirements and enhancements identified in bullet 1) above.

For some items, e.g. d) above, SA6 is dependent on progress and decisions by SA2.

## 5	Expected Output and Time scale

| New specifications |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Rapporteur |
| Internal TR | 23.700-55 | Study on enhanced Application Architecture for UAS applications | SA#96 (June 2022) | SA#97 (Sept 2022) | Atle Monrad, InterDigital, atle.monrad@interdigital.com |

NOTE:	Conclusions and completion of the study will be aligned with the study in SA2.

## 6	Work item Rapporteur(s)

Monrad, Atle, InterDigital, atle.monrad@interdigital.com

## 7	Work item leadership

SA6.

## 8	Aspects that involve other WGs

SA1 for service requirements, SA2 for system aspects and SA3 for security aspects.

## 9	Supporting Individual Members

Supporting IM name

InterDigital

AT&T

Samsung

Tencent

Qualcomm

SKT

Huawei

Lenovo

Motorola Mobility

Airbus

Deutsche Telekom