3GPP TSG-SA WG6 Meeting #47e	S6-22xxxx

E-meeting, 14th – 22nd of February 2022	(revision of S6-22xxxx)

# Source:	Nokia, Nokia Shanghai Bell, UIC, Kontron Transportation France

# Title:	New WID on Interconnection and Migration Aspects for Railways

# Document for:	Approval

Agenda Item:	10

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: Interconnection and Migration Aspects for Railways

## Acronym: IRail

## Unique identifier: xxxx

Potential target Release: Rel-18

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X |  | X |  |
| No |  |  | X |  |  |
| Don't know | X |  |  |  | X |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a

| X | Feature |
| --- | --- |
|  | Building Block |
|  | Work Task |
|  | Study Item |

### 2.2	Parent Work Item

| Parent Work / Study Items |
| --- |
| Acronym | Working Group | Unique ID | Title (as in 3GPP Work Plan) |
| FS_IRail | SA6 | 880034 | Study of interconnection and migration aspects for railways |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |

Dependency on non-3GPP (draft) specification: None

## 3	Justification

The present level on Mission Critical interconnection and migration functionality has not fully addressed the needs for railway communications. Trains are crossing the border much more frequent than in public safety scenarios, especially the need to continue the communication when crossing borders is essential for railway operations. Before starting the normative stage 2 work on certain aspects, a study was done to identify gaps in existing mechanisms on interconnection and on migration and to develop solutions for those gaps.

The results of the study are captured by a technical report (3GPP TR 23.700-90) which provides recommendations for candidate solutions for normative work.

## 4	Objective

In order to satisfy remaining interconnection and migration needs for railways, enhancements to technical specifications for MCPTT (3GPP TS 23.379), MCVideo (3GPP TS 23.281), MCData (3GPP TS 23.282) and in the common functional architecture (3GPP TS 23.280) are foreseen.

The focus is on the following (according to the study results):

1)	Functional architecture enhancements to support location information for interconnected MC systems.

2)	Private call using a functional alias towards a partner MC system.

3)	Migration towards another MC system during ongoing private communications.

4)	Migration towards another MC system during ongoing group communications.

5)	Optimize connectivity between MC systems for media and signalling routing and the IP connectivity between MC systems.

6)	Support of migration for MC service users towards an MC system when the primary and the partner MC system are not interconnected.

7)	Support of private call forwarding between MCPTT systems.

8)	Support of private call transfer between MCPTT systems.

No dependencies to other 3GPP groups were identified during study phase.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Rapporteur |

| Impacted existing TS/TR |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |
| TS 23.280 | Adding location information related functionality for interconnected MC system, enable migration of authorised MC service users when two MC systems are not interconnected, optimize media and signalling routing between MC systems | SA#98– December 2022 |  |
| TS 23.281 | Support MCVideo private calls towards another MC system by using functional aliases, adding procedures for migration during MCVideo private and group calls | SA#98– December 2022 |  |
| TS 23.282 | Support MCData calls towards another MC system by using functional aliases, adding procedures for migration during private and group MCData calls, optimize the IP connectivity between MCData systems | SA#98– December 2022 |  |
| TS 23.379 | Support MCPTT private calls towards another MC system by using functional aliases, adding procedures for migration during MCPTT private and group calls, enable private call forwarding/transfer between MCPTT systems | SA#98– December 2022 |  |

## 6	Work item Rapporteur(s)

Oettl, Martin, Nokia, martin.oettl@nokia.com

## 7	Work item leadership

SA6

## 8	Aspects that involve other WGs

EPS/5GS transport aspects will involve SA2. Security aspects will involve SA3.

## 9	Supporting Individual Members

Supporting IM name

Nokia

Nokia Shanghai Bell

UIC

Kontron Transportation France

? Korea Railroad Research Institute (KRRI)

? Hansung University

? Motorola Solutions