## Slide 1: Issues using ACR with LADNs
InterDigital

## Slide 2: Overview
5 different ACR scenarios have been specified in 3GPP TS 23.558
  clause 8.8.2.2 to 8.8.2.6
Each flavor of Application Context Relocation supports a variant of Service Continuity Planning
  This result in 10 variations of the ACR procedures
The EEL allows the use of LADNs for EDNs
Issues have been identified when using ACR with LADNs
  When leaving LADNs, some ACR procedures without SCP fail
  When entering LADNs, some ACR procedures with SCP fail

## Slide 3: ACR without SCP
Procedure Name | Initiation by EEC using regular EAS Discovery | EEC executed ACR via S-EES | S-EAS decided ACR | S-EES executed ACR | EEC executed ACR via T-EES
TS 23.558 Clause | Clause 8.8.2.2 | Clause 8.8.2.3 | Clause 8.8.2.4 | Clause 8.8.2.5 | Clause 8.8.2.6
ACR execution steps | 1- T-EAS discovery (EEC/T-EES) 2- ACR initiation (EEC/S-EES) 3- EEC context relocation (S-EES/T-EES) 4- Application context relocation (S-EAS/T-EAS) | 1- T-EAS discovery (EEC/T-EES) 2- ACR initiation (EEC/S-EES) 3- EEC context relocation (S-EES/T-EES) 4- Application context relocation (S-EAS/T-EAS) | 1- T-EAS discovery (S-EAS/T-EES) 2- T-EAS declaration (S-EAS/S-EES) 3- EEC context relocation (S-EES/T-EES) 4- Target information notification (S-EES/EEC) 5- Application context relocation (S-EAS/T-EAS) | 1- T-EAS discovery (S-EES/T-EES) 2- EEC context relocation (S-EES/T-EES) 3- Target information notification (S-EES/EEC) 4- Application context relocation trigger (S-EES/S-EAS) 5- Application context relocation (S-EAS/T-EAS) | 1- T-EAS discovery (EEC/T-EES) 2- ACR initiation (EEC/T-EES) 3- EEC context relocation (T-EES/S-EES) 4- Application context relocation (T-EAS/S-EAS)
When leaving a LADN area
These ACR steps fail because communication between the LADN and the UE is not possible anymore

## Slide 4: ACR with SCP
Procedure Name | Initiation by EEC using regular EAS Discovery | EEC executed ACR via S-EES | S-EAS decided ACR | S-EES executed ACR | EEC executed ACR via T-EES
TS 23.558 Clause | Clause 8.8.2.2 | Clause 8.8.2.3 | Clause 8.8.2.4 | Clause 8.8.2.5 | Clause 8.8.2.6
ACR execution steps | 1- T-EAS discovery (EEC/T-EES) 2- ACR initiation (EEC/S-EES) 3- EEC context relocation (S-EES/T-EES) 4- Application context relocation (S-EAS/T-EAS) | 1- T-EAS discovery (EEC/T-EES) 2- ACR initiation (EEC/S-EES) 3- EEC context relocation (S-EES/T-EES) 4- Application context relocation (S-EAS/T-EAS) | 1- T-EAS discovery (S-EAS/T-EES) 2- T-EAS declaration (S-EAS/S-EES) 3- EEC context relocation (S-EES/T-EES) 4- Target information notification (S-EES/EEC) 5- Application context relocation (S-EAS/T-EAS) | 1- T-EAS discovery (S-EES/T-EES) 2- EEC context relocation (S-EES/T-EES) 3- Target information notification (S-EES/EEC) 4- Application context relocation trigger (S-EES/S-EAS) 5- Application context relocation (S-EAS/T-EAS) | 1- T-EAS discovery (EEC/T-EES) 2- ACR initiation (EEC/T-EES) 3- EEC context relocation (T-EES/S-EES) 4- Application context relocation (T-EAS/S-EAS)
Prior to entering a LADN area
These SCP steps fail (e.g. planning) because communication between the LADN and the UE is not yet possible

## Slide 5: ACR selection as a solution?
“Careful” selection of ACR scenario can sometime prevent LADN issues
  Ex: A UE using LADN resources could select an appropriate ACR scenario
However, ACR selection may not always prevent LADN issues
  Ex: Required ACR/SCP capabilities not supported by AC/EEC/EES/EAS
  Ex. Future EDN type (e.g. target) not known at ACR scenario selection

## Slide 6: Summary
ACR selection performed at the EEL may help prevent ACR issues with LADNs but it does not entirely solve the problem
Proposal:
  The problem must be discussed and acknowledged in SA2 and SA6.
  An LS to SA2 is proposed, asking for feedback of usage of ACR scenarios with LADN EDNs, see S6-220