3GPP TSG-SA WG6 Meeting #48-e	S6-220593

e-meeting, 5th – 14th April 2022	(revision of S6-22xxxx)

Source:	NTT DOCOMO

Title:	Clarification on general description for Solution #3

Spec:	3GPP TR 23.700-95 v1.1.0

Agenda item:	9.5

Document for:	Approval

Contact:	Yuji Suzuki (yuuji.suzuki.rm@nttdocomo.com)

1. Introduction

This contribution proposes to clarify the general description for Solution #3.

2. Reason for Change

The general description for Solution #3 reads that the AEF interacts with the ROAF to obtain the resource owner consent. According to the procedure, however, this process involves not only the ROAF but also the RO client. Thus, it is clarified that the AEF obtain the RO consent from the resource owner authorization function and/or the resource owner client. In addition, the RO registration is performed between the ROAF and RO client, so the description is modified accordingly.

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-95 v1.1.0.

* * * First Change * * * *

## 6.3	Solution #3: Obtaining resource owner consent upon service API invocation

### 6.3.1	Solution description

#### 6.3.1.1	General

This solution addresses the key issue #3 with regard to obtaining resource owner consent. Acting as the user consent enforcement point, the AEF judges whether the invoked service API requires the resource owner consent and whether a valid resource owner consent is already included in the service API invocation. If the resource owner consent is required and a valid resource owner consent is not included in the API invocation, the AEF in collaboration with the resource owner client and the resource owner authorization function obtains a valid resource owner consent before the service API execution is continued. For the interaction between the resource owner authorization function and the resource owner client, the resource owner registration may optionally be performed prior to the service API invocation.

Clause 6.3.1.2 shows the procedure for resource owner registration and clause 6.3.1.3 shows the procedure for obtaining resource owner consent.