3GPP TSG-SA WG6 Meeting #48-e	S6-220594

e-meeting, 5th – 14th April 2022	(revision of S6-22xxxx)

Source:	NTT DOCOMO

Title:	Functional model description to support 3rd party API providers with SNA enhancements

Spec:	3GPP TR 23.700-95 v1.1.0

Agenda item:	9.5

Document for:	Approval

Contact:	Yuji Suzuki (yuuji.suzuki.rm@nttdocomo.com)

1. Introduction

This contribution proposes a functional model to support 3rd party API providers with SNA enhancements.

2. Reason for Change

Current functional model in Clause 6.2.1.2 assumes that the API provider domain is in the PLMN trust domain. According to TS 23.222, however, the API provider domain can also be in the 3rd party trust domain. An enhanced functional model to support 3rd party API providers is needed.

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-95 v1.1.0.

* * * First Change * * * *

#### 6.2.1.2	Functional model

6.2.1.2.1	Functional model description for the CAPIF with SNA enhancements

Figure 6.2.1.2.1-1 shows the reference point based functional model for the CAPIF with enhancements to support SNA.

Figure 6.2.1.2.1-1: Functional model for the CAPIF with SNA enhancements

The resource owner client(s) are application clients used by end-users or subscribers of the API provider domain's service provider.

The resource owner client(s) reside within the API provider domain and interacts with the resource owner authorization function via CAPIF-8. The resource owner communicates with the resource owner authorization function to provide and revoke resource owner consent. The resource owner interactions are supported via a resource owner client, which is a client-side entity.

Editor's Note:	The location of the resource owner authorization function in the CAPIF functional model is FFS.

The API exposing function (e.g NEF) acts as a resource owner consent enforcement point as specified in 3GPP TS 33.501 [8] and interacts with the resource owner authorization function via CAPIF-9. The API exposing function shall support to retrieve the resource owner consent parameters from.the resource owner authorization function.

The API invoker interacts with resource owner authorization function via CAPIF-10/CAPIF-10e. The API invoker shall support to retrieve the resource owner consent parameters from the resource owner authorization function.

The API invoker interacts with CAPIF core function via CAPIF-1/CAPIF-1e to discover and obtain API access information. Further, the API invoker interacts with API exposing function via CAPIF-2/CAPIF-2e to perform service API invocations.

NOTE:	Security aspects including specification of the authorisation procedures are to be decided in SA3.

##### 6.2.1.2.2	Functional model description to support 3rd party API providers with SNA enhancements

Figure 6.2.1.2.2-1 shows the reference point based functional model to support 3rd party API providers with enhancements to support SNA.

Figure 6.2.1.2.2-1: Functional model to support 3rd party API providers with SNA enhancements

Figure 6.2.1.2.2-1 is regarded as an enhancement of Figure 6.2.1-1 of TS 23.222 [3] in the following points:

-	The resource owner authorization function and the resource owner client(s) are introduced in the API provider domains;

NOTE:	Resource owner authorization function within each domain would take care of user’s authorization for the protected resources belonging to its own domain. Therefore, authorization by a resource owner authorization function in the 3rd party API provider domain is necessary because the 3rd party API may make use of resources that are not in the PLMN domain. On the other hand, authorization by a resource owner authorization function in the PLMN domain is necessary because the 3rd party API provider may invoke an API over CAPIF-7e in the PLMN trust domain which would require the resource owner’s authorization/consent before a protected resource in the PLMN domain is accessed.

-	The API invokers interact with the resource owner authorization functions via CAPIF-10/CAPIF-10e;

-	The API exposing function in the 3rd party trust domain interacts with the API exposing function in the PLMN trust domain via CAPIF-7e.

#### The API exposing function may use the resource owner authorization function in the same API provider domain to obtain authorization grant from the resource owner to invoke the service APIs provided by the API provider. If the resource owner has business relationship with different API providers, the resource owner client in Figure 6.2.1.2.2-1 may be the same entity.