3GPP TSG-SA WG6 Meeting #48-e	S6-220741

e-meeting, 5th – 14th April 2022	(revision of S6-22xxxx)

Source:	Samsung

Title:	Pseudo-CR on Update to Solution #6

Spec:	3GPP TR 23.700-95 v1.1.0

Agenda item:	9.5

Document for:	Approval

Contact:	Basavaraj (Basu) Pattan, basavarajjp@samsug.com

1. Introduction

The Solution #6 is updated with more details on how the CCF can be reached by the API invoker and how the API provider may share the IP address information to the CCF.

2. Reason for Change

In absence of API provider information at the CCF for a subscriber IP address, then the CCF may use implementation mechanism to discover the API provider information based on IP address.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-95 v1.1.0.

* * * First Change * * * *

## 6.6	Solution #6: Discover a proper AEF with owner information

### 6.6.1	Description

The API provider hosts one or more service APIs and has a service API arrangement with CAPIF provider to offer the service APIs to the API invoker, as described in 3GPP TS 23.222 [3]. A CAPIF provider may have business relationships with multiple API providers (e.g. MNOs).

The AF knows UE IP address from the Application traffic. If the AF wants to contact with an API exposing function (AEF) provided by MNO but does not know which MNO the UE belongs to, the AF can utilize the information provided by Regional Internet Registry (RIR). e.g. Asia-Pacific Network Information Centre (APNIC) is responsible for providing allocation and administration services to Asia-Pacific's Internet service providers (ISPs) and Internet users. IP "whois" service can be used to retrieve IP address related information, for instance, with input of IP address 223.167.255.255 in https://wq.apnic.net/apnic-bin/whois.pl it gives the following result including the owner for such IP address (only partial result is listed here for relevant info):

% APNIC found the following authoritative answer from: whois.apnic.net

% [whois.apnic.net]

% Whois data copyright terms    http://www.apnic.net/db/dbcopyright.html

% Information related to '223.166.0.0 - 223.167.255.255'

% Abuse contact for '223.166.0.0 - 223.167.255.255' is 'hqs-ipabuse@chinaunicom.cn'

inetnum:        223.166.0.0 - 223.167.255.255

netname:        UNICOM-SH

descr:          CHINA UNICOM Shanghai city network

descr:          China Unicom

descr:          No.21,Jin Rong Street,Beijing,100033

descr:          P.R.China

country:        CN

admin-c:        CH1302-AP

tech-c:         CH1302-AP

remarks:        service provider

mnt-by:         APNIC-HM

mnt-lower:      MAINT-CNCGROUP-SH

mnt-routes:     MAINT-CNCGROUP-RR

status:         ALLOCATED PORTABLE

mnt-irt:        IRT-CU-CN

last-modified:  2013-08-08T23:17:38Z

source:         APNIC

Noting that such interaction with IP address administrative authority is out of the scope of 3GPP.

Once the AF knows which MNO it should contact for the API invocation related to a UE, the AF queries the CAPIF core function (CCF) with required API provider name (e.g. China Mobile Beijing) and CCF responds with the AEF information matching the required API provider name. The CCF knows the API provider name either via API management function triggered Registration procedure for the whole API provider domain functions or via the API publish function triggered service API information publish procedure for the AEF offered API(s). The impact for CAPIF procedures is illustrated in figure 6.6.1-1, and tables 6.6.1-1, table 6.6.1-2 and 6.6.1-3 describe the information flow impact with highlighted IEs.

Figure 6.6.1-1: API provider name used in CAPIF procedures

Table 6.6.1-1: Registration request

| Information element | Status | Description |
| --- | --- | --- |
| List of API provider domain functions | M | List of API provider domain functions including role (e.g. AEF, APF, AMF) and, if required, specific security information. |
| API provider name | O | The API provider name uniquely identifies an API provider (e.g. Internet Service Provider). |
| Security information | M | Information for CAPIF core function to validate the registration request |

Table 6.6.1-2: Service API publish request

| Information element | Status | Description |
| --- | --- | --- |
| API publisher information | M | The information of the API publisher may include identity, authentication and authorization information |
| Service API information | M | The service API information includes the service API name, API provider name (optional), service API type, communication type, description, Serving Area Information (optional), AEF location (optional), interface details (e.g. IP address, port number, URI), protocols, version numbers, and data format. |
| Shareable information | O (see NOTE) | Indicates whether the service API or the service API category can be published to other CCFs. And if sharing, a list of CAPIF provider domain information where the service API or the service API category can be published is contained. |
| NOTE: If the shareable information is not present, the service API is not allowed to be shared. |

Table 6.6.1-3: Service API discover request

| Information element | Status | Description |
| --- | --- | --- |
| API invoker identity information | M | Identity information of the API invoker discovering service APIs |
| Query information | M | Criteria for discovering matching service APIs (e.g. service API type, Serving Area Information (optional), preferred AEF location (optional), required API provider name (optional), interfaces, protocols) (see NOTE) |
| NOTE: It should be possible to discover all the service APIs. |

The API provider name can be shared between CCFs over CAPIF-6/6e reference point and the interconnection service API discovery may also include the required API provider name as query parameter.

Alternatively, to reduce the burden on API invoker side, API invoker may include subscriber IP address in the service API discover request in step 6 above and CCF uses implementation specific means (e.g. whois) to resolve the subscriber IP address to its owner information (e.g. API provider name) and then find the matching service API information with the owner information. CCF may also receive from the API provider, the mapping information between the subscriber IP address range information and the AEF information. For example, a NEF provider may share the IP address range information related to its subscribers that NEF provides the service to, while publishing the APIs at CCF.

* * * End of Changes * * * *