3GPP TSG-SA WG6 Meeting #48-e	S6-220922 REV 1

e-meeting, 5th – 14th April 2022	(revision of S6-220553)

Source:	Convida Wireless LLC

Title:	RO registration via AF

Spec:	3GPP TR 23.700-95 v.1.1.0

Agenda item:	9.5

Document for:	Approval

Contact:	Catalina Mladin, mladin.catalina@convidawireless.com

1. Introduction

This solution enables procedures for obtaining resource owner consent, and as such addresses key issue #3. In order to be able to obtain resource owner consent, a resource owner needs to register with the Resource Owner Authorization Function (ROAF). In cases in which the resource owner is managed via an AF, a registration procedure via the AF needs to be specified.

2. Reason for Change

Enable RO registration via an AF

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-95

* * * First Change * * * *

## 6.x	Solution #x: Resouce Owner registration by AF

### 6.x.1	Solution description

#### 6.x.1.1	General

This solution enables procedures for obtaining resource owner consent, and as such addresses key issue #3. In order to be able to obtain resource owner consent, a resource owner needs to register with the Resource Owner Authorization Function (ROAF).

In cases in which the resource owner is managed via an AF or when an RO client is not available at the UE (e.g. IoT devices), a registration procedure initiated by the AF needs to be specified. For constrained UE cases, the AF is also provisioned with conditions for triggering resource owner consent, e.g. time, API Invoker location, etc.

#### 6.x.1.2	Resource owner registration by AF

Figure 6.x.1.2-1 shows the procedure for resource owner registration byan AF.

Pre-conditions:

1.	The AF is authorised to access the resource owner authorization function on behalf of the resource owner; and

2.	The AF is pre-provisioned with resource owner information for registration

Figure 6.x.1.2-1: Procedure for resource owner registration by AF

- The AF sends resource owner registration request to the resource owner authorization function, including the resource owner identity (e.g., GPSI), security credentials and conditions for triggering resource owner consent.

Editor’s note: Provisioning of conditions for triggering resource owner consent to the AF is FFS.

2. The ROAF initiates the verification procedure and validates the resource owner registration request.

3. The ROAF sends resource owner registration response to the AF.

### 6.x.2	Solution evaluation

This solution complements the existing resource owner registration solution by enabling a registration via an AF, which is viable.