3GPP TSG-SA WG6 Meeting #48-e	S6-220549 Rev 2

e-meeting, 5th – 14th April 2022	(revision of S6-22xxxx)

Source:	Convida Wireless LLC

Title:	Solution for KI #1 Support for E2E Redundant Transport

Spec:	3GPP TR 23.700-34 v0.3.0

Agenda item:	9.10

Document for:	Approval

Contact:	Catalina Mladin, mladin.catalina@convidawireless.com

1. Introduction

This pCR provides a solution for Key Issue #1 on Redundant Transport

2. Reason for Change

Provide a solution for Key Issue #1

Rev1 removes comments and changes on changes, corrects agenda item.

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-34.

* * * First Change * * * *

## 6.X	Solution #X: Client initiated request for redundant transport

### 6.X.2	Solution description

#### 6.X.2.1	General

The following solution is provided for key issue #1. It complements solution #2.

#### 6.X.2.2	Procedure

Pre-conditions:

- The VAL server can discover and select the SEALDD server using CAPIF functions.

Figure 6.X.2.2-1: Client initiated request for redundant transport

1.	A VAL client determines to use SEALDD service to ensure that the data transmission quality for the application traffic is met and makes a service request to the SEALDD client. The request includes the application ID, the VAL server ID/address, the QoS requirements for the application traffic,

2. Upon receiving the request, the SEALDD client decides to establish redundant transmission path according to the QoS requirements. If necessary, the SEALDD client discovers a SEALDD server that supports redundant transport and can provide the SEALDD service to the VAL server.

NOTE: This step includes any other procedures necessary for the SEALDD client to be ready to receive services from the SEALDD server (e.g., registration, authorization). The step also includes any authorization necessary in the SEALDD layer (i.e., by SEALDD client, SEALDD server) to determine whether the redundant transmissions can be initiated on behalf of the VAL client.

3.	The SEALDD client sends a request to the SEALDD server to configure redundant transport for the application traffic. The request may include the application ID, the UE ID/address, the VAL server ID/address, the QoS requirements, the UE location, and a request for redundant transport. 4.	The SEALDD server allocates IP addresses and ports for the redundant transport paths and initiates the AF traffic influence procedure with the 5G network to create or update URSP rules for the UE. The request includes the UE ID and application descriptor for the application traffic. The UE receives the new or updated URSP rules from the 5G core network.

Editor’s Note: It is FFS whether and how the SEALDD user plane management functions (e.g., allocation of IP address) need to be considered as part of the NRM function.

5.	The SEALDD server responds to the SEALDD client providing the configuration status. The response includes the IP addresses and ports for the redundant transmission paths allocated in step 4. The SEALDD client and SEALDD server store the mapping between the application traffic and SEALDD traffic.

6.	The UE establishes redundant PDU sessions with the 5G network using the new or updated URSP rules.

The VAL client sends application traffic to the SEALDD client, which duplicates the application data on the redundant PDU sessions. The SEALDD server receives the redundant traffic and reassembles the data to send to the VAL server. Similarly, the SEALDD server duplicates downlink traffic from the VAL server and sends the data to the SEALDD client on the redundant PDU sessions. The SEALDD client eliminates the redundant data and reassembles data to send to the VAL client.

### 6.X.3	Solution evaluation

Editor's note:	Solution evaluation is FFS.