3GPP TSG-SA WG6 Meeting #48-e	S6-220919 REV1

e-meeting, 5th – 14th April 2022	(revision of S6-220745)

Source:	Convida Wireless LLC

Title:	Data storage solution

Spec:	3GPP TR 23.700-34 v.0.3.0

Agenda item:	9.11

Document for:	Approval

Contact:	Catalina Mladin, mladin.catalina@convidawireless.com

1. Introduction

This pCR provides a Solution for Key Issue #5 on data storage service in SEALDD.

2. Reason for Change

Address Key Issue #5.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-34.

* * * First Change * * * *

## 6.X	Solution #X: Data storage creation

### 6.X.2	Solution description

#### 6.X.2.1	General

The following solution corresponds to the key issue #5 on SEALDD enabled data storage.

#### 6.X.2.2	Storage service creation request procedure

Figure 6.X.2.2-1: Storage service creation request

- The VAL client/server determines to use SEALDD storage service, which could store/host data on behalf of the VAL client/server. The VAL client/server makes a storage service creation request to the SEALDD server. If the request is initiated by the VAL client, the request is first sent to the SEALDD client hosted on the same UE and then forwarded to the SEALDD server. The request includes the data to be stored and information associated with the data, such as access control policy, expiration time of the storage, etc. The VAL client/server may also specify in the request if/what management or status information of the data storage is required (e.g., information about how often the stored data is accessed).

Editor’s Note: How to use the Access Control information is FFS

2.  The SEALDD server processes the storage service request. If the request is accepted, the SEALDD server configures the storage service based on the request and stores the data at the storage server. If status information of the stored data is requested, the SEALDD server will start to track the accesses to the data for the data access status.

3.	The SEALDD server sends a response to the requesting VAL client/server. The response indicates if the request is accepted and the identifier of the stored data (if applicable). Upon receiving the response, the requesting VAL client/server may create a record for the stored data.

#### 6.X.2.2	Storage management procedure

Pre-conditions:

- The SEALDD service is configured to track and maintain data storage access information (i.e. status information)

- A storage service creation request procedure from a VAL client/server to the SEALDD storage server has been performed. The request includes a subscription to data storage access information (i.e. status information)

Figure 6.X.2.2-1: Storage management procedure

1.	Based on the configured subscription for data storage status information, the SEALDD server may send a notification to the requester with the collected information.

2.	Based on the received stored data status information, the requesting VAL client/server determines to perform a management operation, such as to update, refresh, or delete the stored data. The VAL client/server sends a request to the SEALDD server to perform the determined management operation.

3.	The SEALDD server processes the management request. If the request is accepted, the SEALDD server performs the required management operation on the stored data.

4.	The SEALDD server sends a response to the requesting VAL client/server with the result of the management operation, which may include updated information of the stored data.

#### 6.x.2.2	Information Flows

Editor’s note: Information flows for this solution are FFS.

### 6.x.3	Evaluation

Editor's Note: The evaluation of this solution is FFS.