## Slide 1: Comparison of solutions for Common EAS Selection
Basavaraj (Basu) Pattan,
Samsung

## Slide 2: Outline
Comparison of following Proposals
  Convida Proposal (S6-220547 and S6-220548)
  InterDigital Proposal (S6-220542)
  Apple Proposal (S6-220623)
  Ericsson Proposal (S6-220629)
  Huawei Proposal (S6-220721)
  Samsung Proposal (S6-220737)
Disclaimer:
The comparison of proposals is to the best of my interpretations and knowledge.
The comparison is not technical evaluation of solutions but only conceptual comparison to determine potential merger among proposed solutions.
Potential enhancements to the solutions (likely to be in future revisions) are not considered as they are still under discussion.

## Slide 3: Comparison of Proposals
 | Convida | InterDigital | Apple | Ericsson | Huawei | Samsung
Scope | Same/Different ACs on Different UEs connected to Same EES and Same EDN | Same/Different AC on Different UEs connected to Different EES and Different EDN | Same AC on Different UEs connected to Same selected EES and Same EDN | Same/Different AC on Different UEs connected to Different EES and Different EDN | Same AC on Different UEs connected to Same selected EES and Same EDN | Same/Different AC on Different UEs connected to Different EES and Same EDN
Common EAS Users Grouping | Pre-decided | Dynamic | Pre-decided at Cloud entity | Pre-decided | Pre-decided Group at Centralized Server | Dynamic
Location sharing between UEs | No | No | Yes | No | Yes | No
Common EAS Indication | “AC association information” Preconfigured in EEC context | Unique EAS instance (EAS endpoint + EES ID) in AC profile | Group ID + Location of each UE | Group info. + EAS info + EDN id | Group ID + location information of each UE or required service area | Pre-configured Grouping info - Multi-User/Multi-Session in AC Profile and EAS Profile
Need for Common EAS awareness | Each UE shares with EES via EEC Registration, EAS Discovery | Shared to ECS via Service Provisioning and EES via EAS Discovery | Shared to ECS via Service Provisioning and to selected EES via EAS Discovery | UE shares to EES via new request “EAS selection declaration” | Shared to ECS via Service Provisioning | Shared to EES via Registration and EAS Discovery
Who decides need for common EAS? | ASP/User | User/Application layer | Cloud entity | ASP | ASP | ASP/User
Common EAS determined by? | EES | EEC | ECS selects EES and EES selects common EAS | Binding Server | ECS selects EES and EES selects common EAS | EEC selects common EAS
Dissemination of selected Common EAS | NA | AC to AC | EES to EEC | Binding Server to EES and EEC | EES to EEC | EES to other EES to EEC
Architectural impact | No | No | Yes (Cloud Entity) | Yes (Binding Server) | Yes (Centralized Server) | No

## Slide 4: Backup

## Slide 5: Comparison of Proposals and Recommendation
Recommendation: Apple and Huawei solutions can be potentially merged. Convida and Samsung solutions are close.
 | Convida | InterDigital | Apple | Ericsson | Huawei | Samsung
Scope | Same or Different ACs on Different UEs connected to Same EES and Same EDN | Same or different AC on Different UEs connected to Different EES and Different EDN | Same AC on Different UEs connected to Same selected EES and Same EDN | Same or different AC on Different UEs connected to Different EES and Different EDN | Same AC on Different UEs connected to Same selected EES and Same EDN | Same/Different AC on Different UEs connected to Different EES and Same EDN
Common EAS Users Grouping | Decided before registration/ EAS discovery or dynamic (group /user ID are examples) | Dynamic | Pre-decided at Cloud entity | Pre-decided or dynamic (group id is just one example) | Pre-decided Group at Centralized Server | Dynamic
Location sharing between UEs | No | No | Yes | No | Yes | No
Common EAS Indication | “AC association information” provided at registration ,EAS discovery | Unique EAS instance (EAS endpoint + EES ID) in AC profile | Group ID + Location of each UE | Group Info (e.g. group id) + EAS info + EDN id | Group ID + location information of each UE | Pre-configured Grouping info - Multi-User/Multi-Session in AC Profile and EAS Profile
Need for Common EAS awareness | Each UE shares “AC association information” with EES via EEC Registration, EAS Discovery | “EAS selection information” used as a filter for Service Provisioning with ECS and EAS Discovery with EES | Shared to ECS via Service Provisioning and to selected EES via EAS Discovery | UE shares “Group ID” to EES via new request “EAS selection declaration” Or via existing “EAS discovery” | Shared to ECS via Service Provisioning | Shared to EES via Registration and EAS Discovery
Who decides need for common EAS? | ASP, User, Cloud entity | Users / Application layer | Cloud entity? | ASP | ASP? | ASP
Common EAS determined by? | EES | First user (EEC) | ECS selects EES and EES selects common EAS | Binding Server | ECS selects EES and EES selects common EAS | EEC selects common EAS
Dissemination of selected Common EAS | EES to EEC, between EESs via ACR | Application layer (e.g. AC to AC, via cloud, via SMS, etc.) | EES to EEC | Binding Server to EES and EEC | EES to EEC | EES to other EES to EEC
Architectural impact | No | No | Yes (Cloud Entity) | Yes (Binding Server) | Yes (Centralized Server) | No
Updates with company inputs

## Slide 6: Thank you!