3GPP TSG-SA WG6 Meeting #48-e	S6-220872_Rev1

e-meeting, 5th – 14th April 2022	(revision of S6-220740)

Source:	Samsung

Title:	Pseudo-CR on update to solution#3

Spec:	3GPP TR 23.700-96 V0.4.0

Agenda item:	9.7

Document for:	Approval

Contact:	Basavaraj (Basu) Pattan, basavarajjp@samusung.com

1. Introduction

This pCR brings updates to architecture solution #3.

2. Reason for Change

Proposed updates inline as per the discussions in S6-220739, on SA6 conf call held on March 10th, 2022:

- Fused Location Function still keeps the functionality of fusing location information from multiple sources

- SEAL LM retains the management aspects including location reporting

- Any additional Common service capabilities (geofencing, location analytics, heatmap) could be considered as enhancements to SEAL LM or 5GFLS on a case-by-case avoiding duplication with SEAL

- Fused Location Function resides outside SEAL LMS.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-96 V0.4.0.

* * * First Change * * * *

## 7.3	Solution #3: Functional architecture for fused location service leveraging SEAL location management

### 7.3.1	Solution description

This solution leverages SEAL to address key issue #1: Architecture enhancement of application enablement for location.

#### 7.3.1.1	Functional architecture

The figure 7.3.1.1-1 identifies the architecture of fused location service enabled by 5GS leveraging SEAL.

Figure 7.3.1.1-1:	 Functional architecture of fused location service leveraging SEAL location management

In the architecture, the SEAL Location management server interacts with the Fused location function for fusion of different location technologies.

The architecture supports multiple sources of location information including:

-	Location of AMF service exposed by NEF (as defined in 3GPP TS 23.502 [12]);

-	LCS location retrieved from either NEF or GMLC (as defined in 3GPP TS 23.273 [4]);

-	SUPL location retrieved from SLP (as defined in OMA AD SUPL [10]);

-	Location retrieved from 3rd party location server or location management client.

#### 7.3.1.2	Functional components and reference points

The Fused location function provides location information of the target UE based on positioning or location data retrived from one or multiple location sources including:

-	the NEF (as defined in 3GPP TS 23.501 [5] and 3GPP TS 23.273 [4]) via N33 reference point;

-	the GMLC (as defined in 3GPP TS 23.273 [4]) via Le reference point;

-	the SLP (as defined in OMA AD SUPL [10]) of SUPL network; and

-	the 3rd party location server.

Fused location function provides normalized description of location data to the location service comsumer through the northbound API.

The 3rd Party Location Server provides the location of a certain location technology (typically the network-based positioning) e.g. Bluetooth or the 3rd Party Location Server provides the location information from another operators e.g. if the UE has multiple USIMs to connect to different operators.

The Location management client represents the client of the requestor/sender UE for location reporting as defined in 3GPP TS 23.434 [13].

The Fused location client represents the client of the sender UE for location reporting via the 3GPP defined access and non-3GPP defined access  over FLS-X1 interface.

The location management server is a functional entity that receives and stores user location information and provides user location information to the vertical application server as defined in 3GPP TS 23.434 [13]. The location management server acquires location information from one or more sources including:

-	the NEF (as defined in 3GPP TS 23.501 [5] and 3GPP TS 23.273 [4]) via N33 reference point;

the Fused location function; and

-	the location management client.

The VAL client and VAL server (vertical application layer entities) are as defined in 3GPP TS 23.434 [13].

The interfaces are described as followed:

LM-UU:	Reference point as defined in 3GPP TS 23.434 [13].

LM-S:		Reference point as defined in 3GPP TS 23.434 [13].

FLS-X2:	The reference point is used for location retrieval of the target UE from 3rd party location server. The FLS-X2 can be the LM-S interface.

N33:	Service-based interface as defined in 3GPP TS 23.501 [5].

Le:	Reference point as defined in OMA AD MLS [11].

FLS-S:	Reference point used for fused location retrieval from Fused location function either by VAL Server or by Location management server.

Editor's note:	Impacts of architectural changes to existing SEAL LM procedures in 3GPP TS 23.434 [13] are FFS.

Editor's note: The enhancements to location management client, LM-UU and LM-S providing fused location service are FFS.

#### 7.3.1.3	(Informative) Deployment models

In deployments where Fused Location Function resides outside of SEAL LM is shown by Figure 7.3.1.1-1. In another deployment the Fused Location Function can be collocated within SEAL LM. Such function model is as shown in Figure 7.3.1.3-1.

Figure 7.3.1.3-1:	 Functional architecture of fused location service collacted within SEAL location management

Editor Note: The current deployment model only support to get location information from 3GPP defined acess. How to get the location information from the non-3GPP defined access is FFS.

### 7.3.2	Solution evaluation

Editor's Note:	This clause provides an evaluation of the solution. The evaluation should include the descriptions of the impacts to existing architectures.

* * * End of Changes * * * *