3GPP TSG-SA WG6 Meeting #49-e	S6-221106

e-meeting, 16th – 25th May 2022	(revision of S6-22xxxx)

Source:	NTT DOCOMO

Title:	Clarification of the functional model

Spec:	3GPP TR 23.700-95 v1.2.0

Agenda item:	9.5

Document for:	Approval

Contact:	Yuji Suzuki (yuuji.suzuki.rm@nttdocomo.com)

1. Introduction

This contribution proposes to clarify the functional models for different API provider scenarios.

2. Reason for Change

The TR has specified that the authorization function obtains the resource owner consent and authorizes the API invoker to invoke service APIs. To clarify the role of the authorization function and the resource owner client in the CAPIF functional models, only necessary CAPIF entities are shown in the clause 6.2.1.2. Also, CAPIF-11/11e is introduced for interaction between the API invoker and the resource owner client.

Where the authorization function is located is covered in clause 6.2.1.3 as deployment models. In this clause, two deployment models (i.e., authorization function is in or outside the CCF) are illustrated for each of the two cases, namely the PLMN providing the service APIs and the 3rd party providing the service APIs. The deployment models are labeled as A-1, A-2, B-1, and B-2.

The case where the authorization function is in the 3rd party domain is out of scope, but this deployment model is also illustrated in Annex for reference.

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-95 v1.2.0.

* * * First Change * * * *

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 22.261: "Service requirements for the 5G system; Stage 1"

[3]	3GPP TS 23.222: "Common API Framework for 3GPP Northbound APIs"

[4]	3GPP TS 23.434: "Service Enabler Architecture Layer for Verticals (SEAL); Functional architecture and information flows"

[5]	3GPP TS 23.558: "Architecture for enabling Edge Applications"

[6]	3GPP TS 29.513: "Policy and Charging Control signalling flows and QoS parameter mapping"

[7]	3GPP TS 23.682: "Architecture enhancements to facilitate communications with packet data networks and applications"

[8]	3GPP TS 33.501: "Security architecture and procedures for 5G system"

[9]	IETF RFC 6749: "The OAuth 2.0 Authorization Framework"

[10]	IETF RFC 8693: "OAuth 2.0 Token Exchange"

[x]	3GPP TS 33.122: " Security aspects of Common API Framework (CAPIF) for 3GPP northbound APIs "

* * * Next Change * * * *

## 6.2	Solution #2: Functional model description for SNA

### 6.2.1	Solution description

#### 6.2.1.1	General

This solution addresses the key issues #1, #2 and #3 with regard to the functional model to support the UE- and AF-originated API invocation and to support obtaining and revoking resource owner consent from the resource owner client. As the resource owner client is a new entity for CAPIF, the functional model for the CAPIF should be updated including the resource owner client and authorization function.

#### 6.2.1.2	Functional model

##### 6.2.1.2.1	Functional model description for the CAPIF with SNA enhancements

Figure 6.2.1.2.1-1 shows the reference point based functional model for the CAPIF with enhancements to support SNA, where the service APIs are provided by the PLMN.

Figure 6.2.1.2.1-1: Functional model for the CAPIF authorization with SNA enhancements—PLMN providing service APIs

The resource owner client(s) are application clients used by end-users or subscribers of the API provider domain's service provider.

The authorization function exposes authorization APIs and provides functionalities for authorization, such as a token endpoint and an authorization endpoint. When the service APIs are provided by the PLMN, the authorization function may reside within the CAPIF core function. The resource owner client(s) interacts with the authorization function via CAPIF-8. The resource owner communicates with the authorization function to provide and revoke resource owner consent. The resource owner interactions are supported via a resource owner client, which is a client-side entity.

Editor's Note:	The consent provisioning via CAPIF-8 is FFS.

The API exposing function (e.g NEF) acts as a resource owner consent enforcement point as specified in 3GPP TS 33.501 [8] and interacts with the authorization function via CAPIF-9. The API exposing function can retrieve the resource owner consent parameters from.the authorization function.

The API invoker interacts with authorization function via CAPIF-10/CAPIF-10e.

The API invoker interacts with the resource owner client via CAPIF-11/CAPIF-11e.

NOTE:	Security aspects including specification of the authorisation procedures are to be decided in SA3.

##### 6.2.1.2.2	Functional model description for the CAPIF with SNA enhancements to support 3rd party API provider

Editor's Note:	 As for the CAPIF functional model with SNA enhancements to support 3rd party API provider, whether the authorization server may reside in the PLMN trust domain is FFS and needs coordination with SA3. If the authorization server may not reside in the PLMN trust domain, the present document does not support cases where the API provider is outside the PLMN trust domain.

NOTE:	The case where the API provider and the authorization function are located outside the PLMN trust domain is out of scope of the present document. A possible deployment model for this case is described in an informative Annex A for reference.

#### 6.2.1.3	Deployment models

NOTE:	The viability of each deployment model in this clause is assessed in collaboration with SA3.

6.2.1.3.1	Deployment model A-1 for PLMN providing the API provider

Figure 6.2.1.3.1-1 shows a deployment model A-1 for PLMN providing the API provider. In this deployment model, the authorization function resides in the CAPIF core function.

Figure 6.2.1.3.1-1: Deployment model A-1 for the CAPIF with SNA enhancements—PLMN providing service APIs

##### 6.2.1.3.2	Deployment model A-2 for PLMN providing the API provider

Figure 6.2.1.3.2-1 shows a deployment model A-2 for PLMN providing the API provider. In this deployment model, the authorization function resides outside the CAPIF core function and is regarded as an entity in the API provider domain.

Figure 6.2.1.3.2-1: Deployment model A-2 for the CAPIF with SNA enhancements—PLMN providing service APIs

* * * Next Change * * * *

# Annex A (informative):
Authorization function provided by 3rd party API provider

## A.1	Example of authorization function deployment

This specification assumes that the authorization function is provided as a part of the CAPIF core function, as stated in TS 33.122 [x]. In addition to these functional models illustrated in clause 6.2, the 3rd party API provider may implement its own authorization function in its trust domain. Although the authorization processes in the 3rd party domain is out of this document's scope, this clause describes a possible deployment model for reference. The deployment model is not limited to the one described in this clause.

Figure A.1-1 shows a possible functional model for the CAPIF with enhancements to support SNA, where the authorization function is provided by a 3rd party API provider in order to control access to protected resources residing within the 3rd party’s span of control. The gray-colored entities and the interfaces drawn with dash-dotted lines are out of 3GPP's scope.

Figure A.1-1: Functional model for the CAPIF with SNA enhancements—Authorization function provided by 3rd party API provider

# Annex B (informative):
Change history

| Change history |
| --- |
| Date | Meeting | TDoc | CR | Rev | Cat | Subject/Comment | New version |
| 2021-07 | SA6#44-e | S6-211548 |  |  |  | TR skeleton | 0.0.0 |
| 2021-07 | SA6#44-e |  |  |  |  | S6-211821, S6-211852, S6-211853, S6-211854, S6-211855, S6-211856 | 0.1.0 |
| 2021-09 | SA6#45-e |  |  |  |  | S6-211871, S6-212075, S6-212076, S6-212165 | 0.2.0 |
| 2021-10 | SA6#45-bis-e |  |  |  |  | S6-212242, S6-212475 | 0.3.0 |
| 2021-11 | SA6#46-e |  |  |  |  | S6-212809, S6-212810, S6-212811, S6-212812, S6-212826 | 0.4.0 |
| 2021-11 | SA#94-e | SP-211508 |  |  |  | Presentation for information at SA#94-e | 1.0.0 |
| 2022-02 | SA6#47-e |  |  |  |  | S6-220449, S6-220450, S6-220451, S6-220452, S6-220453 | 1.1.0 |
| 2022-04 | SA6#48-e |  |  |  |  | S6-220774, S6-220775, S6-220776, S6-220873, S6-220944, S6-220945, S6-220946, S6-220947 | 1.2.0 |