## Slide 1: Federation and Roaming: Use cases and solution options
Nishant Gupta
Qualcomm

## Slide 2: Outline
Use cases
Solution options
Comparison
Conclusion
Way forward proposal

## Slide 3: Use case 1: Generic ‘Edge service authorization’
Deployment
  User is a subscriber of ECSP1
  ECSP1 and ECSP2 are federation partners.
Scenario
  User requires an EAS that is not available via ECSP1; or
  User is at a location where only ECSP2 provides edge services.
Expectation
  User should be able to discover the applications (e.g., EAS2) available via ECSP2 at its current location
NOTE: ‘Edge service authorization(s)’ is agnostic to applications. It is analogous to an internet authorization, where the user simply purchases internet access, and not ‘internet access for application 1’
ECSP#1
ECSP#2
ECSP#2
EAS2
Federation agreement
ASP service agreement
UE
ECSP#1
Edge Service Authorization (s)
EAS1
ASP service agreement

## Slide 4: Use case 2: ASP is partner of only primary ECSP
Deployment details
  User is a subscriber of ECSP1
  ASP is partner of only ECSP1
  ECSP1 and ECSP2 are federation partners
Scenario
  User requires an EAS at a location where ECSP#1 does not provide services, but ECSP#2 does.
Expectation
  ECSP1 requests ECSP2 to instantiate the EAS required by the user
  ECSP1 redirects the user to ECS/EES of ECSP2
  EEC discovers the EAS available through ECSP2
ECSP#1
ECSP#2
ECSP#2
EAS1
Federation agreement
UE
ECSP#1
EAS1
ASP service agreement
Edge Service Authorization (s)

## Slide 5: Use case 3: ASP is partner of only partner ECSP
Deployment details
  User is a subscriber of ECSP1
  ASP is partner of only ECSP2 (e.g., Edge services in a Sports Stadium are provided only by ECSP2)
  ECSP1 and ECSP2 are federation partners
Scenario
  User visits the stadium to watch a game
  User receives an (offline/online) advertisement of AR based edge applications available in the stadium to enhance user’s experience
Expectation
  Given location of the user, ECSP1 redirects the user to ECS/EES of ECSP2 in the stadium
  EEC discovers applications available through ECSP2
  User uses the applications available via ECSP2.
ECSP#1
ECSP#2
ECSP#2
EAS
Federation agreement
ASP service agreement
UE
ECSP#1
Edge Service Authorization (s)

## Slide 6: Use case 4: ASP is partner of both ECSPs
Deployment details
  User is a subscriber of ECSP1
  ASP is partner of both ECSPs
  ECSP1 and ECSP2 are federation partners
Scenario
  User requires an EAS at a location where ECSP#1 does not provide services, but ECSP#2 does.
Expectation
  ECSP1 redirects the user to ECS/EES of ECSP2
  EEC discovers the EAS available through ECSP2
ECSP#1
ECSP#2
Web-App#2
UE
ECSP#2
ASP
Web-App#2
ASP Service Agreement
ASP Service Agreement
ECSP#1
Federation agreement
NOTE: ASP can redirect the UE to ECSP2, but ASP will require knowing that ECSP1 and ECSP2 are federation partners and ECSP2 can trust the UE.

## Slide 7: Use case 5: Browser based applications
Deployment
  User is a subscriber of ECSP1.
  ASP is partner of ECSP1 and ECSP2
  ECSP1 and ECSP2 are federation partners
  ASP does not have a dedicated AC
Scenario
  User is at a location where only ECSP2 provides edge services.
  User uses web browser to connect to the EAS, e.g., a streaming service like Netflix.
Expectation
  ECSP1 checks if the EAS is available via ECSP2 and redirects the UE to ECSP2 if the EAS is available via ECSP2.
ECSP#1
ECSP#2
Web-App#2
UE
ECSP#2
ASP
Web-App#2
Configuring AC/EEC
ASP Service Agreement
ASP Service Agreement
ECSP#1
Federation agreement
NOTE: ASP can not redirect the UE to ECSP2 as there is no dedicated AC on the UE

## Slide 8: Use case 6: Edge-unaware application clients
Deployment
  User is a subscriber of ECSP1.
  ASP is partner of ECSP1 and ECSP2
  ECSP1 and ECSP2 are federation partners
  ASP’s dedicated AC is not edge-aware (e.g., a legacy application)
Scenario
  User is at a location where only ECSP2 provides edge services.
Expectation
  ECSP1 checks if the EAS is available via ECSP2 and redirects the UE to ECSP2 if the application is available via ECSP2.
NOTE: ASP can not redirect the UE to ECSP2 as AC is not Edge-aware
ECSP#1
ECSP#2
EAS
UE
ECSP#2
ASP
EAS
Service agreement (Web-App#2)
Service agreement (Web-App#2)
ECSP#1
Federation agreement
Configuring AC/EEC

## Slide 9: Use case 7: No Cloud Application Servers
Deployment
  User is a subscriber of ECSP1.
  ASP is partner of ECSP1 and ECSP2
  ECSP1 and ECSP2 are federation partners
  ASP has only EASs and no Cloud Application Server (CAS)
Scenario
  User is at a location where only ECSP2 provides edge services.
Expectation
  ECSP1 checks if the EAS is available via ECSP2 and redirects the UE to ECSP2 if the application is available via ECSP2.
NOTE: ASP can not redirect the UE to ECSP2 as there is no CAS to provide edge information
ECSP#1
ECSP#2
EAS
UE
ECSP#2
ASP
EAS
ASP Service agreement
ASP service agreement
ECSP#1
Federation agreement
Configuring AC/EEC
Excerpt from TS 23.558 clause 6.3.6: “It is possible that the server functions of an application are available only as an EAS.”

## Slide 10: Use case 8: ACR within Federation and Roaming
Deployment
  User is a subscriber of ECSP1.
  ASP is partner of multiple ECSPs
  ECSPs are federation partners
Scenario
  T-EAS discovery is initiated by EEC or S-EES
Expectation
  Find a partner ECSP that has the required EAS as quickly as possible to avoid service continuity failure.

## Slide 11: Solution Options
Pre-configuring the ECS with relevant information (Out of scope of 3GPP)
OAM based ECS configuration (SA5’s scope)
A searchable repository (SA6’s scope)

## Slide 12: Comparison
# | OAM based ECS configuration | A searchable repository
 | ECSPs share EAS information with each partner ECSP individually at the time of EAS (de)instantiation – P2P model. | ECSPs share EAS information with the searchable repository as part of ECS registration – Hub and Spoke model.
2. | Sharing information based on EAS instantiation is inaccurate as it does not take EAS registration into account, which enables EAS’s discovery. (TS 23.558, clause 8.3.4.1 “The EAS Registration procedure allows an EAS to provide its information to an EES in order to enable its discovery.”) | Sharing of information is based on EAS registration – no conflict with Rel-17.
3. | Huge waste of resources if partner ECSPs do not require the information | Information is shared once to the edge repository – further distribution is on a need basis only (query based).
4. | Sharing information of all instantiated EASs exposes ECSPs business-sensitive information about all EAS deployments to all partners, who may never require this information. | Information is shared to partners only on a need basis
5. | Not clear how this model works when federation brokers are used. | Edge repository works with both direct (one-to-one) and broker-based federation.
6. | Some use cases from previous slides will not work unless information of all EASs is shared with partner ECSPs – which will require huge resources for distribution and maintenance. | All use cases will work with minimum resource consumption as information needs to be maintained at a central place, and not with individual ECSPs.

## Slide 13: Conclusion
Preconfiguring ECS is out of scope of 3GPP
  Capture as an option, but work on scenarios where pre-configuration is not available (e.g., OAM based configuration and edge repository)
OAM based configurations is in scope of SA5
  Has multiple challenges, see slide 11.
  Capture as an option, not as a mandatory mechanism. Initiate LS to SA5 to check feasibility.
  Work on scenarios where OAM based configurations are not available
Edge Repository is in scope of SA6
  Capture as an option for cases where pre-configuration and OAM based configuration are not available.

## Slide 14: Proposed way forward
All 3 approaches are valid for different business models and assumptions.
Incorporate all 3 approaches in the following order.
Step a: ECS determines that information of a federation partner needs to be provided.
Step b: ECS checks availability of any preconfigured or OEM configured information.
Step c: If required information is available, ECS provides it to the requestor (EEC/S-EES).
Step d: If not, ECS queries the repository and seeks relevant ECS information.
Step e: If available with repository, ECS provides the information to the requestor (EEC/S-EES); otherwise ECS sends a negative response back to the requestor.
See related contributions for more details.