## Slide 1: EAS bundles: open issues
Nishant Gupta
Qualcomm

## Slide 2: Outline
Deployment consideration
Open discussions
  Can a bundle be spread across EDNs?
  Do EAS profile need to indicate EAS bundle information?
  Do EASs of a bundle interact with each other?

## Slide 3: Deployment consideration
Availability zone
  “An Availability Zone is the lowest level of abstraction exposed to an Application Provider who wants to deploy an Application on Edge Cloud.” – OPG.02 Operator Platform Telco Edge Requirements
  Like “Geographical service area” defined in Rel-17.
  No standard size/shape – can be as large or as small as ECSP prefers.
One availability zone can comprise of one or more Edge Data Networks, providing same or different KPI capabilities throughout the availability zone.
Each Edge Data Network can comprise of one or more Edge Hosting Environments.
One or more Edge Enabler Servers may be located in an Edge Data Network.
EDN-A2
Availability Zone – A
EDN-A1
EDN-A3
EHE-A11
EHE-A12
EHE-A13
EHE-A21
EHE-A22
EHE-A31
~30ms latency
~40ms latency
~50ms latency

## Slide 4: Bundle deployment examples
EDN-A2
Availability Zone – A
EDN-A1
EDN-A3
EHE-A11
EHE-A12
EHE-A13
EHE-A21
EHE-A22
EHE-A31
EDN-A2
Availability Zone – A
EDN-A1
EDN-A3
EHE-A11
EHE-A12
EHE-A13
EHE-A21
EHE-A22
EHE-A31
EAS1 EAS2 EAS3
EAS1
EAS2 EAS3
EAS4
EAS4
EDN-A2
Availability Zone – A
EDN-A1
EDN-A3
EHE-A11
EHE-A12
EHE-A13
EHE-A21
EHE-A22
EHE-A31
EAS1 EAS2 EAS3 EAS4
~30ms latency
~40ms latency
~50ms latency
~30ms latency
~40ms latency
~50ms latency
~30ms latency
~40ms latency
~50ms latency
Example deployment 1
Example deployment 2
Example deployment 3
EAS | Latency tolerance
EAS1 | 35ms
EAS2 | 60ms
EAS3 | 60ms
EAS4 | 45ms
Considering a bundle of 4 EASs with the following latency tolerance:

## Slide 5: Can a bundle be spread across EDNs?
Yes! An EAS bundle can be spread across EDNs, as long as application’s KPI requirements are met.
EDN-A2
Availability Zone – City A
EDN-A1
EDN-A3
EHE-A11
EHE-A12
EHE-A13
EHE-A21
EHE-A22
EHE-A31
EAS1
EAS2 EAS3
EAS4
~30ms latency
~40ms latency
~50ms latency
EAS | Latency tolerance
EAS1 | 35ms
EAS2 | 60ms
EAS3 | 60ms
EAS4 | 45ms

## Slide 6: Does EAS profile need to indicate EAS bundle information?
ASPs need to indicate affinity requirements to ECSP for the EASs in the bundle.
EAS bundle information at the ECS/EES eases operations for coordinated EAS discovery and coordinated ACR -
  Discovery of one of the bundled EAS can provide information of all the EASs in the bundle.
  ACR for one of the bundled EAS can trigger ACR detection for all the EASs of the bundle.
  EAS bundle information at the EES/ECS is particularly useful for EAS initiated and EES initiated scenarios.
Conclusion: EAS bundle information needs to be included in the EAS profiles.
EDN-A2
Availability Zone – City A
EDN-A1
EDN-A3
EHE-A11
EHE-A12
EHE-A13
EHE-A21
EHE-A22
EHE-A31
EAS1 EAS2 EAS3 EAS4
~30ms latency
~40ms latency
~50ms latency

## Slide 7: Do EASs of a bundle interact with each other?
It depends on application’s requirements.
In below examples, EASs of a gaming application may require sync, while EASs of a streaming application may not; while both application would benefit from coordinated discovery and coordinated ACR.
Game Engine
Game Renderer
Chat server
Video component
Audio component
Subtext component
Gaming application
Streaming Application

## Slide 8
Thank you!