## Slide 1: Service Continuity support for ENS
06 Nov, 2023
Sapan Shah (Samsung)

## Slide 2: EEC/AC connecting to S-EES/S-EAS
1) Normal scenario
2) ENS via lead ECSP
Normal Scenario
  EEC requests EES to discover EAS, EES responds with one or more EASs.
  AC connects to EAS to receive service.
ENS via lead ECSP
  EEC requests EES to discover EAS, required EAS is not found with EES, so EES sends discovery request to the partner EES (it finds partner EES details from ECS – not shown in the picture for simplicity).
  Partner EES sends one or more EASs. Source EES sends the response to EEC.
  AC connects to the EAS to receive service.
Difference
  In ENS case, S-EAS is not directly connected to S-EES. It is connected via EES (of partner ECSP).

## Slide 3: ACR
1) Normal scenario
2) ENS via lead ECSP
T-EES can be anywhere – intra-EDN or inter-EDN.
ECS not shown for simplicity
T-EES can be anywhere – intra-EDN or inter-EDN.
ECS not shown for simplicity

## Slide 4: Interaction between S-EAS and S-EES
1) Normal scenario
2) ENS via lead ECSP
Multiple interactions between S-EAS and S-EES during ACR procedures over EDGE-3.
Need to define interaction between S-EAS to S-EES using EES (partner ECSP).

## Slide 5: Conclusion
To support service continuity for ENS via leading ECSP.
  Interactions between S-EAS (deployed in partner ECSP) and S-EES (in lead ECSP) need to be enabled via EES (of partner ECSP)

## Slide 6
Thanks