## Slide 1: Discussion on E2E KPI guarantee for XR application
Jian Zhang
Huawei, Hisilicon

## Slide 2: Outline
Background
Potential gaps for E2E KPI guarantee
Conclusion and proposal

## Slide 3: Background
RAN
UPF
enabler client
XR AS/EAS
XR client
5G CP
N33/N5
UE
Enabler server
DN/EDN
Overall E2E KPI composition over 5G network
data transmission
Application processing
Typically, the overall E2E processing of XR service consists of several parts, such as media transmission over 5G network, and application processing (e.g. media rendering).
In real-time XR service, E2E KPI guarantee (e.g. low latency) is critical to provide immersive experience for XR users, For example, regarding of the cloud AR gaming scenario, the E2E latency should be less than 100ms.

## Slide 4: Potential gaps for E2E KPI guarantee
In Rel-17 and Rel-18, the EAS instatiation mechanism has been studied and specified in EDGEAPP topic of 3GPP TS 23.558, the EES may trigger the ECSP management to instatiate EAS, as described:
    The EES may trigger the ECSP management system (which is specified in TS 28.538 [22]) to instantiate the EAS serving the AC in the EDN corresponding to the EAS that can be instantiable before returning the EAS information to the EEC.
Potential gap#1: There is no detailed information about what the size of the computing resource to the management system should be provided by EES. For the real-time XR applications with E2E KPI requirements, with the appropriate EAS (i.e. XR application server) with the required size of computing resource is critical to impact the processing latency of the application (e.g. media rendering).
EEC
ECS
ECSP management system
EES
1. Service provisioning procedure
2. EAS discovery request
3. EAS instatiation determination
4. EAS instatiation request (if required)
5. EAS discovery response
EAS instantiation procedure triggered by EAS discovery request in clause 8.12.1 of TS 23.558

## Slide 5: Potential gaps for E2E KPI guarantee
Setting up an AF session with required QoS procedure in clause 4.15.6.6 of TS 23.502
In 5G network, the AF can request the required QoS by utilizing the AF session with required QoS procedure in clause 4.15.6.6 of TS 23.502.
  In step 1, “The AF sends a request to reserve resources for an AF session using Nnef_AFsessionWithQoS_Create request message (UE address, AF Identifier, Flow description information or External Application Identifier, QoS Reference or individual QoS parameters, Alternative Service Requirements (as described in clause 6.1.3.22 of TS 23.503 [20]), DNN, S-NSSAI) to the NEF.”
Potential gap#2: This procedure focuses on the transmission quality of the 5G network. However, even with lower transmission latency provided by 5G network, if XR application server cannot provide the appropriate lower application processing latency, the E2E KPI application requirements of XR application still cannot be satisfied.

## Slide 6: Conclusion and Proposal
As the enablement layer, it can be the bridge between the 5G network and application server to determine how the E2E KPI application requirements of XR application can be achieved. The following open issues are identified:
  How to support the E2E KPI guarantee to meet real-time XR service requirements, e.g. considering the potential enhancements to EDGEAPP in XR application server discovery or instantiation.
  What information is useful to interact between 5G network and enablement layer to guarantee the real-time XR service requirements.
The related introduced key issue S6-240262 is requested to be approved, to discuss more possible solutions to achieve E2E KPI guarantee, which is critical for XR application experience.
Notes: Mapping关系slide6对应CR被agreed