## Slide 1: Device disable – Issues with coupling 3GPP MC & OMA
UK Home Office, Samsung, BDBOS

## Slide 2: Additional complexity
The proposed OMA DM coupling with 3GPP MC introduces additional nodes and reference points to the functional architecture.
  These will increase the complexity of the service architecture and the amount of coding needed to implement the related protocols.
The complexities will transcend to MC device conformance testing also.
  With OMA DM 2.0 coupled to the functional architecture, the conformance test specifications will have to cover both 3GPP and OMA standard compliance.
  This will increase the cost and time taken for conformance testing, eventually pushing up the device costs for the user organisations.

## Slide 3: Device procurement constraints on a UO
In many user organisations – UO’s (eg: ESN, BDBOS) emergency service providers (individual police forces etc.) will procure their own MC devices which meet a baseline MC criterion.
  The varying requirements and budget at disposal will impact these choices. For example, a police force covering a large rural area will have different range and battery life requirements to those of the Met police in London.
  The UO’s need to be able to allow this device choice to individual forces. When devices also must support OMA DM 2.0, this choice is severely curtailed.
OMA DM 2.0 is not supported by Apple iOS and Linux operating systems.
  In some MC systems (eg: FirstNet), a significant proportion of devices run on Apple iOS. So, this device disable solution cannot reach such markets.

## Slide 4: Operational difficulties
A solution operated outside MC system (like OMA DM) is not directly accessible to operational supervisors/ team leaders on the ground, who may need to disable a device immediately upon request.
  They will need to contact the control room or the admin portal to request disabling through MDM/EMM. This does not meet the ‘immediate’ disable requirement.
In some MC systems, the EMM/MDM solutions will not be 24/7 available with immediate access.
  The control rooms/authorized users will have to reach out to system admins to enact disable/re-enable through EMM/MDM.
  In some MC systems the system admin role is not a 24/7 role.