## Slide 1: MC gateway enhancement discussion
Cuili Ge –gecuili@huawei.com
Huawei, Hisilicon

## Slide 2: Outline
Current MC gateway summary
Some issues
Potential enhancements

## Slide 3: Current MC gateway summary
Figure 11.2.1-1: Functional model of MC gateway UE application plane with MC client hosted in the non- 3GPP device
Figure 11.2.1-3: Functional model of MC gateway UE application plane with MC client hosted in the MC gateway UE
GW-local support
MBMS related signalling exchange
Location management related signalling exchange

## Slide 4: Current MC gateway summary
Whole flows using MC gateway UE, take the MC clients are hosted in the non-3GPP device as an example
CSC server
MC想 client
MC gateway UE
MC service server
Non-3GPP device
non-3GPP access connection
3GPP network
Register to network, setup PDU session
1. Identify authentication
2. Service authorization
3. Interact with CMS, GMS to get the profiles.
4. Affiliation, group call, private call and so on
5. Media plane data exchange
CSC client
>>>> The MC gateway UE are worked as a transparent router.

## Slide 5: Some Issues - 1
CSC server
MC service client
MC service server
3GPP network
2. Service authorization
3. Interact with CMS, GMS to get the profiles.
4. Affiliation, group call, private call and so on
5. Media plane data exchange
Non 3GPP device
MC gateway UE
CSC client
1. Identify authentication
(1) Any traffic regardless it is MCX related or not can goes through the MC gateway UE as the MC gateway UE is not aware of the traffic.
(2) The Uu resource is limited. If any traffic can go through the MC gateway UE, the Uu resource may be wasted.
(3) If the MC service user switch to another MC gateway UE, the whole flows has to be performed from the beginning.
>>>> Are we going to solve those issues?

## Slide 6: Some Issues - 2
[R-5.15-006] An MCX User shall be able to access multiple gateway MCX UEs simultaneously from a single device while restricting a MCX Service to one gateway (e.g., MCPTT on gateway UE 1, MCData and MCVideo on gateway UE 2).
>>>> Are we going to support this requirements?

## Slide 7: Potential enhancements
Enhance the MC gateway UE to control only the MCX and authorized traffic can be forwarded.
Optimize the experience during the switching of MC gateway UE.
Design procedures to support [R-5.15-006].