## Slide 1: Device disable – Proposals for way forward in Rel. 20
UK Home Office, BDBOS, Samsung

## Slide 2: Limit the scope to temp. device disable
Some comments in the last meeting about including the MC user disable also (as per SA1 requirements).
  SA1 requirements are quite detailed, also differentiates between temporary and permanent disablement and having ‘limited’ MC service availability.
  It will be difficult to address all these requirements in one release for SA6.
MC user disabling is a simpler process and cannot be coupled with MC device disable.
  MC user ID is already defined and it is easier to block access from this ID to the MC system.
  In MC device disable, the MC user shall be able to continue the task by logging onto another MC device. So, MC user disable has different use cases.
Clear use cases and requirements for temporary device disable for MC services were presented by UKHO in the first few SA6 meetings of Release 20.
  SA6 can focus to prioritize solutions for this aspect in Rel. 20 and tackle other aspects in later releases.

## Slide 3: Disabling all MC services - first, viable step
Some comments on addressing ‘limited service availability as per user org. policy’.
Two user organisations (UKHO, BDBOS) have indicated their preference to temporarily disable ALL MC services.
  This still leaves the possibility to track and communicate with the device using the non-MC, public telephony features of the device.
Limited service provision may be more complicated due to the interactions of such services in the functional architecture.
  For example, some MC Location features will need GMS to be also active. Ambient listening cannot simply be isolated from the other PTT features in the MCPTT server.
Can we treat disabling ALL MC services as the baseline solution for Release 20?
  If limited service requirements come from other user organisations, they can be addressed as enhancements in Release 21 onwards.

## Slide 4: Agree on a unique device ID first?
There is a general consensus that a device ID is a ‘missing piece’ in SA6 specs.
  Such an ID is useful not just in device disable, but also for Location, Ambient Listening, Discreet Monitoring etc., when multiple devices are used by a single MC user.
Both Samsung and Airbus proposals will need a unique device ID, to disable and re-enable the correct device.
  The device ID shall be unique and globally routable (considering partner MC systems also).
  The device ID associations shall be continually updated (with the current MC user, enable/disable state etc.) in a suitable database in the MC system.
We think there is sufficient understanding on this device ID now in SA6. We’d propose it to be specified first and to be included in TS 23.280 clause 8.

## Slide 5: Urgent consultation with SA3
UKHO believes the discussions with SA3 should begin very soon to establish the aspects such as listed below.
Security aspects when the device is in the temporarily disabled state.
  The device shall be ‘logged off’ from MC services but still shall be responsive to a re-enable request if this comes from the MC system.
  Even if the device is found, the current user or another MC user shall not be able to log-in, until the device is properly re-enabled.
How to remotely re-enable the device to allow it back again to the MC service(s).
  This process shall be developed with SA3 inputs, to ensure the security and resilience levels expected in MC systems.