## Slide 1: Discussion Paper: Location information in MC Service Call Setup Signalling Stage 1/ Stage 2 Alignment across MCData, MCPTT and MC Video (Rel20)
Andreas Platzer, Ute Becker
BDBOS

## Slide 2: Requirements (TS 22.280 Location)
Requirements
  [R-6.12-001] The MCX Service shall provide Location information of the transmitting MCX UE to receiving MCX UEs subject to privacy restrictions.
  [R-6.12-002] The MCX Service shall support conveyance of Location information provided by 3GPP location.
    MCX common requirement
    Not restricted to emergency use cases
    Describes availability of location information during call establishment

## Slide 3: MCData
Request Type | Direction | Location | Chapter
standalone data request | client – server |  | 7.4.2.1.1
 | server – client |  | 7.4.2.1.1
standalone session data request | client – server |  | 7.4.2.1.3
 | server – client |  | 7.4.2.1.3
session data request | client – server |  | 7.4.2.1.5
 | server – client |  | 7.4.2.1.5
group standalone data request | client – server |  | 7.4.2.1.7
 | server – client |  | 7.4.2.1.8
group session standalone data request | client – server |  | 7.4.2.1.10
 | server – client |  | 7.4.2.1.11
group data request | client – server |  | 7.4.2.1.13
 | server – client |  | 7.4.2.1.14
ad hoc group data session request | client – server |  | 7.17.2.1
 | server – client |  | 7.17.2.4
Almost complete
 only one gap remaining:
„ad hoc group data session request“

## Slide 4: MCPTT
Request Type | Direction | Location | Chapter
group call request | client – server |  | 10.6.2.2.7
 | server – client |  | 10.6.2.2.9
group-broadcast group call request | client – server |  | 10.6.2.2.26
 | server – client |  | 10.6.2.2.27
emergency group call request | client – server |  | 10.6.2.2.1
 | server – client |  | 
imminent peril group call request | client – server |  | 10.6.2.2.5
 | server – client |  | 
ad hoc group call request (include emergency) | client – server |  | 10.19.2.1
 | server – client |  | 10.19.2.5
private call request | client – server |  | 10.7.2.1.1
 | server – client |  | 10.7.2.1.2a
emergency private call request | client – server |  | 10.7.2.1.5
 | server – client |  | 10.7.2.1.5a
Currently not fully aligned across all call types

## Slide 5: MCVideo
Request Type | Direction | Location | Chapter
group call request | client – server |  | 7.1.2.2.1
 | server – client |  | 7.1.2.2.2
emergency group call request | client – server |  | 7.1.2.2.18
 | server – client |  | 7.1.2.2.18
imminent peril group call request | client – server |  | 7.1.2.2.22
 | server – client |  | 7.1.2.2.22
private call request | client – server |  | 7.2.2.2.1
 | server – client |  | 7.2.2.2.2
emergency private call request | client – server |  | 7.2.2.2.6
 | server – client |  | 7.2.2.2.7
Currently limited to group call procedures

## Slide 6: Summary
MC Service | Alignment Status
Requirements | 🟩Common requirement for all MC Services
MCData | 🟩Nearly complete; a template for other services
MCPTT | 🟨Almost complete, but full consistency across call types still to be achieved
MCVideo | 🟥Location handling needs extension beyond group call