## Slide 1: Discussion Paper: Hidden User Support
Adinarayana K Setty (Motorola Solutions), Anatoli Levine (Softil)

## Slide 2: Requirement
End User Requirement :
  Some organizations do not want certain users to be seen by other users.
  Those users are not seen when they are present on the network or affiliated to a Group, however they can listen to the Group, and they will receive SDS messages sent to the Group.
  If they do choose to press PTT or send an SDS message to the Group, their User or device information is not displayed to other users.
Feature requirement :
  “Hide a sensitive user's presence and affiliation from other users”
Notes: Deleting the editor´s note in clauses 10.19.2.3 Ad hoc group call request (MCPTT server – group host MCPTT server) and 10.19.2.6 Ad hoc group call response (MCPTT server – MCPTT server):
Editor's Note: It is FFS if the server to server message is needed in a call request or response message.

## Slide 3: Considerations
User Authentication :
  Hidden user will be a MC user, expected follow TS 33.180 Clause 5.1.2 for a MC User authentication.
User Service Authorization :
  MC service client expected to follow TS 33.180 Clause 5.1.3 for MCX user service authorisation.
Hidden user configuration :
  Proposed to have new data attribute in MC Service User profile (as per TS 23.280 Clause 10.1.4) to indicate MC user wishes to remain hidden.

## Slide 4: Considerations
Hiding MC user details as part of MC User Registration or MC User Service setting
  MC User wanting to hide user identities can also communicate in MC User REGISTER or MC User service setting procedures.
Hidden User MC service consideration
  When hidden user joins the MCPTT group call, notification should not be sent to other MC Users.
  When hidden user grabs floor starts speaking, hidden user MC Service ID , Alias details needs to be hidden.
  When hidden user initiates MCPTT group call, hidden user details should not be sent in notification, signaling , media messages.
  Proposal is to send MCPTT Group URI to other MC Users when Hidden user starts voice communication.
  When hidden user sends messages to MCData Group, hidden user MC service ID is hidden from other users.

## Slide 5: Other considerations
Hidden user group configuration
  Proposal is to have list of MC service groups configured for hidden user.
  This will be list of groups for which hidden user is authorized to perform MC service communication.
Group Affiliation
  On learning hidden user details as part of configurations, proposal is for MC Service client to perform Implicit affiliation to authorized groups.
  Proposal is to allow Explicit affiliation to groups from Hidden user MC Service client; This is to accommodate dynamic addition of groups to authorized group list.
Group Regroup operations
  Hidden user is expected to be involved in Group-regroup , Temporary Group operations , Adhoc Group.

## Slide 6: Scope
With in scope
  MC service group communication.
Out of scope
  MC Service private communication.
Topics for further Study
  Encryption and secured MC service communication.
  Migration.
  Interoperability.