## Slide 1: N6 measurement exposure considerations
Walter Featherstone
Apple

## Slide 2: Outline
Background
  SA6/SA2 LS exchange
EAS Profile
  EAS Service KPIs
  DNAIs associated with EAS instance
Highlight potential opportunities to leverage N6 delay
  Session with QoS
  EAS Discovery
Proposed response to SA2

## Slide 3: Background (LS exchange)
In S6-253741/S2-2508200 (sent at SA6#68), SA6 requested exposure of N6 measurements (PSA UPF to Edge Application Server)
In the SA2 LS (S2-2509811/S6-255010)
  “SA2 kindly asks SA6 to provide further details, e.g., scenarios, for N6 delay measurement exposure.”
They also indicate that:
  “SA2 has defined N6 delay measurement for Local UPF (re)selection to be performed only by SMF”.
    I.e., only the core network selects the DNAI (PCF/SMF/UPF)
  “SA2 has concern on potential network topology information exposure in case where UPF related information is paired with N6 delay measurement information exposure.”

## Slide 4: EAS Profile and its DNAI(s), TS 23.558
8.2.4 EAS Profile
  NOTE 1: Information elements in the EAS Profile are provided by the ASP.
    Implies IEs in EAS Profile are relatively static and do not provide runtime / real time performance information
  An EAS Profile includes information about an EAS used to describe services and service characteristics offered.
  List of EAS DNAI(s) (O): DNAI(s) associated with the EAS.
    This IE is used as Potential Locations of Applications in clause 5.6.7 of 3GPP TS 23.501.
    It is a subset of the DNAI(s) associated with the EDN where the EAS resides.
An EAS profile may include more than one DNAI, i.e., the EAS is reachable via different paths each potentially offering different performance KPIs
An EAS profile is specific to an Edge Data Network (EDN)
An EAS profile is EAS instance specific (ID and Endpoint are mandatory)
  It could be a logical service endpoint, but multiple DNAIs could still be associated with it

## Slide 5: EAS Profile and its Service KPIs, TS 23.558
8.2.4 EAS Profile
  EAS Service KPIs (O): Service characteristics provided by EAS, detailed in Table 8.2.5-1
Table 8.2.5-1: EAS Service KPIs
  Information Element (O): Maximum Response time (NOTE)
  Description: The maximum response time advertised for the AC's service requests.
  NOTE: The maximum response time includes the round-trip time of the request and response packet for communication between the AC and EAS, the processing time at the server and the time required by the server to consume 3GPP Core Network capabilities, if any.
Only a single set of EAS Service KPIs are provided, even though multiple DNAIs may be provided in the EAS Profile
Response time E2E between AC & EAS and therefore includes N6 component of the delay

## Slide 6: Session with QoS, TS 23.502 & TS 23.503
23.502, 5.2.6.9.2 Nnef_AFsessionWithQoS_Create service operation
  Description: The consumer requests the network to provide a specific QoS for an AF session for a UE or a list of UEs.
23.502, 5.2.6.33.2 Nnef_AF_request_for_QoS_Create service operation
  Description: The consumer requests the network to provide a specific QoS for a traffic flow for a UE or a group of UEs.
Inputs, Optional: … RT Latency Indication as described in clause 6.1.3.22 of TS 23.503
23.502, 6.1.3.22 AF session with required QoS
  The AF may request that a data session to a UE is set up with a specific QoS (e.g. low latency or PDV) and priority handling. The AF can request the network to provide QoS for the AF session based on the service requirements with the help of a QoS Reference parameter that refers to pre-defined QoS information. Instead of the QoS Reference, the AF may provide individual QoS parameters associated to the Flow Description.
23.502, 6.1.3.27.2 UL/DL policy control based on round-trip latency requirement
  The AF may provide a round-trip (RT) latency indication together with a single direction delay requirement between the UE and the PSA UPF expressed as the QoS Reference or the individual QoS parameters (as described in clause 6.1.3.22). The RT latency indication indicates the need to meet the RT latency requirement of the service data flow, i.e. doubling of the single direction delay requirement between the UE and the PSA UPF.
When making Session with QoS requests towards the core network, enabler layer entities (e.g., EES) should subtract the N6 component of the overall EAS Service KPIs “Maximum Response time”

## Slide 7: EDGEAPP: EAS discovery (TS 23.558, 8.5)
EES processing of the request: “If the EEC indicates that service continuity support is required, when identifying the EAS, the EES shall take the indication which ACR scenarios are supported by the AC, the EEC, the EES and the EAS and which of these are preferred by the AC into consideration. The EES may select one EAS and determine whether to perform application traffic influence for this EAS in advance based on AC's service KPI or EAS’s service KPI in desired response time, when the EAS does not perform traffic influence in advance. If the EES determines to perform application traffic influence for this EAS in advance, then the EES will applies the AF traffic influence of the EAS in the 3GPP Core Network before sending EAS discovery response”
  AC’s service KPIs are E2E, implying N6 component of delay should be accounted for
The response: “If the EES perform traffic influence for EAS(s) in step 2, then the discovered EAS(s) is with optimized traffic route. Depending on the EAS discovery filters received in the EAS discovery request, the response may include additional information regarding matched capabilities, e.g. service permissions levels, KPIs, AC locations(s) that the EASs can support, ACR scenarios supported by the EAS, etc.”
  Note that in the response (see table 8.5.3.3-1), “Traffic influence performed indication” is present only when the “EAS selection request indicator” is provided in the EAS discovery request message
  The service KPIs that an EAS can support are E2E, implying N6 component of delay should be accounted for

## Slide 8: EDGEAPP: EAS discovery (TS 23.558, 8.5)
EES processing of the request: “when the UE in the overlapping area between the EDNs of common EAS and EAS registered to this EES (e.g. UE can connect either common EAS or EAS registered to this EES which is UE is in the common EAS service area), the EES identifies either common EAS or EAS registered to this EES for the UE based on the UE location, EAS discovery filters, application group profile, common EAS KPI as specified in table 8.2.5 and EDN information, registered EAS KPI as specified in table 8.2.5 and EDN information, and inter-EAS communication performance of these EASs and checks whether the common EAS or EAS registered to this EES can provide better E2E response time. ”
  Real time insight into the current latency could enable a more informed decision to be made regarding EAS selection
“NOTE 13: As long as a proper EAS (e.g. considering expected AC service KPIs included in EAS discovery request) is discovered and selected by the EES, EEC of a constraint UE can stop sending EAS discovery to rest candidate EES(s), and provide the selected EAS information to AC.
  Realtime insight into the current latency could ensure appropriate prioritization of the candidate EAS

## Slide 9: Topology exposure
Exposing N6 delay measurements per DNAI provides performance information, not explicit topology information
  The N6 delay between UPF and EAS is a metric, not a topology map
  It does not identify specific UPFs, including their IP address(es) or port numbers
  It uses abstract identifiers (DNAIs), which are opaque logical labels

## Slide 10: Summary
The 5GC has the capability to perform N6 measurements
  The measurement results are leveraged within the 5GC but not exposed even to the AF that provides the assistance information necessary to perform such measurements
  Availability of N6 measurements at the enabler layer could facilitate appropriate KPI related requests towards the 5GC and its own internal decision making, e.g.,
    AF Session with QoS in which the round-trip latency accounts only for the UE to PSA UPF portion of the AC to EAS communication path
    EAS discovery, including in support of Application Context Relocation procedures. Depending on the trigger (e.g., EEC/UE, EAS itself, Cloud Application Server (CAS), or another EES), if N6 delay measurement information were available to the EES it could assist in ranking or selecting candidate EAS Profiles to return in the discovery response.

## Slide 11: Proposal
Send reply LS to SA2 providing exemplary potential scenarios where N6 measurements could be leveraged (see S6-255122)
Make a request to SA2 in that LS to expose N6 measurement information results based on DNAI, but not exposing UPF specific information