## Slide 1: Discussion on the Way Forward for WA5
MediaTek Inc.
Contact: Yu-Jen Ku (Yu-Jen.Ku@mediatek.com)

## Slide 2: Outline
Background
Way forward proposals and justifications
Summary

## Slide 3: Background
In SA6#69, S6-254714 endorses the candidate 6G application enablement study work tasks for further discussion
For WA5 (Compute and Communication Aspects), the following work tasks are listed as candidates:
  WT5.1: Study potential enablement capabilities (complementing computing at the core network) to support managing application compute resources at the VAL UE and edge/cloud side
    NOTE: The progress of this WT may depend on SA2 efforts
  WT5.2: Void. Merged to 5.4
  WT5.3: Study of application enabler requirements in compute and communication aspects for the support of computing services
  WT5.4: How to enable computing service with co-ordination between CN and 3rd party
    NOTE: The progress of this WT needs to co-ordinate with SA2 WG
  WT5.5: How to enable joint consideration of the communication and computing requirements among UE/Edge/Cloud continuum
    Note: The progress of this WT needs to co-ordinate with SA2 WG
  WT5.6: Investigating the mechanisms of compute-intensive application model/paradigm (e.g., C-S, web application, serverless and so on), analyzing the potential requirements on enabler layer to utilize computing resource offered by MNO operator and the network layer computing mechanism provided by SA2.
  WT5.7: Study the need and challenges related to Compute Resource Discovery
  WT5.8: Study efficient usage of available resources for application enablement
  WT5.9: Study enabling new business case by providing compute as a service to applications and service providers
  WT5.10: Study of Compute Enablement framework to enable end devices (e.g., smartphones, connected vehicles, etc.) to become part compute infrastructure orchestrated by the 6G network.

## Slide 4: Proposal 1 [1/2]
Motivation: the study principle of WTs 5.4, 5.5, 5.6, 5.7, 5.8, 5.9 should consider both the compute and the communication aspects/reqs. of the 6G application enabler.
  Proposal: WTs 5.4, 5.5, 5.6, 5.7, 5.8, 5.9 can be the candidate objectives under the general WT5.3. WT5.1 can be merged with WT5.3.
In this new WT3 (See next slide)
  [old] WT5.4: becomes [new] WT5.3-1
  [old] WT5.5: becomes [new] WT5.3-2
  [old] WT5.6:
    the first part of WT5.6 is the same as the general description of WT5.3
    the second part of WT5.6: becomes [new] WT5.3-3
  [old] WT5.7: merged to [new] WT5.3-4
  [old] WT5.8: covered by [new] WT5.3-3
  [old] WT5.9: covered by [new] WT5.3-1

## Slide 5: Proposal 1 [2/2]
[NEW] WT5.3: Study of application enabler requirements in compute and communication aspects for the support of computing services
  WT5.3-1: How to enable computing service with co-ordination between CN and 3rd party
  WT5.3-2: How to enable joint consideration of the communication and computing requirements among UE/Edge/Cloud continuum
  WT5.3-3: Analyzing the potential requirements on enabler layer to utilize computing resource offered by MNO operator and the network layer computing mechanism provided by SA2
  WT5.3-4: Study the need and challenges related to discovering and determining availability of compute resources for providing computing services
  NOTE: the scope of this WT depends on SA2 progress
[old] WT5.4
[old] WT5.9
[old] WT5.5
[old] WT5.6 (2nd part)
[old] WT5.8
[old] WT5.7

## Slide 6: Justification
WT5.3-1 (previously the WT5.4): How to enable computing service with co-ordination between CN and 3rd party
  Concerns from NWM#2:
    SA6 should target at the computing resource owned by MNO but NOT controlled by CN
    Should wait the finalization of work aspects by SA2
  Justification:
    CN manages the communication resources and its own controlled computing resources.
    By coordinating with the 3rd party managed computing resources, the compute offloading can be achieved by the coupling of communication and computing resources (including CN and 3rd party controlled) management. Providing an opportunity of end-to-end performance optimization for computing services.
    A note is added to reflect the fact that scope of this WT depends on SA2 progress

## Slide 7: Justification
WT5.3-2 (previously the WT5.5): How to enable joint consideration of the communication and computing requirements among UE/Edge/Cloud continuum
  Concerns from NWM#2:
    Merge with WT5.3 or WT5.6
  Justification:
    Jointly considering the communication and computing requirements is required in 6G to achieve good performance of computing task offloading
      e.g., An efficient AI inference splitting between UE and Edge server requires end-to-end information, including UE/Edge computing and network communication information
      e.g., To ensure end-to-end delay performance of compute offloading, if the communication delay increases, the server can add more resources for the task to reduce the computing delay (see Appendix)

## Slide 8: Justification
WT5.3-3 (previously the 2nd part of WT5.6): Analyzing the potential requirements on enabler layer to utilize computing resource offered by MNO operator and the network layer computing mechanism provided by SA2
  Concerns from NWM#2:
    Covered by WT5.3 or WT5.6
  Justification:
    It is essential to analyze the requirements for the application enabler to utilize the various computing resources that are available. E.g., study on how the enabler request enough computing resources for offloading the service.
    The requirement may include both computing and communication aspects, for example, study on whether/how the application’s end-to-end delay requirement for compute offloading can impact the utilization of different computing resources

## Slide 9: Justification
WT5.3-4 (previously the WT5.7): Study the need and challenges related to discovering and determining availability of compute resources for providing computing services
  Concerns from NWM#2:
    The objective seems to be already addressed in 5GA. It is not clear what the new aspects are.
    Cloud solutions offer this, there is no need to overlay more on them
    It is a bit of solution-oriented description. The computing resource should be restricted to “non-CN controlled”.
  Justification:
    The computing resources now may include CN and 3rd party managed computing resources, it is essential to study on how to discover the candidate of computing resources
    This WT can study how the computing resource can be discovered by jointly considering the computing resource availability condition and the communication QoS condition between the UE and the compute resource host

## Slide 10: Proposal 2
2. WT5.10:
It can be studied further on how to enable end devices to provide computing services as part of the 6G network compute infrastructure. There are use cases in SA1 that the compute tasks from an end device are offloaded to another end device, such as UAV and CPE. Therefore, we support and propose the revised WT5.10 as:
  WT5.10: Study of Compute Enablement framework to enable end devices (e.g., UAVs, CPEs, etc.) to become part of compute infrastructure orchestrated by the 6G network

## Slide 11: Summary
  Proposal 1: Merging of WT5.1, 5.3, 5.4, 5.5, 5.6, 5.7, 5.8, 5.9 to the new WT5.3:
    WT5.3: Study of application enabler requirements in compute and communication aspects for the support of computing services
      WT5.3-1: How to enable computing service with co-ordination between CN and 3rd party
      WT5.3-2: How to enable joint consideration of the communication and computing requirements among UE/Edge/Cloud continuum
      WT5.3-3: Analyzing the potential requirements on enabler layer to utilize computing resource offered by MNO operator and the network layer computing mechanism provided by SA2
      WT5.3-4: Study the need and challenges related to discovering and determining availability of compute resources for providing computing services
      NOTE: the scope of this WT depends on SA2 progress
  Proposal 2: Revised WT5.10:
    WT5.10: Study of Compute Enablement framework to enable end devices (e.g., UAVs, CPEs, etc.) to become part of compute infrastructure orchestrated by the 6G network

## Slide 12: Appendix: Performance Evaluation on Joint Consideration of Computing and Communication Requirements
Disjoint delay management (legacy):
  A job is successful offloaded if both (1) and (2) are met
    (1) Communication Delay ≤ Communication Delay Budget
    (2) Compute Delay ≤ Compute Delay Budget
Joint delay management:
  A job is successful offloaded if
    Communication Delay + Compute Delay ≤ Total Delay Budget
System Model
Budget Design | Compute Capacity Scale
Joint | 8
Disjoint | 11
More efficient use of compute capacity
System Service Capacity KPI
System Service Capacity KPI
Gain via joint delay budget design
Budget Design | Service Capacity
Joint | 80
Disjoint | 55
45% Increase