## Slide 1: Discussion paper on IOPS system Network layer aspects
Ericsson
Rana.alhalaseh@ericsson.com

## Slide 2: Content
History of IOPS in 3GPP
Stage 1 requirements (TS 22.346)
IOPS LTE NW aspects
IOPS application layer aspects
Issues in IOPS EPS system
IOPS deployment vs network resilience

## Slide 3: IOPS history in 3GPP
Rel-13
Rel-17
Rel-19
SA1: FS_IOPS TR 22.897
SA2: FS_IOPS_St2 TR 23.797 LTE NW layer
SA3: FS_IOPS_Sec TR 33.897 LTE NW layer sec
SA1: IOPS TS 22.346
SA2: IOPS TS 23.401 info. Annex K LTE deployment guidance
SA3: IOPS TS 33.401 Annex F LTE security deployment guidance
No standardized Stage 2 APP layer solution
SA6: MCIOPS TS 23.180 APP layer solution over IOPS LTE system
SA6: FS_Generic_IOPS TR 23.700-09
SA6: Generic_IOPS TS 23.180 generalize the APP layer solution over 3GPP NW
Stage 1 stage 1 requirement
Stage 2 NW layer aspects
Stage 2 APP layer aspects
Rel-20
SA3: MCX20_SEC TS 33.180 CR0228 APP layer security aspects*
* Status: Untreated as per SA3#124

## Slide 4: TS 22.346 IOPS requirements
Isolated E-UTRAN: either an E-UTRAN without normal connectivity with the EPC or deployed NeNBs with E-UTRAN functionality.
Isolated E-UTRAN operation: Comprises two situations: 1) In the event of an interruption to normal backhaul connectivity Isolated E-UTRAN operation aims to adapt to the failure and maintain an acceptable level of network operation in the Isolated E-UTRAN. The restoration of service is the eventual goal. 2) Operation following the deployment of one or more Nomadic eNBs either without backhaul or with limited backhaul.
Limited backhaul capability: Isolated E-UTRAN operation supports operation where the Isolated E-UTRAN has no backhaul capability to the EPC. Furthermore Isolated E-UTRAN operation may have limited backhaul capability to the EPC. For the case of limited backhaul capability to the EPC only the signalling of public safety UEs can reliably be communicated to the EPC; in addition users may have the possibility to transmit a limited amount of user data with no guarantee of service.
Nomadic eNB (NeNB): An NeNB is a nomadic cell and may consist: base station, antennas, microwave backhaul and support for local services. The NeNB is intended for Public Safety use providing coverage or additional capacity where: 1) coverage was never present (e.g. forest fire or underground rescue) or 2) where, for example, due to natural disaster coverage is no longer present.

## Slide 5: TS 22.346 IOPS requirements

## Slide 6: IOPS in SA2 vs SA3 vs SA6
IOPS LTE system (or any IOPS 3GPP system) is under the control of SA2 (network aspect of IOPS 3GPP system)
SA6 defines an application layer solution, so that MC services can be utilized on top of SA2’s network solution
SA6’s present generic IOPS solution (in TS 23.180 Rel-19) is an application layer solution that is agnostic to the 3GPP IOPS system so that MC services can run on any 3GPP IOPS system
This does not imply that there is a generic IOPS 3GPP system (it is under the control of SA2 to define)
SA3 covers security aspects of the NW layer based on SA2 work, and covers security aspects of APP layer based on SA6 work
LS S6-255100 mixes up these fundamental concepts
SA6
SA2

## Slide 7: IOPS LTE NW aspects
FS_IOPS_St2 is based on proprietary deployment experience using 3GPP specs
IOPS_St2 results in an informative annex K in TS 23.401 that includes deployment guidance for LTE IOPS system
It considers no backhaul IOPS scenario and it is applicable to nomadic scenario
Signaling only backhaul and limited backhaul scenarios are left for implementation
The IOPS LTE system has its own IOPS-PLMN ID
IOPS enabled UE has IOPS-PLMN ID configured in USIM application
SA6
SA2

## Slide 8: IOPS LTE NW aspects
Figure K.2.4-1 of TS 23.401 illustrates switching between normal operation (via a macro EPC) and local IOPS EPS system
It covers nomadic scenario as well (except of steps 1, 2 and 3)

## Slide 9: IOPS application layer aspects
Generic_IOPS is to generalize the IOPS application layer solution
NW aspects of IOPS is under the control of SA2
Figure 7.3.3-1 MCPTT functional model for the application plane in the IOPS mode of operation (TS 23.180 v. 18.0.0)
Figure 7.3.3-1: MCPTT functional model for the application plane in the IOPS mode of operation (TS 23.180 v. 19.1.0)

## Slide 10: Issues in IOPS EPS system
Issue 1: Local HSS
  Duplicate of all MC user subscription information in a local HSS
    This is to ensure serving of max number of MC users as possible when the backhaul interruption occurs
  The local HSS is at (less secured) distributed sites
  Security credentials are provisioned in the local HSS prior to backhaul loss event
    Security credentials may be compromised at local (less secured) location
Notes: Security credentials are available at the USIM of the IOPS enabled MC UEs (not an issue)

## Slide 11: Issues in IOPS EPS system
Issue 2: Deployment cost
  The IOPS EPS system (including IOPS enabled eNB) needs to be deployed at larger number of sites
    To ensure providing local MC services for larger number of users once backhaul interruption occurs
  This results in higher costs of deployment
  PLMN operators have not yet embraced and shown commitment to the present solution

## Slide 12: Issues in IOPS EPS system
Isolated operation scenario
  There is standardized solution that is not implementable given the two issues
  Stage1 requirements (Rel-13) need to be revisited to increase the resilience of the NW to avoid resulting in an IOPS isolated deployment
  A lot of enhancements and features are included in the NW aspects for 5GS, which can be considered for NW resilience
Nomadic eNB/gNB scenario
  Low scale and controlled local distribution for disaster relief that may result in minimizing impact of the two issues
  Local nomadic gNB cell can be deployed without the need of including informative annex (neither in TS 23.501 nor in 33.501)
    A nomadic gNB cell can be deployed locally with the minimum number of NFs given existing procedures and security aspects

## Slide 13: IOPS vs NW resilience
Isolated operation scenario
  Several WIDs were submitted in SA2 over the past releases to duplicate IOPS EPS into a IOPS 5G system
  A SID in SA2 would be needed instead of WID to study the requirement given existing issues
  Otherwise, a WID results in a solution with the similar issues
  Via a WID, 3GPP specs would include NW aspects of a 5G IOPS system with no implementation
Network resilience
  The focus should be to increase the NW resilience to avoid resulting in a local isolated deployment
  Several NW enhancements and features are considered in 5GS
    Wireless Access Backhaul (WAB)
    Minimization of service interruption (MINT) feature via disaster roaming
    Various ProSe features including multihop* (beyond local MC services)
    NTN
    Standalone Non-Public Network (SNPN)
    Off-NW communication via direct communication and UE2UE relay
    On-NW communication via UE2NW relay

## Slide 14: Failure scenario vs 5GS features
Backhaul failure
  WAB
  Satellite backhaul
  ProSe features including multihop
  SNPN
RAN failure
  MINT feature via disaster roaming
  ProSe features including multihop
  NTN
  SNPN
  ATSSS via non-3GPP access (N3IWF/W-AGF)
    WAB: Wireless Access Backhaul
    MINT: Minimization of service interruption
    SNPN: Standalone Non-Public Network
    N3IWF: Non-3GPP InterWorking Function
    W-AGF: Wireline Access Gateway Function

## Slide 15: Conclusion and way forward
NW layer of a 5G IOPS system needs to be studied within a SID, to study stage 1 requirements given existing issues
Copy- paste of existing informative annex to be applicable to 5GS results in a standardized solution with same issues as in IOPS EPS system
If companies have proposals that have impact on SA2/SA3 specs related to NW layer, they need to bring them directly in the respective WG. SA6’s work related to the APP layer IOPS solution is concluded
Rel-13 SA1 requirements need to be revisited to focus on increasing the NW resilience to avoid resulting in an isolated deployment
Several enhancements and features are introduced as part of 5GS that can be beneficial to increase the NW resilience

## Slide 16: Thank You!