## Slide 1: Discussion paper on the quality of indirect path
Netherlands Police
Ericsson

## Slide 2: Content
Use cases and requirements
Proposed solution
  S6-255096
  S6-255097

## Slide 3: Enhancing indoor coverage for the fire brigade
Rel-17 SA1 study Enhanced Relays for Energy eFficiency and Extensive Coverage (FS_REFEC)
TR 22.866
  8 use cases
    5.4 Enhancing indoor coverage for the fire brigade
  7 traffic scenarios
    6.7 Traffic Scenario: Public safety
Rel-17 SA1 normative work item REFEC
  Requirements added to TS 22.261 Service requirements for the 5G system

## Slide 4: 5.4 Enhancing indoor coverage for the fire brigade
Smoke diver team entering hospital to rescue cook in cellar
Commander is outside, monitoring the operation
On the way two multihop relay UEs are deployed
Second smoke diver team is sent in to help to unblock entry
Insight into the quality of the indirect communication path will help the commander to take the right decisions
Cook is rescued
gNB
R
Hospital
R
Cellar
R
R
R
R

## Slide 5: Use case Consolidated requirements Service requirements
REFEC study TR 22.866
  5.4.6 Potential New Requirements needed to support the use case
    [PR 5.4.6-3] The 5G system shall enable the end user to determine when a remote UE is losing signal of UE-to-Network Relay UE.
    NOTE: e.g. allows the user to decide when to deploy additional multi-hop relay UEs to maintain a reliable communication path.
  Converted to consolidated requirements in 8.1.1
    [PR 8.1.1-4] The 5G system shall be able to provide indication to a remote UE (alternatively, an authorized user) on the quality of currently available Indirect 3GPP Communication paths.
Normative REFEC work
  Requirements integrated into clause 6.9.2.2 of TS 22.261 Service requirements for the 5G System
    The 5G system shall be able to provide indication to a remote UE (alternatively, an authorized user) on the quality of currently available indirect network connection paths.

## Slide 6: TS 23.304
The remote UE possesses: Path Information, Hop-Count and Hop-Limit for Model A and Model B (multihop) UE2NW relay discovery
Path information: an (ordered) list of User Info ID(s) and corresponding L2 ID(s) of Intermediate UE-to-Network Relay(s) that indicates the transmitted path of the message
Hop-Count: indicates the number of hops between the 5G ProSe Remote UE and the 5G ProSe UE-to-Network Relay on the path selected by the 5G ProSe UE-to-Network Relay
Hop-Limit: an unmodified value that indicates the hop limit of the message. It is set, by the 5G ProSe Remote UE, to a value smaller than the (pre)configured maximum number of hops
Figure 4.2.7.1-1: Reference architecture for 5G ProSe Layer-3 UE-to-Network Relay
Figure 4.2.7.1A-1: Reference architecture for 5G ProSe Multi-hop Layer-3 UE-to-Network Relay
Notes: User Info ID: The User Info ID is configured for Model A or Model B Public Safety Direct Discovery based on the policy of the HPLMN or 3rd party public safety provider application server that allocates it. The User Info ID is sent by the announcing or discoverer or discoveree UE over the air. The definition of values of User Info ID is out of scope of this specification.
Source Layer-2 ID: A link-layer identity that identifies a device that originates ProSe communication frames.
Destination Layer-2 ID: A link-layer identity that identifies a device or a group of devices that are recipients of ProSe communication frames.

## Slide 7: TS 38.300
SL-RSRP_1
SD-RSRP_1
SL-RSRP_2
SD-RSRP_2
RSRP
RSRQ
Each MC service client obtains the signal strength measurement from the (ProSe) lower layers of the MC service (relay) UE
MC service client at 5G ProSe UE2NW relay reports quality of direct path:
  RSRP: Reference Signal Received Power
  RSRQ: Reference Signal Received Quality
MC service clients at MC service UE and 5G ProSe intermediate UE2NW relay report quality of indirect path:
  SL-RSRP: Sidelink Reference Signal Received Power
  SD-RSRP: Sidelink Discovery Reference Signal Received Power
Path information
Hop-Count
Hop-Limit
Assumption: there is only one 5G ProSe intermediate UE2NW relay in the indirect path
Notes: Quality of the indirect path depends on the quality of the Uu interface

## Slide 8: Proposal (1): indirect path
4.SL-RSRP_1
SD-RSRP_1
8. SL-RSRP_2
SD-RSRP_2
8. RSRP
RSRQ
4. Path information, Hop-Count, Hop-Limit
MC service client
(authorized user)
MC service server
1. Quality of MC service client connection request
2. Authorization check
3. Quality of MC service client connection request
5. Quality of MC service client connection response
6. Information evaluation
7(8). Quality of MC service client connection request (response)
11. Quality of MC service client connection response
10. Store information

## Slide 9: Proposal (1): indirect path
Figure 10.6.1-1: MC service user authentication and registration with Primary MC system, single domain

## Slide 10: Proposal (1): indirect path

## Slide 11: Proposal (2): direct path
4.SL-RSRP_1
SD-RSRP_1
8. SL-RSRP_2
SD-RSRP_2
8. RSRP
RSRQ
4. Path information, Hop-Count, Hop-Limit
MC service client
(authorized user)
MC service server
1. Quality of MC service client connection request
2. Authorization check
3. Quality of MC service client connection request
5. Quality of MC service client connection response
6. Information evaluation
7(8). Quality of MC service client connection request (response)
11. Quality of MC service client connection response
10. Information storing
The quality of direct path is implicit in the quality of indirect path procedure.
The quality of indirect path depends on the quality of direct path of the UE2NW relay
Any MC service client can also report the quality of its direct connection (via the Uu interface).
The requirement on RAN quality information in TS 22.261 clause 6.10.2 is fulfilled
TS 22.261 clause 6.10.2:The 5G system shall provide a means by which an MNO can inform authorised 3rd parties of changes in the
  RAT type that is serving a UE;
  cell ID;
  RAN quality of signal information;
  signed frequency band.

## Slide 12: Proposal (2): direct path

## Slide 13: Thank You!