## Slide 1: Group host MCPTT server
Jerry Shih, at&t

## Slide 2: Roles of MCPTT Server (TS 23.379 7.4.2.3.2)
The MCPTT server shall support the controlling role and the participating role. The MCPTT server may perform the controlling role for private calls and group calls. The MCPTT server performing the controlling role for a private call or group call may also perform a participating role for the same private call or group call. For each private call and group call, there shall be only one MCPTT server assuming the controlling role, while one or more MCPTT servers in participating role may be involved.
The MCPTT server performing the controlling roles is responsible for:
- call control (e.g. policy enforcement for participation in the MCPTT group calls) towards all the MCPTT users of the group call and private call;
- interfacing with the group management server for group policy and affiliation status information of this MCPTT server's served affiliated users;
- enforcing functional alias priority handling;
- managing floor control entity in a group call and private call;
- managing media handling entity in call i.e. conferencing, transcoding ; and
- interfacing with the recording server for the management of the recording processes.
The controlling roles for group call, private call and functional alias are independent with each other.
The MCPTT server performing the participating roles is responsible for:
- call control (e.g. authorization for participation in the MCPTT group calls) to its MCPTT users for group call and private call;
- group affiliation support for MCPTT user, including enforcement of maximum N2 number of simultaneous group affiliations by a user;
- enforcing functional alias priority handling;
- relaying the call control and floor control messages between the MCPTT client and the MCPTT server performing the controlling role; and
- media handling in call for its MCPTT users, i.e. transcoding, lawful interception for both unicast and multicast media.
NOTE 2: The MCPTT server in the controlling role and the MCPTT server in the participating role can belong to the same MCPTT system or to different MCPTT systems.
-

## Slide 3: MCPTT Server serving both Participating and Controlling Roles

## Slide 4: Using Group host MCPTT Server
The MCPTT group ID determines which server to host the group communication; It indicates the MC service server within the MC system:
Setup individual connection to participants
Fan out messages to all
Floor control
Group policy enforcement
Etc.

## Slide 5: Normal Group calls using Group host MCPTT Server
Information Element | Status | Description
MCPTT ID | M | The MCPTT ID of the calling party
Functional alias | O | The functional alias of the calling party
MCPTT group ID | M | The MCPTT group ID of the group on which the call is initiated
SDP offer | M | Media parameters of MCPTT server
Broadcast indicator | O | Indicates that the group call request is for a broadcast group call
Implicit floor request (see NOTE) | O | Indicates that the originating client requests the floor.
Requested priority | O | Priority level requested for the call.
Location information | O | Location of the calling party
Remotely initiated call request indicator | O | Indicates that the MCPTT group call request is a result of receiving of a remotely initiated call request and may be included only for remotely initiated call
NOTE: This information element shall be included only when the originating client requests the floor. |  | 
10.6.2.2.8 Group call request (MCPTT server – group host MCPTT server)
Table 10.6.2.2.8-1 describes the information flow group call request between the MCPTT server and the group host MCPTT server.
Table 10.6.2.2.8-1: Group call request information elements
10.6.2.2.8 Group call request (MCPTT server – group host MCPTT server)
Information Element | Status | Description
MCPTT ID | M | The MCPTT ID of the calling party
Functional alias | O | The functional alias of the calling party
MCPTT group ID | M | The MCPTT group ID of the group on which the call is requested
SDP offer | M | Media parameters of MCPTT clients
Implicit floor request | O | When originating client requests the floor, this element shall be included
Broadcast indicator | O | Indicates that the group call request is for a broadcast group call
Location information | O | Location of the calling party.
Requested priority | O | Application priority level requested for this call
Remotely initiated call request indicator | O | Indicates that the MCPTT group call request is a result of receiving of a remotely initiated call request and may be included only for remotely initiated call
10.6.2.2.7 Group call request (MCPTT client – MCPTT server)

## Slide 6: AHGC Using Group host MCPTT Server
Information Element | Status | Description
MCPTT ID | M | The MCPTT ID of the calling party
Functional alias | O | The functional alias of the calling party
MCPTT ad hoc group ID (see NOTE 1) | O | The MCPTT group ID to be associated with the ad hoc group communication
Encryption supported (see NOTE 2) | O | Indicates whether this ad hoc group call supports end-to-end encryption
MCPTT ID list (see NOTE 3, NOTE 6, NOTE 7) | O | MCPTT IDs of the participants being invited for the ad hoc group call
Functional alias list (see NOTE 3, NOTE 6, NOTE 7) | O | The functional alias(es) of the participants being invited for the ad hoc group call
SDP offer | M | Offered Media parameters
Implicit floor request (see NOTE 4) | O | When originating client requests the floor, this element shall be included
Broadcast indicator (see NOTE 5) | O | Indicates that the ad hoc group call request is for a broadcast ad hoc group call
Imminent peril indicator (see NOTE 5) | O | Indicates that the ad hoc group call request is an MCPTT imminent peril ad hoc group call
Emergency Indicator (see NOTE 5) | O | Indicates that the ad hoc group call request is an MCPTT emergency ad hoc group call
MCPTT ID list (see NOTE 3) | O | List of participants required to acknowledge the ad hoc group call before start of the audio transmission
Location information | O | Location of the calling party.
Criteria for determining the participants (see NOTE 6, NOTE 7) | O | Carries the details of criteria or meaningful label identifying the criteria or the combination of both which will be used by the MCPTT server for determining the participants e.g., it can be a location based criteria to invite participants in a particular area
Requested priority | O | Application priority level requested for this group call
10.19.2.1 Ad hoc group call request (MCPTT client – MCPTT server)
10.19.2.3 Ad hoc group call request (MCPTT server – group host MCPTT server)
Information Element | Status | Description
MCPTT ID | M | The MCPTT ID of the calling party
Functional alias | O | The functional alias of the calling party
MCPTT ad hoc group ID | M | The MCPTT group ID to be associated with the ad hoc group call
MCPTT ID list (see NOTE 1, NOTE 3) | O | MCPTT IDs of the participants being invited for the ad hoc group call
SDP offer | M | Offered Media parameters of MCPTT server
Implicit floor request (see NOTE 4) | O | Indicates that the originating client requests the floor
Broadcast indicator (see NOTE 2) | O | Indicates that the ad hoc group call request is for a broadcast ad hoc group call
Imminent peril indicator (see NOTE 2) | O | Indicates that the ad hoc group call request is an MCPTT imminent peril ad hoc group call
Emergency Indicator (see NOTE 2) | O | Indicates that the ad hoc group call request is an MCPTT emergency ad hoc group call
Preconfigured MCPTT group ID | O | Group identity whose configuration is to be applied for this ad hoc group call.
Criteria for determining the participants (see NOTE 3) | O | Carries the details of criteria or meaningful label identifying the criteria or the combination of both which will be used by the MCPTT server for determining the participants e.g., it can be a location based criteria to invite participants in a particular area
Requested priority | O | Application priority level requested for this group call

## Slide 7: Summary

## Slide 8: Next Step
To complete the procedure using a group host MCPTT server for AHGC.
  A CR to update the 10.19.2.3 information flow.
  A CR to add the procedure using group host MCPTT server for AHGC is submitted to this meeting.