## Slide 1: Discussion on network selection optimization related to a proposed WID in SP-170159 and a companion CR in SP-170160 Huawei, HiSilicon, Intel
3GPP TSG Meeting #75 SA-170215
Dubrovnik, Croatia, March 6-10, 2017

## Slide 2
Current art of PLMN selection
  The requirements on PLMN selection are defined in SA1 in stage 1 TS 22.011 (sub 3.2).
  The UE’s behaviour for PLMN selection is specified in CT1 in stage 2 TS 23.122 (sub 4.4), which has worked very well for a very long time since specified.
  For automatic network selection, the UE has followed the following preferential order to select the network
  1. RPLMN
  2. HPLMN (and EHPLMN)
  3. PLMN in User-Controlled list
  4. PLMN in Operator-Controlled list
  5. Other PLMNs with high signal quality criteria
  6. Other PLMNs in order of decreasing signal quality
Notes: DRX: eRAN 3.0

## Slide 3
Current art of HPLMN selection
  The MS shall search for all access technologies it is capable of. No priority is defined for the preferred access technology and the priority is an implementation issue, but "HPLMN Selector with Access Technology" data file on the SIM may be used to optimise the procedure.
  An MS using a SIM without access technology information storage (i.e. without the "HPLMN Selector with Access Technology" data file present) shall search for all access technologies it is capable of. The priority ordering amongst the access technologies is implementation dependent.
Notes: DRX: eRAN 3.0

## Slide 4
HPLMN selection modified in SA1#77
  In SA1#77 meeting (Feb. 2017), a new Rel-15 WID on HPLMN Radio Access Technology deployment Optimisation in Network Selection (HORNS) was agreed. (SP-170159/S1-171457)
  SA1 also agreed a CR (SP-170160/S1-171467) including below updates:
    A UE shall register and get service from the most suitable available PLMN as quickly and efficiently as possible.
    In the case that the UE finds a suitable RPLMN, HPLMN, or EHPLMN in any Access Technology at the appropriate point in the search, the UE may end the search process.
    A HPLMN Selector with Access Technology data field exists on the USIM to allow the HPLMN to optimise the procedure of searching for the HPLMN.
    In the case that the HPLMN Selector with Access Technology data file is present and the Access Technology element has been populated then the HPLMN may configure the UE to optimise the HPLMN search procedure by restricting the PLMN search to that specific set of Access Technologies.
  SA1 has sent an LS (S1-171468) to CT1 and CT6 to review the agreed SA1 CR and to evaluate the specification impacts. The LS has not been seen and the evaluations have not been conducted yet!
  Note 1: Before SA1#77 meeting, in CT1#101 meeting (Nov. 2016), CT1 discussed a disc paper (C1-164961) and a supporting CR (C1-164962) on the same topic but no consensus achieved (CR was postponed).
  Note 2: Before SA1#77 meeting, in CT6#82 meeting (Nov. 2016), CT6 discussed a CR (C6-160521) on the same topic and got postponed due to CT1 linkage. This CR was revised and resubmitted in CT6#83 meeting (Feb. 2017) and got postponed again (C6-170015).
Notes: DRX: eRAN 3.0

## Slide 5
Comments and questions to the new proposal
  The current text in TS 23.122 “In i, the MS shall search for all access technologies it is capable of.” just indicates the UE’s intention in order to select its HPLMN as far as possible, but does not mandate the UE to search all other supported RATs once the UE has already selected its HPLMN on an RAT. So no problem in the current TS 23.122.
  A reasonable UE implementation is: to use the priority order in "HPLMN Selector with Access Technology" data file on the SIM (if presented) to search for HPLMN and once the UE has selected its HPLMN on a higher priority RAT, it stops the search process. However, no restriction on the UE to only use the RAT in the USIM data file for HPLMN search.
  Some potential risks with the new proposal in SA1#77 (SP-170160/S1-171467):
  Assume an operator is undergoing removal of an old RAT (e.g. 2G) in some regions to sell new USIM cards for their subscribers located in those regions (e.g. 2G was removed from the new sold USIM card). If these subscribers used the new USIM card when moving to other regions in which only 2G was deployed, or 2G had better coverage than other RATs, they will never (or more likely cannot) obtain services from this operator (HPLMN), as the UE cannot select its HPLMN by searching 2G even the UE supports 2G.
  This proposal mandates the operator to configure all RATs it deployed in the USIM data file even in some regions it only deployed part of RATs (3G, or 4G) or some deployed RATs need to be removed. More potential risks may be added.
  Finally, this may only work if the Operators keep the USIM content up to date, with respect to the applied RATs and updates/changes to roaming agreements. Without proper up-to-date maintenance of such info this way have serious drawback of avoidance/degradation of services as potentially available PLMN/RATs would not be scanned or not taken into account for registration
Notes: DRX: eRAN 3.0

## Slide 6
Comments and questions to the new proposal
  Any benefit gained from this new proposal if the UE has already performed a reasonable implementation as indicated above? No, and in fact added risks as in the example above.
  The “reason for change” in the CR cover page only talks about PLMN selection but it is also adding a requirement on service registration (1st sentence added by the CR, “A UE shall register and get service …”).
  The “Consequences if not approved” in the CR cover page is empty which means no problem occurs without this CR. Why adding new requirements then?
  The new terms “the most suitable available PLMN” and “suitable RPLMN, HPLMN, or EHPLMN” are used in the CR without any SA1 definition. Note that so far only “suitable cell” was defined/used but not “suitable PLMN”.
  In our view, also the terms “as quickly and efficiently as possible” in the sentence above are ill-defined and not suitable for a stage 1 requirement. What does “efficiently” mean in this context? How are these criteria to be tested?
  The whole sentence is misleading, as it is hiding the fact that there are additional, competing targets, e.g. a preference to select the HPLMN, or the target to avoid “PLMN selection ping-pong” – which implies a preference for the RPLMN. In practice, actually these additional targets determine the overall logic of automatic PLMN selection, not the target to register “as quickly and efficiently as possible”.
Notes: DRX: eRAN 3.0

## Slide 7
Issues with the WID
10. According to section 3 “Justification”, the WID aims at addressing 2 problems:
initial network selection on power-on when out-of-coverage of HPLMN and HPLMN does not deploy all RATs;
roaming agreements restricted to certain RATs (e.g. roaming agreement with VPLMN1 for RAT = 3G, but not for RAT = 4G).
But in section 4 “Objective” the corresponding item 2 is: “Optimise initial network selection on power-on in coverage of HPLMN when HPLMN does not deploy all 3GPP RATs”.
11. For item 3 in section 4: “Consistent UE roaming service when HPLMN only has a roaming agreement for a subset of 3GPP access technologies” it is not clear what is meant by “consistent”.
12. The problem description in section 3 suggests that this item is also intended to affect inter-RAT cell re-selection. (“After the UE has successfully registered on VPLMN B in 3G, it can reselect or be redirected to VPLMN B in 4G, where its registration update will be rejected. This causes un-necessary signalling between the UE and the network, and service interruption at the UE.”)
This has nothing to do with PLMN selection (note that a background search for higher priority PLMN/access technology combinations will not trigger a selection of VPLMN B/4G if the UE is already registered on VPLMN B/3G), and it will probably affect also RAN2 and RAN6 which are currently not mentioned in section 8 of the WID.
Notes: DRX: eRAN 3.0

## Slide 8
Proposal on the way forward
  The source companies are requesting SA plenary to refer the WID HORNS in SP-170159/S1-171457 and the companion CR in SP-170160/S1-171467 back to SA1 until further technical feedback is provided by CT1 and CT6, and possibly RAN groups. The CR is an optimization and a part of Rel-15 and therefore no urgency to rush!
  SA to allow (or guide via an LS) CT1 and CT6 (and possibly RAN2) time to receive the SA1 LS in S1-171468 and to analyze and evaluate potential impacts by the proposed optimization and then to provide feedback to the May SA1 meeting. The proposed handling will not impose delay to the work to still be handled in Rel-15.
Notes: DRX: eRAN 3.0