TSG SA Rel-18 Prioritization Workshop	SP-211193

9-10 December 2021, Electronic meeting                                   (revision of SP-211160)

SA WG2 Meeting #148e	S2-2109328

Elbonia, Nov. 15 - 22, 2021	(revision of S2-2108455r02)

# Source:	Intel, Qualcomm Incorporated, OPPO, ZTE, NTT Docomo, vivo, Telecom Italia, China Unicom, Huawei, HiSilicon, Vodafone, CATT, MediaTek, KPN, China Telecom, CMCC, KDDI, Xiaomi, Apple, Verizon UK Ltd, Samsung, Lenovo, Motorola Mobility, LG Electronics, Rakuten Mobile Inc., Ericsson, Convida Wireless, Orange, DISH Network

# Title:	New SID: Study on enhancement of 5G UE Policy

# Document for:	Approval

Agenda Item:	9.1.3

3GPP™ Work Item Description

For guidance, see 3GPP Working Procedures, article 39; and 3GPP TR 21.900.
Comprehensive instructions can be found at http://www.3gpp.org/Work-Items

# Title: 	Study on enhancement of 5G UE Policy

## Acronym:	FS_eUEPO

## Unique identifier:

Potential target Release: Rel-18

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X |  | X |  |
| No | X |  | X |  |  |
| Don’t know |  |  |  |  | X |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a …

|  | Feature |
| --- | --- |
|  | Building Block |
|  | Work Task |
| X | Study Item |

### 2.2	Parent Work Item

For a brand-new topic, use “N/A” in the table below. Otherwise indicate the parent Work Item.

| Parent Work / Study Items |
| --- |
| Acronym | Working Group | Unique ID | Title (as in 3GPP Work Plan) |
| N/A | N/A | N/A | N/A |

### 2.3	Other related Work Items and dependencies

{List here other Work Items which relate to the proposed one but are not part of the hierarchical structure.}

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |

## 3	Justification

Some issues on the current design of UE Policy were identified:

- #1: URSP is only provided by H-PCF in HPLMN, and in roaming case, the current assumption is that the H-PCF provides URSP rules that are valid for each VPLMN which has roaming agreements with HPLMN. In some scenarios, there may be different URSP rules required for the same application when used in different V-PLMNs. In addition, URSP construction may not satisfy the more dynamic cases, e.g. Edge Computing related URSP rule update (e.g. DNN, SSC mode and S-NSSAI update). As such, a more dynamic mechanism needs to be investigated (e.g. V-PCF involved) to support the VPLMN URSP update for both home-routed and LBO roaming scenarios.

- #2: In Rel-15 5GS design, several triggers for UE Policy provisioning have been identified in clause 6.1.2.2.2 of 23.503. UE triggered UE Policy provisioning procedure can be done via initial Registration in 5GS or Mobility Registration Update when UE moves from EPS to 5GS.  Meanwhile, in Rel-15 5GS UE Policy design, the UE needs to include all its stored PSIs (for URSP and ANDSP) in the UE Policy Container reported to PCF. PCF will assume that UE has no policy if a PSI is missing and provision the corresponding UE Policies, even if the UE has no interest in requesting such policies.  This is inefficient and may result in overload of control plane signalling. This study will investigate the optimization of the UE Policy (e.g. URSP, ANDSP, etc.) requesting and distribution procedure.

- #3:  Void.#4: In 5G deployment, the operator may restrict the usage of a specific network slice (e.g. based on the combination of S-NSSAI and DNN) to some specific third party Service Provider, which can be achieved by constructing the proper URSP rule at PCF and provisioning it to UE side, but currently the 5G network does not know whether the URSP is enforced by the UE. The network may need to be made aware when an application of a third party Service Provider is routed using provisioned URSP Rules.

- #5: Although the handling of UE policies (i.e., URSP and ANDSP) interworking in 5GS and EPS has been specified in TS 24.526, there are networks without ANDSF deployments or the UE will not be able to receive URSP in EPC. In such cases, there is discrepancy in UE behaviour when it is under EPC coverage as it is lacking policies for the EPC side and the UE policies cannot be updated.

- #6: GSMA 5GJA has requested SA2 (S2-2105356) to investigate how to support both standardized (e.g. Enterprise, Gaming, Video Streaming, etc.) and operator-specific traffic categories in the traffic descriptor of URSP.

## 4	Objective

Following objectives will be studied:

-	WT#1: URSP rule provisioning and updating procedures for home-routed and LBO roaming scenario, while keeping the existing framework of policy control based on HPLMN;

-	WT#2: Optimization on UE Policy requesting and provisioning related aspects:

-	WT#2.1: void;

-	WT#2.2: Optimization of the UE Policy (e.g. URSP, ANDSP, etc.) requesting and distribution procedure, i.e. possible extensions to the existing procedures to request UE Policies in a backward compatible way.

- 	#3:  Void.-	#4 Investigate whether and how the network can be made aware when the UE enforces URSP rule and investigate whether and what actions the 5G network can perform.

- 	#5: Investigate if enhancements are needed for provisioning UE with consistent URSP and/or ANDSP across 5GC and EPC, and study the mechanism if needed.

NOTE 1: No new interface will be defined.

-	#6: Investigate how to support standardized and operator-specific traffic categories in the traffic descriptor of URSP.

NOTE 2: This study needs to coordinate with other Rel-18 study items (e.g. edge computing) if there are overlapping aspects.

## TU estimates and dependencies

| Work Task ID | TU Estimate (Study) | TU Estimate (Normative) | RAN Dependency (Yes/No/Maybe) | Inter Work Tasks Dependency Editor’s Note: This column should highlight if WT#x is self-contained, or is depended on completion of other WTs |
| --- | --- | --- | --- | --- |
| WT#1 | 1 | 0.5 | No | WT#1 is self-contained |
| WT#2 |  |  | No |  |
| WT#2.1 | N/A | N/A | N/A | N/A |
| WT#2.2 | 0.75 | 0.5 | No | WT#2.2 is self-contained |
| WT#3 | N/A | N/A | N/A | N/A |
| WT#4 | 1.5 | 0.75 | No | WT#4 is self-contained |
| WT#5 | 1 | 0.5 | No | WT#5 is self-contained |
| WT#6 | 1 | 0.5 | No | WT#6 is self-contained |

Total TU estimates for the study phase: 5.25

Total TU estimates for the normative phase: 2.75

Total TU estimates: 8

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Proposed Spec no. or series | Type (see note 1) | Rapporteur(s) (see note 2) | For info at TSG# | For approval at TSG# | Remarks |
| New TR 23.7xy | Internal TR | Changhong Shan, Intel (chang.hong.shan@intel.com) | TSG#96 (June 2022) | TSG#97 (September 2022) | Including the study outputs on key issues, solutions, and architecture impacts. |

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# |

## 6	Work item Rapporteur(s)

Changhong Shan, Intel, chang.hong.shan@intel.com

## 7	Work item leadership

SA2

## 8	Aspects that involve other WGs

SA3 for security aspects. SA3-LI for LI aspects. SA5 for management and charging aspects. SA6 for application layer aspects.

## 9	Supporting Individual Members

Supporting IM name

Intel

Qualcomm Incorporated

OPPO

ZTE

NTT Docomo

vivo

Telecom Italia

China Unicom

Huawei

HiSilicon

Vodafone

CATT

MediaTek

KPN

China Telecom

CMCC

KDDI

Xiaomi

Apple

Verizon UK Ltd

Samsung

Lenovo

Motorola Mobility

LG Electronics

Rakuten Mobile Inc.

Ericsson

Convida Wireless

Orange

DISH Network

form change history:

2013-12-06 v1.14.1 modified §11 to read: <FamilyName>, <GivenName>, (If the person is new to 3GPP work, give full contact coordinates, in particular, email address.)

2013-10-03 v1.14.0 removal of embedded help text

v1.13.2: adds tdoc header

v1.13.1: minor changes resulting from discussions at CT#41 & SA#41

v1.13.0: mods to enforce linkage amongst stages 1, 2, 3

draft mods Scarrone-Meredith 2008-07 ff

v1.12.1: removes revision marks following approval at SP-29
v1.12.0: includes provision for Study Items (SP-29)

v1.11.0: includes those changes from v1.8.0 agreed at SP-25.

v1.10.0: full circle

v1.9.0: a clean sheet

v1.8.0: includes comments from SA#24

v1.7.0: includes comments from RAN, CN and T #24; also includes “early implementation” data

v1.6.0: includes comments made during review period prior to TSGs#24

v1.5.0: includes comments made at TSGs#23 (Phoenix)

v1.4.0: offered to SA#23 for approval

v1.3.0: offered to CN#23, RAN#23 and T#23 for comments

DRAFT4 v1.3.0: 2004-03-09: Incorporation of comments from Leaders list

DRAFT3 v1.3.0: 2004-02-19: Incorporation of comments from MCC members

DRAFT2 v1.3.0: 2004-01-29: Complete redraft:

v1.2.0: 2002-07-04: "USIM" box changed to "UICC apps"

2003-05-28: spelling of “rapporteur” corrected

2002-07-04: "USIM" box changed to "UICC apps"