TSG SA Rel-18 Prioritization Workshop	SP-211169

9-10 December 2021, Electronic meeting

SA WG2 Meeting #148e	S2-2109363

# November 15th – 22nd, 2021; Elbonia        			(revision of S2-2108855r09)

Source:	Nokia, Nokia Shanghai Bell,

Title:	New SID: new Study on the support for 5WWC, Phase 2

# Document for:	Approval

Agenda Item:	9.1.3

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: Study on the support for 5WWC, Phase 2

## Acronym: FS_5WWC_Ph2

## Unique identifier:

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X |  | X |  |
| No | X |  |  |  |  |
| Don't know |  |  | X |  | X |

Potential AN impacts are not for NG RAN.

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

|  | Feature |
| --- | --- |
|  | Building Block |
|  | Work Task |
| X | Study Item |

### 2.2	Parent Work Item

| Parent Work Items |
| --- |
| Unique ID | Title |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |
| 820014 | Wireless and Wireline Convergence for the 5G system architecture | SA2 normative work for supporting Trusted Non-3GPP access network and Wireline Access network |
| 900012 | Access Traffic Steering, Switch and Splitting support in the 5G system architecture | SA2 R17 normative work for support of Multi-access PDU session |

Dependency on non-3GPP (draft) specification: coordination with BBF and Cablelabs is needed for this study

## 3	Justification

The support of wireline access has been specified in TS 23.501/502/503 and in TS 23.316 in Rel-16. However, some scenarios have not been addressed or partially solved during Rel-16 study/normative work. To better support Wireline access in 5G system and Trusted Non-3GPP Access network, the issues not solved need further studies in Rel-18.

SA2 received different LS from BBF asking for 5GC to support features not supported by R16 5WWC

-	Heterogeneous wireline access MTUs for User plane traffic (see S2-2105358 / BBF LIAISE 464),

-	How to support differentiated IP services for different Non-3GPP devices behind a 5G-RG working in L2 Bridge mode in BBF LS-291/S2-1903875.

22.261 § 6.38.2.1 contains requirements targeting the CPN (defined as part of PIRATES) such as:

-	“Subject to local regulations, the 5G system shall support regulatory requirements for emergency calls, PWS and eCall for UEs connected via a CPN.”

-	“The 5G system shall support real time E2E QoS monitoring and control for any data traffic between a UE within a CPN and the 5G network (i.e. via eRG or via PRAS and eRG)”.

As part of TEI17_N3SLICE it has not been possible to work on How to select a TNGF/N3IWF that supports the S-NSSAI(s) requested by the UE during registration via trusted non-3GPP access network because N3SLICE had the constraint not to impact the UE.

ATSSS has evolved in 3GPP R17 and it should be checked whether some post R16 ATSSS enhancements could be useful for wireline access

NOTE: Non-3GPP devices are defined by SA1;

## 4	Objective

The following aspects will be studied (each numbered bullet corresponds to a sub- work task):

Work task #2: Whether and how to improve the support of devices connecting behind 5G-RG including :

- community WiFi

a1) how to enable community WiFi including the support of network control (e.g based on authentication with 5G network, based on association between the devices and the 5G-RG)

a2) How to support the UE mobility from/to 3GPP access to Community Wifi

- providing differentiated service (e.g.  QoS and charging) for UE and Non-3GPP devices connected behind a 5G RG. This may imply s studying ways for 5GC to identify Non-3GPP devices connected behind a 5G RG and/or their traffic. Conclusions may differ for UE and for Non-3GPP devices .

- Void

- Support of emergency calls, for UE(s) connected behind the 5G RG. This bullet requires co-operation with BBF and Cable labs;

Work task #3 Trusted/untrusted Non-3GPP access network

- How to select a TNGF/N3IWF that supports the S-NSSAI(s) needed by the UE.

Based on the study conclusions it will be decided which item is subject to normative specifications.

Co-ordination with BBF and CableLabs will take place as needed during the study.

## TU estimates and dependencies

| Work Task ID | TU Estimate (Study) | TU Estimate (Normative) | NG RAN Dependency (Yes/No/Maybe) | Inter Work Tasks Dependency |
| --- | --- | --- | --- | --- |
| WT#2 | 2 | 1.25 | NO | Self-contained |
| WT#2a | .75 | .5 |  |  |
| WT#2b | .75 | .5 |  |  |
| WT#2d | .5 | .25 |  |  |
| WT#3 | .75 | .5 | NO | Self-contained |
| WT#3b | .75 | .5 |  |  |

Total TU estimates for the study phase:     2.75

Total TU estimates for the normative phase:       1.75

Total TU estimate: Study + Normative =      4.5

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Remarks |
| Internal TR | TR 23.xxx | Study on support for 5WWC, Phase 2 | SA#96 June 2022 | SA#96 . June 2022 | A new TR will be produced instead of reusing existing TR 23.716 |

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |

## 6	Work item Rapporteur(s)

Laurent.thiebaut@nokia.comor

## 7	Work item leadership

SA2

## 8	Aspects that involve other WGs

SA3 for security aspects. SA5 for management and charging aspects.

## 9	Supporting Individual Members

Supporting IM name

Nokia

Nokia Shanghai Bell

Huawei

HiSilicon

Deutsche Telekom

Broadcom

Lenovo

Motorola Mobility

Qualcomm

KPN

China Telecom

Cable Labs

Charter

Apple

# Comments

Can be done via a TEI18

Can be done by a TEI18

Can be done by a TEI18