## Slide 1: FS_HLCOM conclusion
Intel; S2-151035

## Slide 2: Discussion
During the conference call on 26 Mar 2015 it was initially proposed to categorise the solutions in the TR as follows:
  CN stores MT data until UE is reachable
    Solution 2 DL data buffering in SGW/Gn-SGSN
    Solution 5 DL data buffering in SGW with SCS/AS Assistance
    Solution 6 PPD based data storage and delivery of high latency data
  AS sends MT data when UE is reachable
    Solution 3 Reusing MONTE solution
    Solution 4 Availability Notification after DDN Failure
    Solution 8 Enhanced Power Saving Mode (ePSM)
After some discussion it was clarified that all the solutions in the second category can be complemented to work with Solution 2
  The description of Solution 8 (ePSM) actually explicitly refers to the use of SGW buffering in case there is no absolute clock reference available on which to lock the ePSM cycle or if SCEF is not deployed

## Slide 3: Intermediate conclusion
Given that Solution 2 (SGW buffering) is the common denominator and is compatible with all other solutions in the TR, following was discussed on HLCOM CC:
  Proposal 1: agree on specifying SGW buffering as the base solution for HLCOM
  Proposal 2: select an incremental enhancement from the other solutions in the TR

## Slide 4: Why isn’t SGW good enough? (1/2)
Non-deterministic behaviour: DL data can be for multiple applications on UE from multiple ASs. Hard to standardise the logic on which applications data to buffer and for how long
When used with PSM (step 6b), SGW buffering relies on TAU/RAU request to “un-buffer” the DL data

## Slide 5: Why isn’t SGW good enough? (2/2)
As discussed in the past, coupling the exit from PSM mode with transmission of a TAU Request has several major drawbacks in case of low volume MT data that have certain max delay requirements:
  It creates unnecessary signalling load on the network
    With low volume MT data most of the traffic will be TAU signalling
  It consumes battery
    With low volume MT data most of the battery power will be consumed by TAU signalling
SGW buffering may also interfere with e2e retransmission timers
  Unless 3rd party ASs are provided with information on the UE unavailability, they will likely perform retransmissions, making the SGW buffer multiple copies of the same packet
Handing DL data from multiple applications with different delay characteristics
  S-GW needs to apply different logic for each application buffering or else buffering would not be efficient.

## Slide 6: What about eDRX? (1/2)
When used with eDRX (step 6a), SGW buffering relies on storing of the S1 Paging message in the eNB (steps 6.a.1; 6.a.2) for a long period of time
Potential delay up to several minutes!

## Slide 7: What about eDRX? (2/2)
DRX today is designed in such a way that there is only one Paging Occasion (PO) within a DRX cycle
It is possible for UE to miss the PO
  E.g. due to frame timing or SFN numbering not being aligned between cells
With today’s DRX, missing a PO is not dramatic as UE can be paged again shortly afterwards (e.g. after 2.56s in the worst case, 2.56s being the max Idle mode DRX value today)
With the expected eDRX values (e.g. 10 minutes) missing a PO becomes a reliability issue

## Slide 8: MT data with enhanced PSM (ePSM)
It is assumed that step 6 occurs while the background (Ti + Tp) cycle was in Idle mode

## Slide 9: Why is ePSM good for FS_HLCom? (1/2)
The FS_HLCom WID (SP-140635) states the following objective
  In addressing the above, the following problem will be studied:
    Downlink access for devices that are not reachable for a long period and the problems associated with such devices (e.g. packet discard when the UE sleeps, frequent retransmissions, load on the CN network, waste of radio resources and UE power when the network unnecessarily conveys retransmit packets, etc). This study may propose and evaluate enhancements to the 3GPP system. Depending on conclusions, the study may also propose 3GPP enablers to be used by the service layer e.g. defined by other SDOs for downlink access to devices that are not reachable for a long period.
Downlink access for devices that are not reachable for a long period: By tuning the intervals during which UE is reachable (Ti) or non-reachable (Tp), the UE can be brought out of power saving mode often enough to support MT data that have maximum delay delivery requirements without compromising the battery savings enabled by PSM
Packet discard when the UE sleeps: packet discarding with ePSM is avoided because the 3rd party App Servers knows the description of the ePSM cycle and therefore always know when to initiate MT data
Frequent retransmissions: with ePSM there are no retransmissions because the buffering is pushed up to the data source (i.e. the App Server)

## Slide 10: Why is ePSM good for FS_HLCom? (2/2)
Load on the CN network: by using a deterministic ePSM cycle that needs to be signalled towards 3rd party App Servers only once and by decoupling the sojourn in power saving mode from the Periodic TAU timer, ePSM dramatically reduces the signalling load on the CN. Regarding the CN U-plane, ePSM also brings benefits in that it requires no buffering in the SGW
Waste of radio resources and UE power: with ePSM there is no waste of resources because UE can alternate between successive Idle and PSM interval without any (AS or NAS) signalling with the network. This also dramatically reduces battery consumption in the UE
  given that in use cases with very low traffic volume, the main cause for battery consumption is the Periodic TAU signalling; by decoupling Periodic TAU from PSM, ePSM allows for use of higher Periodic TAU timer values
3GPP enablers to be used by the service layer: ePSM proposes a specific service enabler: exposing the ePSM cycle description via the Service Capability Exposure Function (SCEF)

## Slide 11: How does ePSM relate to eDRX?
  While the parallel study on FS_eDRX (TR 23.770) is still ongoing, some preliminary observations can be made:
    ePSM can avoid long SGW buffering
    if absolute clock reference (e.g. SIB16) is available and SCEF is deployed
    ePSM is more resilient to Paging Occasion misses
      While in Ti interval, the UE can use existing Idle mode DRX
      Example: with Ti = 10s and DRX cycle of 2.56s there are 4 consecutive Paging Occasions within one Ti interval
    Several eDRX key issues in TR 23.770 (e.g. SGW/PGW retransmissions, MT Location services) can be easily addressed with ePSM by simply exporting the ePSM cycle (to the SGW or PGW or GMLC)
  The efficiency of ePSM depends on Ti
    ePSM has one more parameter to play with (Ti)
    For relatively short Ti (e.g. 10s) we expect the efficiency will be comparable with eDRX

## Slide 12: How does ePSM impact the system?
  ePSM only impacts the UE and the MME
    MME:
      Configuration of ePSM in the UE
      The mobile reachable timer is set to a value similar to the Periodic TAU timer (i.e. the same as in the case when PSM is not activated)
      May need to track UE’s ePSM cycle and use SGW buffering (only if SCEF is not available)
    UE:
      Alternating between "Idle mode interval" and "PSM interval" without any signalling with the network
      The handling of Ti and Tp timers is performed in the NAS. Upon Ti expiry the NAS requests the AS to go to deep sleep. Upon Tp expiry the NAS awakes the AS. When awake, the AS may occasionally re-sync with the absolute clock reference provided in SIB16
  No standardisation impact on E-UTRAN
    SIB16 needs to be deployed to provide UTC (Coordinated Universal Time) as the absolute clock reference

## Slide 13: Final conclusion
It is proposed the following:
  Proposal 1: agree on specifying SGW buffering as the base solution for HLCOM
  Proposal 2: select ePSM as an incremental enhancement
When ePSM is used:
  If an absolute reference clock is available (e.g. UTC in E-UTRAN SIB16) and if SCEF is deployed, the SGW buffering is not used
  If either the absolute reference clock is missing or the SCEF is not deployed, then SGW complements the ePSM solution
    ePSM still has the two major benefits for low volume MT data with max delay requirements: 1) reduces signalling load on the network and 2) saves battery power

## Slide 14: Backup (all slides based on the Rapporteur’s conf call presentation)

## Slide 15: Solution 2 – “DL data buffering in SGW/Gn-SGSN”
Buffer in SGW until the device wakes up
M2M Device
SGW
PGW
PCRF
AS / SCS
SCEF
HSS
MME
Device using sleep functions for power saving
2.
2.
Paging (eDRX) or
eRAB establishment (TAU/PSM)

## Slide 16: Solution 5 – “DL data buffering in SGW with SCS/AS Assistance”
Buffer in SGW. Buffer time set in HSS by AS/SCS using SCEF signaling
M2M Device
SGW
PGW
PCRF
AS / SCS
SCEF
HSS
MME
Device using sleep functions for power saving
5.
Buffer time parameter when PDN connection is created or modified

## Slide 17: Solution 6 – “PPD based data storage and delivery of high latency data”
Specific paging & buffering based on policy/PCEF differentiation of high latency data
M2M Device
SGW
PGW
PCRF
AS / SCS
SCEF
HSS
MME
Device using sleep functions for power saving
6.
6.
6.
Buffer time based on policy from PGW/PCRF
Paging based on policy from PGW/PCRF
6.

## Slide 18: Solution 3 – “Reusing MONTE solution”
AS/SCS requests one-time activity notification
Buffer in SGW until the device wakes up
M2M Device
SGW
PGW
PCRF
AS / SCS
SCEF
HSS
MME
Device using sleep functions for power saving
3.
3.
2.
2.
Paging (if idle or eDRX) or
eRAB establishment (TAU/PSM)

## Slide 19: Solution 4 – “Availability Notification after DDN Failure”
Activity notification when waking up after DDN failure
M2M Device
SGW
PGW
PCRF
AS / SCS
SCEF
HSS
MME
Device using sleep functions for power saving
4.
4.
4.
4.
Config
Notification
Paging (if idle or eDRX) or
eRAB establishment (TAU/PSM)
DDN
1st DL packet
2nd DL packet

## Slide 20: Solution 8 – “Enhanced Power Saving Mode (ePSM)”
UE & MME stay in time synch. AS/SCS retrieves using SCEF the time synch parameters that the UE and MME has negotiated (ePSM)
Buffer in SGW until the device wakes up (needed only if the absolute refrence clock on which to lock the ePSM cycle is not available)
M2M Device
SGW
PGW
PCRF
AS / SCS
SCEF
MME
Device using sleep functions for power saving
8.
8.
2.
2.

## Slide 21: Thank You