## Slide 1: Evaluation of “ePSM” proposal in FS_HLCom
Qualcomm Inc., LG Electronics
S2-151154
SA2#108, 13-17 April 2015
San Jose Del Cabo, Mexico

## Slide 2: Where does “ePSM fit”?
Does it solve the handling of MT data for PSM?
  NO
    In S2-151035 it is proposed that another solution is used for Rel-12 PSM: S-GW buffering (a Category 1 solution).
    However, it was already discussed that S-GW buffering alone may not be enough for PSM, as it may lead to needing to store data in the S-GW for hours.
    So another Category 2 solution would be needed for PSM.
    ePSM (alternative 8) actually creates a new solution that is applicable only to rel.13 UEs and SGSN/MMEs that support ePSM.
      Not applicable to UEs that support PSM only (e.g. rel.12 UEs)
      Not applicable to MME/SGSN that support PSM only
  “ePSM” (alternative 8) is an entirely new end to end solution that does not solve the goals of HLCom for PSM, nor for extended DRX UEs.

## Slide 3: Is “ePSM” as an entirely new solution in the UE justified?
Use case –> More Fitting Solution
  MO data Only -> PSM
    No need to be available, UE only leaves PSM when MO data, signaling like pTAU required, so better power consumption than ePSM
  MO data + Scheduled MT data -> PSM
    No need to be available, UE only leaves PSM when MO data, scheduled MT data or signaling erquired, so better power consumption than PSM.
  MO data + Unscheduled MT data with constrained delay tolerance -> Extended DRX.
    Only one paging occasion.
    UE needs to stay available for larger times and read multiple paging occasions at legacy DRX, due to e.g. possible MT SMS, NW originated signaling, so power consumption is worse than eDRX at same delay tolerance requirement.
Do we need a third power saving solution in the UE?
  All use cases are covered by either PSM or Extended DRX.
    ePSM does not cover any of the use cases with better performance
  ePSM does not seem to outperform both PSM and extended DRX in any scenario.

## Slide 4: Conclusion
“ePSM” is an entirely new UE power consumption solution that:
  Does not really solve the issues that motivated by HLCom for UEs that support PSM
    It relies on other solutions to do that
  As a new solution, it does not provide better power consumption than PSM and extended DRX in any scenario.
  It requires UE and SGSN/MME changes and as such is not applicable for UEs and SGSN/MMEs that use PSM or eDRX.
It is therefore proposed that “ePSM” is not further considered as a solution for FS_HLCom.

## Slide 5: Annex

## Slide 6: Status of UE Power Consumption Optimizations
Rel-12:
  SA2 MTC_UEPCOP:
    PSM was adopted as the power consumption reduction technique
    Extended DRX was studied in both RAN2 and SA2 and ultimately not adopted due to lack of time
    Power consumption reduction numbers were produced by multiple companies in RAN2.
Rel-13:
  Extended DRX:
    Study Item in SA2 and Work Item in RAN2
    Extensive motivation analysis presented at both RAN plenary and SA2 (S2-143325).
    Main benefit for unscheduled MT data with delay tolerance constraints
  FS_HLCom:
    How to deal with MT data, when the UE may be unreachable for periods of time.
    It is clear that a solution for Power Saving Mode is required.
    It was also agreed that MT data aspects of extended DRX are studied as part of FS_HLCom