## Slide 1: LADN Use cases and LADN discovery
2018. 05
Samsung Electronics

## Slide 2: Scenario A. Operator LADN service with APP
Operator deploy LADN service
  Operator provides the LADN configuration, connectivity and service including UE application.
  AMF provides LADN Information to the UE to notify the LADN application.
Subscribed DNN
Registration Request
UE
LADN service area
AMF
UDM
APP
Operator Application
(LADN DNN)
Service
Mobile
Operator
Configure LADN DNN
Launch LADN service
LADN DNN
LADN Service Area
LADN Information
Configure LADN Information
Provide Mobile APP (w/ LADN DNN)
SMF
UPF
Registration Accept (LADN Information)

## Slide 3: Scenario B. Operator LADN service for MEC
Operator deployed MEC in a certain area (as LADN service area)
  A UE always discover the available LADN(s)
  Whenever UE moves into the MEC area, UE connects the internet through LADN
LADN service area
AMF
UDM
Mobile
Operator
Configure
DNN subscription for the UE
LADN DNN
LADN Service Area
LADN Information
Configure LADN Information
SMF
UPF
LADN
UE

## Slide 4: Scenario C. LADN service provider
Operator provides LADN connectivity for operator service or for partner service provider
  Operator prepares a LADN connectivity with LADN DNN.
  Service provider provides application with LADN DNN.
  Operator configures wildcard DNN for the UE to allow to use LADN connectivity service
  When LADN application is launched in the UE, the UE discovers the LADN Information for the LADN DNN
UE
LADN service area
AMF
UDM
APP
Application
(LADN DNN)
Service
Operator
Scarlet
LADN Connectivity
LADN DNN
LADN Service Area
LADN Information
Configure LADN
SMF
UPF
Wildcard DNN
Violet
Service
Provider
LADN DNN
Available LADN Information

## Slide 5: Scenario D. User use available LADN
Based on user input, the UE may request all the available LADN Information in the current Registration Area
User may select one of available LADN to establish LADN PDU session.
LADN Configuration
Use LADN
Available LADNs
LADN DNN 1 connected
LADN DNN 2 available
LADN DNN 3 not available
LADN service area
AMF
UDM
LADN
Information
Registration Request for available LADN
Registration Accept (LADN Information)
Mobile
Operator
LADN Connectivity
SMF
UPF
Wildcard DNN
LADN

## Slide 6: Solution 1. Network provision of LADN Info for explicit subscription (existing)
The UE subscribed the LADN DNN under operator control
  The specific LADN DNN is included in the subscribed DNN list from UDM
How AMF provides the LADN information to the UE?
  During registration procedure, the AMF provides the LADN information to the UE if the AMF is configured with the LADN DNN, the LADN DNN is included in the subscribed LADN DNN list.
UE
LADN service area
AMF
UDM
Subscribed DNN
Registration Request
Registration Accept (LADN Information)
Notes: How AMF provides the LADN information to the UE?
  During registration procedure, the AMF retrieves the subscribed DNN list including LADN DNN. The AMF provides the LADN information to the UE if the AMF is configured with the LADN DNN, the LADN DNN is included in the subscribed LADN DNN list.

## Slide 7: Solution 2. UE requested LADN Info with specific LADN
The UE may request the LADN Information for specific LADN if the UE is subscribed to the wildcard subscription.
  The UE is configured with LADN DNN after launching an application with LADN DNN
  The UE triggers to perform a registration procedure to retrieve LADN Information for the specific LADN DNN.
How AMF provides the LADN information to the UE?
  The UE provides the LADN DNN list in the Registration Request
  The AMF provides the requested LADN information to the UE if the requested DNN is included either in explicit or wildcard
UE
LADN service area
AMF
UDM
LADN
Information
Wildcard DNN
Registration Request (LADN DNN)
Registration Accept (LADN Information)
Notes: How AMF provides the LADN information to the UE?
  During registration procedure, the AMF retrieves the subscribed DNN list including LADN DNN. The AMF provides the LADN information to the UE if the AMF is configured with the LADN DNN, the LADN DNN is included in the subscribed LADN DNN list.

## Slide 8: Solution 3. UE requested LADN Info with wildcard LADN
The UE may request the LADN Information for available LADN if the UE is subscribed to the wildcard subscription.
  The UE implementation (e.g. framework) requires to receives the available LADNs based on UE implementation (e.g. user input, or program logic)
  The UE triggers to perform a registration procedure to retrieve the LADN information for the wildcard LADN
How AMF provides the LADN information to the UE?
  The UE provides the wildcard DNN in the Registration Request
  The AMF provides the available LADN information to the UE if the available DNN is included either in explicit or wildcard
UE
LADN service area
AMF
UDM
LADN
Information
Wildcard DNN
Registration Request (Wildcard DNN)
Registration Accept (LADN Information)
Notes: How AMF provides the LADN information to the UE?
  During registration procedure, the AMF retrieves the subscribed DNN list including LADN DNN. The AMF provides the LADN information to the UE if the AMF is configured with the LADN DNN, the LADN DNN is included in the subscribed LADN DNN list.

## Slide 9: Summary of Proposal
How AMF provides the LADN Information to the UE?
  For Scenario A and B, network provision of LADN discovery is used
  For Scenario C and D, UE-requested LADN discovery is used
Solution | Registration Request | Registration Response | Scenarios
Network provision of LADN Information | - | LADN Information for explicitly subscribed LADN DNN(s) | Scenario A and B
UE requested LADN Information discovery | Specific LADN DNN(s) | LADN Information for UE requested LADN DNN(s) in the subscription listNOTE 1. | Scenario C
 | Wildcard DNN (i.e. “*”) | LADN information for all the available LADN DNN(s) in the subscription listNOTE 1. | Scenario D
NOTE 1. the subscription list may include explicit DNN subscription list and/or a wildcard DNN. |  |  |