## Slide 1: Draft Session Outcome of Slice SLA discussion in eNA
China Mobile

## Slide 2: Slice SLA related TDocs and Common Understandings
Slice SLA related TDocs
Common understandings
  The slice radio resource configuration parameters i.e. “Guaranteed/maximum slice radio resource” have already been defined by SA5, i.e. RRMPolicyRatio2 (including rRMPolicyMaxRatio, rRMPolicyMarginMaxRatio, rRMPolicyMinRatio, rRMPolicyMarginMinRatio) in clause 4.4.1, TS 28.541 v15.1.0.
  The slice QoE provided by NWDAF will benefit for slice radio resource configuration/adjustment by OAM.
 | China Mobile/Huawei | Samsung | Ericsson | Nokia
RAN3 |  |  |  | 
SA2 |  |  |  | 
SA5 |  |  |  | 

## Slide 3: Questions and Proposals (1)
Question 1
  Whether Slice SLA fulfilment should be evaluated by OAM or Control Plane i.e. NSSF.
Proposals
  1) SLA fulfillment is done by OAM (QoE from NWDAF to OAM)
    Lack of solution how OAM is done
  2) SLA fulfillment is done by CP (SLA requirement from OAM to NWDAF)
    NWDAF is a proper NF to achieve so
Anyhow SLA/QoE fulfillment shall be provided to RAN for dynamic resource scheduling
Agreement: define NWDAF service to provide slicing QoE. Any consumers with QoE requirement (either CP or OAM) can invoke the service.

## Slide 4: Questions and Proposals (2)
Question 2
  Cause Domain could be not only RAN, but also CN or Transport Network. Do we need to differentiate different domains?
    S2-1900315 (Ericsson): “Solution 33 is a cross domain solution covering actions in RAN, CN and possibly in TN. OAM has the network overview that is required to take appropriate actions. Path bottlenecks can appear in any domain, therefore OAM is used, since it’s capable of triggering actions in the different domains. It has also the capability to evaluate the SLA, as it is a statistical measure on slice level, and understand whether it is breached or not.”
  RAN is always resource limited. CN and TN generally is predictive and resource can be guaranteed though other mechanism e.g., scale in/out in the cloud.
    Therefore, RAN should be the focus for R16
Proposals
  Since domains (such as TN) is outside 3GPP scope. It need further study, maybe in later release, how those cause domain can be done (through OAM or through CPF)
  Outcome: no clear agreement.

## Slide 5: Questions and Proposals (3)
Question 3
  As OAM configured RRMPolicyRatio2 could be very flexible, the margin between guaranteed/maximum slice radio resource could be big (in order to have a better radio resource sharing), whether RAN need some information from network to schedule slice radio resource within such the big margin
    S2-1902163 (Nokia): ” There is nothing that NG-RAN could do with this information, rather only O&M can exploit this information to take appropriate actions: potential appropriate O&M semi-static actions would depend on the SLA, which can take place at different levels: RAN, transport, Core.”
    R3-190678 (Ericsson): “The indication of SLA fulfilment per slice attempts to influence the RAN RRM, which seems to contradict the specifications. Moreover, in case such indication does not have the right (area) granularity and timing, it exposes to the risk of forcing RAN nodes to unnecessarily adopt sub-optimal RRM policies.”
    Observation: Slice QoE Requirement e.g. Average Service MOS and Percentage UEs’experience satisfied is part of SLA Requirement and control plane is responsible for monitoring Slice QoE fulfillment.
Proposal 3
  RAN (in cell granularity)may need Slice QoE fulfillment, which is taken into account by RAN when scheduling slice radio resource.
    NSSF query NWDAF for the problematic area in cell list granularity and sends slice QoE fulfillment e.g. in minute granularity to RAN
  Outcome: SLA evaluation be done by OAM. Send QoE instead of SLA fulfillment indication to RAN seems ok. But people argue may need to wait for RAN or update the solution to RAN.

## Slide 6: Questions and Proposals (4)
Question 4
  If no slice priority is introduced, RAN has no reason to schedule more resources for the new slice.
    R3-190197 (Nokia): “It is unclear how NG-RAN could improve the service for this slice while not changing the priority with regards to the other slices. ”
    R3-190678 (Ericsson): “It should also be noted that any action that triggers prioritisation of UE handling for a certain slice will induce down-prioritisation of UEs in other slices. Such actions should be therefore taken by a node that understands the status of fulfilment in all slices, so to avoid that prioritisation of UEs handling in one slice causes a lack of SLA fulfilment in another slice. ”
Proposal 4
  The priority of new created slice on trial phase is low compared to the existing slice whose SLA is signed in order to avoid/minimize impact on existing slice.
  RAN schedule the radio resource for the existing slice in priority compared to the newly created slice.
Outcome: It was commented do not discuss RAN3 contributions. While, it was pointed that the priority information already reflected in solution 32, already.

## Slide 7: Summary
  NWDAF evaluate QoE
  QoE send to NSSF and OAM
  OAM do SLA fulfillment evaluation
  NSSF compares slice QoE requirement with NWDAF provided QoE and indicate fulfill or not to RAN
  RAN do the resource adjustment (within the threshold configured by OAM)
  RAN send resource usage to OAM. OAM determine whether to update resource usage based on real RAN resource usage and SLA fulfillment

## Slide 8
Thanks!

## Slide 9: Solution 32 update
Slice level resource configuration and schedule:
- Existing Slice (high priority):
> Guaranteed: 10%
> Maximum: 50%
> Margin: 40%
- New Slice on trail (low priority)
> Guaranteed: 15%
> Maximum: 70%
> Margin 55%
RAN
NSSF
(Admission Control + Slice QoE meet or not?)
CN
OAM (Slice Creation + Slice SLA Evaluation/ Cause Domain Determining +Slice Resource Configuration)
Resource Configuration
(Initially 15%~70%)
3rd AF
⑤ New slice QoE
Slice QoE Requirement, which is a part of SLA Requirement:
- Network Area
- Average Service MOS
- Number of Subscribers
- Percentage UEs’ experience satisfied
NWDAF
(Slice QoE calculation)
② New slice QoE (Network Area by Tenant)
③ Problematic Area Query in cell list granularity
- Average Service MOS < 3
- Percentage UEs’ experience satisfied < 80%
① Cause Domain is RAN for the new slice
AMF
New Slice
Existing Slice
PCF
PCF
Service MOS
④ Slice SLA fulfilment Info Slice QoE Fulfillment e.g. in minute granularity per cell list)