## Slide 1: Discussion on Using Topology Info from OAM for Efficient Data Collection Huawei, HiSilicon, Orange

## Slide 2
Background
Observation 1) Data Collection can be either per CellID or TAI ID
Observation 2) Current TS 28.552 Does not define PM Info per TAI
Examples of Radio PM Clause 5.1 in TS 28.552 all per Cell:
Average delay DL air-interface
DL Total PRB Usage
…

## Slide 3
Problem
NF#1
NF#2
NWDAF
OAM
Subscribe(NetPerformance, AoI=TA#A)
Subscribe(NetPerformance, AoI=“CellID#a, CellIDb, CellIDc”)
AoI = Area of Interest
Subscribe(PM for TA#A”)
Subscribe(PM for CellID#a, CellID#b, CellID#c”)
Collect Data
Notify PM TAI#A
Notify PM CellID#a, CellID#b, CellIDc
Topology Info = TAI#A mapped to CellID#b, CellID#c, CellID#d
Without being aware of CellID x TAI mapping:
-> NWDAF collects 2 times the same data from CellID#b, CellID#c
Questions:
Can SA5 provide PM per TA?
How to avoid that NWDAF collects multi times (directly or indirectly) the same data from OAM?

## Slide 4
Possible Alternatives to Solve the Problem
Alternative 1 – Direct Request for Topology Info from OAM (using existent SA5 services)
Alternative 2 – Topology Info from OAM piggybacked into PM data itself (requires new SA5 services)
NF#1
NF#2
NWDAF
OAM
Subscribe(NetPerformance, AoI=TA#A)
Subscribe(NetPerformance, AoI=“CellID#a, CellIDb, CellIDc”)
AoI = Area of Interest
Subscribe(PM for CellID#a, CellID#b, CellID#c”, CellID#d)
Collect Data
Notify PM CellID#a, CellID#b, CellIDc, CellID#d
GetAttributes(Tracking Areas)
Further aggregates collected data
SubscribeModification(Tracking Areas)
NF#1
NF#2
NWDAF
OAM
Subscribe(NetPerformance, AoI=TA#A)
Subscribe(NetPerformance, AoI=“CellID#a, CellIDb, CellIDc”)
AoI = Area of Interest
Subscribe(PM for TA#A)
Collect Data
Notify (PM TA#A with (CellID#b, CellIDc, CellID#d))
Learns CellID x TA mapping
When a TA changes in OAM, NWDAF will be operating with wrong TA association until OAM notifies a new PM available to be collected by NWDAF, and then NWDAF learns again.
Provisioning Services defined in TS 28.532
Resource Models defined in TS 28.541
NOTE: Topology Info = “TAI#A mapped to CellID#b, CellID#c, CellID#d”

## Slide 5: Proposal of Change in TS 23.288
Based on selected solution, update:

## Slide 6
Thanks!