## Slide 1: SA6 LS (S2-2004784 = S6-200947) on IP address to GPSI translation
Source: Nokia
Document for: Discussion and endorsement
Agenda Item: 4.1
Work Item / Release: EDGEAPP / R17

## Slide 2: SA6 LS (S2-2004784 = S6-200947) on IP address to GPSI translation
SA6 Question: Does the core network provide an API to translate a UE's IP address (private and public) to its GPSI, and if not, would it be feasible to provide such functionality in Rel-17 in order to address the SA6 requirement for UE IP address translation?
SA6 Question: is it feasible to provide application-specific GPSIs, to ensure that a single GPSI can not be used to track an end user's activity across applications (EASs), to protect end user privacy?
ANALYSIS
AF request identifying the UE by its IP address
This IP address may be NATed
SA6 asks to support an API allowing to provide back a GPSI to the AF
There were various associated inputs to this meeting but before going ahead it is suggested to endorse a few points in next 2 slides

## Slide 3: SA6 LS (S2-2004784 = S6-200947) Proposals for endorsement
there is a requirement for 5GC to support API from AF targeting a UE only identified by IP addressing information? :
Decision: yes/no
IP addressing information provided by AF may correspond to NATed IP addressing information ? :
Decision: yes/no
there is a requirement for 5GC to support providing a GPSI back to an AF that that has issued an API targeting a UE only identified by IP addressing information ? :
Decision: yes/no
(how to discuss the SA2 solution (the question is NOT on what the technical solution should be):
  Either via (draft R17 CR(s))
  Or via PCR to 23.748 (for example associated with KI 3)
  Decision: draft R17 CR / PCR to 23.748

## Slide 4: SA6 LS (S2-2004784 = S6-200947) Proposals for endorsement
A LS is to be sent back to SA6 telling that
  SA2 will work on the requirement for 5GC to support API from AF targeting a UE only identified by IP addressing information where the IP addressing information provided by AF may be NATed?
  SA2 will not work further on providing a GPSI back to an AF that that has issued an API targeting a UE only identified by IP addressing information as long as the requirement ahs not been clarified by SA6 and the security aspects analysed by SA3