## Slide 1: FS_IIoT Show of hands questions
Nokia (Rapporteur)

## Slide 2: Key Issue #1 Uplink Time Synchronization
Questions:
  Options for BMCA:
    Option 1: BMCA is C-plane based; TSN AF executes BMCA method.
    Ingress port forwards the Announce messages to TSN AF (or NEF) for BMCA procedure which determines the PTP port states, TSN AF (or NEF) informs the DS-TT and/or NW-TT port states if needed.
    Support Option 1 for BMCA? (YES/NO)
    Option 2: BMCA is U-plane based; NW-TT executes BMCA method.
    Ingress port forwards the Announce messages to NW-TT for BMCA procedure which determines the PTP port states and informs TSN AF (or NEF) on the BMCA result if needed.
    Support Option 2 for BMCA? (YES/NO)
    Way forward: < > Option 2 is proposed as way forward
Notes: Informal company position checking: 9 (Option 2) versus 2 (Option 1); Option 2 supported by majority.

## Slide 3: Key Issue #2 UE-UE TSC Communication
Background
  Item 1: Varying views on support for UE-UE communication for IEEE TSN bridge with or without any pre-configuration.
Questions:
  Option 1: Allow UE-UE communication, 5GS acting as IEEE TSN bridge supported only if they are allowed as configured for e.g., same member of a group, same DNN/S-NSSAI. Support Option 1 for UE-UE communication?
  Option 2: Allow UE-UE communication considering AF request for QoS, as long as they are within the same 5GS acting as IEEE TSN Bridge for ETH PDU Sessions. Support Option 2 for UE-UE communication?
  Option 3: Allow both options – option 1 & 2. Support Option 3 for UE-UE communication?
  Way forward: < > Capture the principle “UE-UE communication (using local switching) is supported for all the UE(s) connected to the same DNN/S-NSSAI, terminating on the same UPF network instance.“
Notes: S2-

## Slide 4: Key Issue #2 UE-UE TSC Communication
Background
  Item 2: Varying views on how the local switching within UPF should be controlled.
    Way forward: < > Capture the principles “For IP PDU Sessions, UE-UE communication using local switching (without routing via N6) can be supported by UPF implementation based on operator policies. For ETH PDU Sessions, Local switching via UPF can be autonomously determined based on MAC learning (for ETH). For ETH IEEE TSN sessions, CNC provided static forwarding rules is supported for UL.”
Notes: EN: Charging is FFS

## Slide 5: Key Issue #3A Support for deterministic services
Background:
  Key issue 3A “focuses on enhancing the NEF framework”; all areas for study of KI#3A only deal with the NEF-AF (TR 23.700-20 clause 5.3.2)
  There is no explicit SA1 requirement about a need for hold and forward functionality for VIAPA services, i.e. SA2 needs to reconfirm with SA1 first.
Question:
  Should it be possible for the NEF to derive Qbv parameters based on QoS information to support Hold and forward functionality in the NW-TT and DS-TT as per Rel-16?
  Note: Rel-16 hold and forward functionality in DS-TT and NW-TT is assumed to be reused as-is.

## Slide 6: Key Issue #3A Support for deterministic services
Burst spread is used as TSCAI for scheduling optimization
  Option 1: Burst Spread can be provided by AF to SMF via NEF/PCF
  Question 1: Should support for Option 1 be specified in the spec?
  Option 2: Burst Spread can be detected by UPF and provided to SMF
  Question 2: Should support for Option 2 be specified in the spec?
  Option 3: Burst Spread can be detected by RAN
  Question 3: Should support for Option 3 be specified in the spec?

## Slide 7: Key Issue #3B Exposure of TSC services Exposure of Time Synchronization
Background
  Conclusion has the following:
  Editor's note: whether there is a need to include validity time for AF time sync request is FFS. Also, how to support validity time is FFS.
  Options
  Option 1: AF assumed to activate and deactivate requests for all the DS-TT(s) (thus maintain validity period accordingly).
  Option 2: AF provides validity period for the request, 5GS maintains the validity period (i.e. new activate requests are not allowed when the validity period expires).
  Way forward: Option 1 seems to be preferred?