## Slide 1: SA2#141E-ProSe KI#1,#5,#7 Controversial Issues and WAs
OPPO, CATT (Rapporteurs)

## Slide 2: KI#1-5G DDNMF Architecture
Interim agreement: 5G-DDNMF is responsible for ProSe code allocation.
Issue: Which architecture is adopted for 5G DDNMF?
Alternatives
  Alt 1: Adopt the architecture of Annex B.2 as the reference architecture, i.e. UE interacts with 5G DDNMF via user plane. (S2-2007664 Qualcomm Incorporated, vivo, CATT)
  Alt 2: Adopt the architecture of Annex B.3 as the reference architecture, i.e. UE interacts with 5G DDNMF via control plane. (S2-2007219 Huawei)
Working assumption
  Alt 1: Adopt the architecture of Annex B.2 as the reference architecture, i.e. UE interacts with 5G DDNMF via user plane?
  Taking S2-2007664 as starting point for further discussion?
  For Alt 1 (annex B.2), the provision of ProSe codes over PC1 instead of PC3 is FFS.

## Slide 3: KI#5-The path selection policy rules update
Issue: Whether the path selection policy rules can be generated/updated based on QNC, NWDAF, AF information?
Alternatives
  Alt 1: QNC, NWDAF, AF information are used for path selection policy generation. (S2-2007298 (Samsung, Huawei, Apple, ZTE, ITRI))
  Alt 2: NWDAF analytics and QNC are not used for path selection policy generation. (S2-2007445 (CATT, OPPO, LG Electronics, Intel))
  Alt 3: NWDAF analytics and AF information are used for path selection policy generation (deduced alternative )
  Alt 4: AF information are used for path selection policy generation.(deduced alternative)
Working assumption
  AF or the existing NWDAF can be used for path selection policy generation; QNC are not used path selection policy generation?
  Taking S2-2007298 as starting point for further discussion?

## Slide 4: KI#7-PC5 charging configuration to the UE
Issue: Whether and how for the network to provide PC5 charging configuration to the UE?
Alternatives:
  Alt1: PCF provides charging configuration to the UE. (S2-2007662(Qualcomm Incorporated, Convida, Matrixx, CATT), S2-2006961(OPPO, NEC))
  Alt2: Fixed in the UE, can rely on SA5 decision. (S2-2007274 (Ericsson))
Working assumption
  Taking Alt1-PCF provides charging configuration to the UE as working assumption?
  Taking S2-2006961 as starting point for further discussion?

## Slide 5: KI#7-UE PC5 charging usage report
Issue: How for the UE to report the PC5 charging usage to the network?
Alternatives
  Alt 1: Report to AMF via NAS, AMF reports to CHF. (CP based solution, S2-2007274 (Ericsson))
  Alt 2: Report to SMF via NAS, SMF reports to the CHF. (CP based solution, S2-2006848(NEC))
  Alt 3: Report to the ADF/CTF via user plane, ADF/CTF reports to the CHF. (UP based solution, S2-2007662 (Qualcomm Incorporated, Convida, Matrixx, CATT))
  Alt 4: Wait for SA5 progress. (S2-2007490 (Nokia))
Working assumption
  SA2 determines UE reports charging usage information via CP or UP via, e.g. show hands.
  CP based solution:
  UP based solution:
  If via CP, which network entity the UE should report to.