## Slide 1: Consideration of the questions raised during CC.

## Slide 2: How the SMF gets MB-SMF ID
  If SMF retrieves MB-SMF ID from UDR (current solution in TR23.757 v1.1.0) is used
    New interface between SMF and UDR just for the purpose of SMF retrieving MB-SMF Id,
      Not compliant with the current system design that access to UDR is restricted to UDM, NEF and PCF;
    If the PCF is used (proposal raised during discussion and not in the TR yet), the solution needs to be described, e.g. how does the first UE Join and PCF interaction work? And subsequent UE join and retrieval?
  It is worthwhile to highlight that retrieving MB-SMF ID is a common issue for both of AMF/SMF-centric solution, and the mechanism doesn’t rely on AMF/SMF-centric principle. In other words, retrieving MB-SMF ID could be applicable for one even such retrieving methods was original designed for the other. Retrieving MB-SMF ID from UDR is only one possible solution.
    Using UDR: new interfaces between UDR/SMF is introduced.
    Using UDM: AMF/SMF contacts with UDR via UDM and the steps are quite similar as the original UDR approach.
    Using PCF: if the PCF is used, it means that SMF will retrieve MB-SMF information from UDR via PCF after receiving the request from the UE. (If the dynamic PCC is configured, then there would be no difficulties to realize such procedure, with only introduce one new IE for the interaction with PCF). Whether PCF already has the MB-SMF information for the MBS session ID or not is dependent on the scenario, but absolutely not an issue.
AMF/SMF
NRF/PCF/UDM/UDR
Request message* (MBS session ID)
Response message (MB-SMF ID)
* The message name is only for illustrative purpose.
SMF-centric and AMF-centric solutions could use the similar mechanism for retrieving MB-SMF ID.

## Slide 3: For location dependent MB service
UDR expected to allocate Area Session identifier.
Similar as MB-SMF ID retrieving issue, this is a detail issue and unrelated to AMF vs SMF centric approach. We could have several candidate alternatives besides using UDR:
  NEF or MB-SMF could also allocate session ID. And after that the session ID together with MBS session context will be stored at MB-SMF locally or UDR.
  One reason of using UDR is, we need session IDs that are unique for the MBS session and there can be multiple NEFs and MB-SMFs to allow different local ingress points. So they would first need to check already allocated area session IDs in the UDR. That is why the functionality is now in the UDR.
AF/NEF
MB-SMF/NEF/UDR
Request message* (location area)
Response message
* The message name is only for illustrative purpose.
Allocate session ID (flow ID) and store it
SMF-centric and AMF-centric solutions could use the similar mechanism for allocating session ID (flow ID).

## Slide 4: UE joining 5MBS may get rejected causing denial of service attack type situation
  UE Join may get rejected due to MBS Session not configured yet in MB-SMF, there is no way for the UE(s) to know when MB-SMF has been configured, the UE(s) may keep trying causing denial of service attack type situation;
  Firstly this is also independent from the AMF vs SMF discussion.
  We could discuss whether this option is supported:
    If UE joining is done per the instruction of the service announcement, and resources in 5GC has already been established, it means this situation (keep trying and causing DDoS) will not happen.
    If we also want to consider the other scenarios, it is related to option to create dynamic multicast sessions when UE joins which will be based on operator policy. Note that RFC 8777 allows to look up source specific multicast address in a trusted and secure DNS. Accepting join requests could be based on that.

## Slide 5: 5MBS in Roaming not addressed
  The inbound roamer would not be able to join the multicast service.
Both AMF-centric and SMF-centric solution are yet to address the roaming case. This is actually solvable and there is no difference between AMF and SMF centric approach.
  In general there hasn’t been much focus on roaming case, and we have not reached the point of having solid conclusions for roaming scenarios. This comment is BTW regardless of AMF and SMF/MB-SMF centric approaches, and actually solvable.
  For inbound roamers, we could achieve that via a local break out PDU session is established for individual delivery and joining. This could be e.g. based on DNN. This avoids multicast distribution trees over network boundaries and related MB-SMF discovery issues.
  Anyway, the support of roaming (and how to support) could be further checked during the normative phase.

## Slide 6: UE join MB service when involving ETSUN procedure not addressed
  How a user from a different region (i.e. different SMF service area) joins a multicast service is not addressed so far
    To address such interaction, additional complexity is expected to cover different ETSUN procedures;
    Depending on RAN feedback whether IDLE UE could receive MB service, further complexity may be expected
Both AMF-centric and SMF-centric solution are yet to address the ETSUN case:
  It seems that most of the companies considers to not address limited MB-SMF service area issue (even in Sol#19).
  Both AMF-centric and SMF-centric actually are the same considering the message from RAN to the MB-SMF (i.e., RANAMFMB-SMF).
  Multicast distribution tree for individual delivery over several regions and related MB-SMF discovery may be an issue for both solutions. However, the option with location dependent services allows to define own ingress points in different regions and thus to avoid the need for multicast distribution trees over several regions.

## Slide 7: Signaling increase unnecessarily due to MBS Session operation performed via PDU Session signaling
  MBS Session Update will have to be performed “per PDU Session per MBS Session” instead of “per MBS Session”
  The proposal of MBS Session deactivation by releasing the MBS QoS Flow or releasing the shared N3 tunnel will have to be performed via PDU Session as well.
It gets into comparison territory and vast majority of companies have already made comparison and support SMF/MB-SMF. Note that for AMF centric and SMF centric solution, update for the shared delivery are basically the same. For the PDU Session update, we could also allow potential enhancement to handle this scenario in a more optimal way.