## Slide 1: FS_MUSIM proposal for working assumption and questions for show-of-hands
Intel (Rapporteur)
SA2#142E, Electronic meeting, 16 – 20 November 2020

## Slide 2: Agenda
Based on the moderated email discussion FS_MUSIM summarized in S2-2008760 the Rapporteur proposes the following items for decision / endorsement in SA2#142E CC#1
    Endorse a Working Assumption on Paging Cause
    Question Q1 for Show of Hands (SoH) on Busy Indication
    Question Q2 for Show of Hands (SoH) on 5GS optimizations for operation “on the same network”

## Slide 3: Working Assumption on Paging Cause for endorsement
During the moderated email discussion FS_MUSIM summarized in S2-2008760 the following question was asked:
    Q1.1: Assuming non-blocking feedback from SA3, RAN2 and RAN3, which of the following Paging Cause options your company can support for inclusion in the final conclusions (more than one option can be supported)?
      Option 1: No Paging Cause.
      Option 2: One Paging Cause (indicate which one i.e. “MMTel Voice” or “Important service”).
      Option 3: Multiple Paging Causes (indicate which ones from the following set: “MMTel Voice”, “MMTel Video”, “SIP Signalling”, “NAS Signalling”, “SMS over NAS” and “Other data”).
26 (28) companies provided replies on Q1.1 as follows:
      13 companies indicated that they can support either Option 2 or Option 3 (sometimes with indicated preference).
      5 (6) companies indicated that they can support Option 2 with Paging Cause for “voice” (including one company that indicated either “important service” or “voice”).
      3 companies indicated that they can support either Option 1 or Option 2.
      3 companies indicated Option 1 as preferred, without indicating any other option.
      1 (2) company indicated Option 1 only.
      1 company indicated Option 3 only.
      NOTE: the numbers in parentheses include the late input provided by two companies
Focusing on Option 2 with Paging Cause for “voice”, it seems that at least 21 (22) companies [and possibly 24 (25)] out of 26 (28) can support that option.
Based on the feedback summarised above, Rapporteur’s proposal is to endorse the following Working Assumption in SA2#142E CC#1:
    WA: One Paging Cause with the meaning of “voice” shall be pursued for normative work.
      The WA shall be checked against feedback from SA3, RAN2 and RAN3.

## Slide 4: Q1 for SoH: Busy Indication
  Q1: Should a Busy Indication (either NAS-based or RRC-based) be pursued for normative work in Rel-17?
      Yes
      No
During the moderated email discussion FS_MUSIM summarized in S2-2008760 companies were invited to provide their opinion:
    Q2.2: Whether they are supportive of Busy Indication (as NAS-only, both NAS and RRC, not at all)?
23 (25) companies provided replies on Q2.2 as follows:
      11 companies replied that Busy Indication should be supported as both NAS and RRC layer (the latter for RRC_Inactive only).
      8 (10) companies replied that no Busy Indication is needed in Rel-17.
      2 companies indicated support for NAS-only Busy Indication
      1 company indicated support for RRC-only Busy Indication.
      NOTE: the numbers in parentheses include the late input provided by two companies
Based on the feedback summarised above, Rapporteur’s proposal is to consider the following question for SoH in SA2#142E CC#1:

## Slide 5: Q2 for SoH: “On the same network”
  Q2: Should 5GS optimizations for operation “on the same network” be pursued for normative work in Rel-17?
      Yes
      No
During the moderated email discussion FS_MUSIM summarized in S2-2008760 the following question was asked:
    Q7.1: Should 5GS optimizations for “on the same network” be pursued for normative work in Rel-17?
23 (25) companies provided replies on Q7.1 as follows:
      11 (13) companies indicated that a solution of this type is not needed for Rel-17.
      10 companies indicated that a solution of this type is needed for Rel-17.
      2 companies abstained.
      NOTE: the numbers in parentheses include the late input provided by two companies
Based on the feedback summarised above, Rapporteur’s proposal is to consider the following question for SoH in SA2#142E CC#1: