## Slide 1: FS_eNPN Input to CC#1, including SoH question
Peter Hedman, Ericsson (rapporteur)
SA2#142E, Electronic meeting, 16 – 20 November 2020

## Slide 2: Background See S2-2008473 - Email discussion on FS_eNPN
KI#4 conclusion includes the following.
“Upon registration to an SNPN for Onboarding, the UE provides the information at RRC level which indicates the registration is for onboarding. This information will be specified only for SNPN and allows NG-RAN to select an appropriate AMF that supports onboarding procedures.”
And
“Upon registration to an SNPN for Onboarding, the UE provides the information at NAS level that the registration request is for onboarding to allow AMF to, e.g., select an appropriate SMF and perform other onboarding-related configuration.”
It is not clear whether the above RRC and NAS information provided by the UE is separate indications, e.g. like in case of RLOS in LTE/S1 mode, or it use an S-NSSAI dedicated for onboarding.

## Slide 3: Question and summary See S2-2008473 - Email discussion on FS_eNPN
Question: Should the RRC and NAS information provided by the UE indicating that the access is for onboarding be:
  A. Separate indications (RRC and NAS) for onboarding, or
  B. an S-NSSAI dedicated for onboarding
Summary
  14# companies prefer to go with option A
  1# company prefer to go with option A, unless a globally standardised S-NSSAI is used to provide the RRC and NAS indications
  3# companies prefer to go with option B.
  1# company can go with either option A or option B but a decision is needed
  2# companies can go with either option A or option B dependent on scenario (i.e. both standardized)

## Slide 4: Proposal See S2-2008473 - Email discussion on FS_eNPN
Given that majority of the companies prefer to go with option A, it is proposed that Option A is agreed as the way forward.
The P-CR in S2-2008467 implements Option A.
If no agreement it is proposed to do a SoH at CC#1 with following question:
  Should the RRC and NAS information provided by the UE indicating that the access is for onboarding be:
    A. Separate indications (RRC and NAS) for onboarding, or
    B. an S-NSSAI dedicated for onboarding
Option A: Yes: No:
Option B: Yes: No: