## Slide 1: Session Join Authorization
Jeffrey Zhang
Juniper Networks

## Slide 2: Why this discussion
There have been confusion/disconnect on authorization and people were just talking about different things
This slide deck tries to list all aspects related to session join authorization, and try to get closer to consensus

## Slide 3: Level of session join authorization
Feature level vs. service/session level
  Feature level: whether a UE is allowed to join any multicast session at all
  Service/session level: whether a UE is allowed join a particular session
    A UE may be allowed to join session 1 while denied to join session 2
Consensus in 23.757, Clause 8.9 – both are to be standardized
  5GC Authorization of UE joining 5MBS multicast sessions on 5MBS feature level.
  5GC Authorization of UE joining a specific multicast MBS Service.

## Slide 4: Who performs per-session join authorization
5GS based authorization
  5GS performs authorization based on AF-provided information
  Consensus in Clause 8.9 of 23.757: to be supported
AS based authorization
  Authorization is deferred to the AS
  Whether it is to be supported is to be determined during normative phase
  Discussed in pre-143e CC#1 but there were lots of confusions/disconnect
    This slide deck tries to restate/clarify some points made during CC#1

## Slide 5: AS based authorization
Two types of AS based authorization
  5GS asks AS to authorize 5MBS session join request sent by UE to 5GS
  AS and UE interact at application layer; AS then notifies 5GS to start/stop sending multicast session data to the UE
    Solution #6.34 in 23.757; only the notification part needs to be standardized.
    Consensus: to be supported, as stated in 8.2.2.2 of 23.757:
      The UE may perform application level join/leave to a multicast session, the 5GC shall support multicast session join/leave operation for a user, e.g based on AF request
So only #1 remains open
  This should clarify the disconnects/confusions during CC#1 and recorded in the minutes
  Only one real question (from Judy) remains – next slide

## Slide 6: Latency concern?
If we defer the authorization to AS when the join request comes in from a UE, would the latency be too large?
This is indeed not appropriate for latency sensitive services
But it may be acceptable and preferred for other services
  It saves the trouble of AF providing authorization information and 5GS storing the information
  For CP based joins, authorization is needed only once when the initial join is received, unlike up based joins
    Is this true?
    If UP based join is to be supported, the authorization can also be optimized to only apply for the initial join
  Implementation wise, only need an API for 5GS to request the authorization
    For the AS to provide the authorization result, the procedure for method #2 of AS based authorization can be used (the AS asks 5GS to start/stop sending to a UE)

## Slide 7: Proposal
Support for 5GS to request AS to perform per-session authorization
Regardless the conclusion on the above, other authorization level/methods are to be supported as already concluded:
  Per feature/service level authorization
  Per service level authorization by 5GS based on AF-provided information
  Application layer authorization between AS and UE, then AS requests 5GC to start/stop sending session data to a particular UE