## Slide 1
5MBS Issues (based on TR 23.757 v17.0.0 + 23.247 v0.1.0)
For information
Source: Ericsson

## Slide 2: Issues
Attempt to address scalability issue resulting in more issues, e,g.
  Non-coherent approach: different entities involved in Activation and Deactivation
Option 2
AMF
UE
SMF
MB-SMF
MBS deactivate
NG-RAN
MBS contexts and N3 may be kept for connected and inactive UEs
Variant 2c
DeActivate (MBS session id, list of NG-RAN nodes)
UE
NG-RAN
AMF
SMF
MB-SMF
    MBS Session Deactivate via MB-SMF -> AMF -> RAN (S2-2101017 (SA2#143E));
Scalability issue due to the solution built on per UE/PDU Session signaling;
    MBS Session Update not addressed (MBS QoS Flow update/creation/deletion)
    MBS Session Activation (S2-2102942, SA2#144E) via MB-SMF -> SMF -> AMF -> RAN

## Slide 3: Issues
(CONT’d) Attempt to address scalability issue resulting in more issues, e,g.
  No solutions addressing all CM states, e.g. during MBS Session Activation:
    Q1: If joined UEs are CONNECTED but does not have UP in the SMF handling UE join, how would such UE be associated with MBS Session in RAN?
    Q2: If all joined UEs have UP activated, how would the “inactive” MBS Session in RAN be activated again?

## Slide 4: Issues
UE join is rejected if the AF has not provided service requirements (including QoS information), there are implications on AF/AS
Foreseen complexity to support ETSUN scenarios in future release
  I-SMF may need to be involved in HO procedures (Xn/N2, with/without I-SMF with change, with I-SMF removal/addition), and
  SMF may be required to discover MB-SMF in another SMF service area,
  Some investigation was done in S2-2101015 (SA2#143E)

## Slide 5: Way forward proposal
To achieve single/coherent solution agree on following working assumptions:
  MB-SMF is the initiator of NG-RAN specific MB-SM information sent via AMF over N2 to NG-RANNote1
  Mobility Management in AMF is part of for MBS traffic delivery control Note2
  Details of AMF involvement are FFS
  Solution shall be:
    Addressing all CM-states
    Scalable, i.e. addressing activation/de-activation for a very large number of UEs;
Note 1: text is aligned with TS 23.501 §6.2.2 (SMF):
Initiator of AN specific SM information sent via AMF over N2 to AN.
Note 2: “MBS traffic delivery control” refers to where to deliver the MBS traffic based on UE’s whereabout, e.g. S2-2102942 request AMF to translate a UE list into group paging area.

## Slide 6
Thank You!